## Slide 1
Integrated Sensing and Communication Phase 2
Xiaomi
Motivations, Use cases and Proposed Objectives
XIAO MI
COPY RIGHT 2024, ALL RIGHTS RESERVED
3GPP TSG-SA WG1 Meeting #106 S1- 241064
Jeju, Korea, 27 - 31 May 2024
(revision of S1- 240044)

## Slide 2
Dynamic Sensing service quality (KPIs)
Scenarios
  Vehicle drive under bad weather conditions (e.g., snow, fog, rain, sand storms, dense smoke) equipped sensors, like lidar, camera, ultrasonic radar and 3GPP sensing.
  3GPP sensing has much better performance than lidar, camera, ultrasonic radar, but cannot reach service quality requirement for normal weather condition.
  3GPP sensing results with decreased sensing service quality is still valuable since autonomous driving have five levels, from L1 to L5
  3GPP sensing provide required service quality requirement after car return to normal weather conditions
Potential requirements
  3GPP sensing should be able to handle multiple performance requirements in a single sensing service request.
  (Even best effort is acceptable in some cases)
i
A stopped vehicle is detected
XIAO MI
COPY RIGHT 2024, ALL RIGHTS RESERVED

## Slide 3
Static Sensing Result Exposure/Distribution
XIAO MI
COPY RIGHT 2024, ALL RIGHTS RESERVED
Scenario
  It is assumed that sensing data of a specific sensing area are static, i.e. real-time/on-demand detection is not necessary, thus can be stored for future use. One example is the 3D map of an area.
Service flows
  At Time A, Alice triggers sensing service request related to Area X from her UE. The network triggers sensing detection based on the request.
  The detected sensing data is then transmitted to the sensing data processor for processing and the sensing result is provided to Alice’s UE and also stored in the network.
  At Time B, Bob triggers sensing service request related to Area X from his UE. The network checks from the stored sensing information matching the service request and finds available sensing data, and the sensing result is provided to Bob’s UE.
  Sensing Result as a Service enables the 3GPP operators to provide sensing result based on the stored sensing result matching to the service requirement.
Sensing database
Sensing area
Sensing data
…
Sensing KPIs
Core network checks the sensing database.
i
New sensing request

## Slide 4
XIAO MI
COPY RIGHT 2024, ALL RIGHTS RESERVED
Scenarios
  In vehicular scenarios, multiple vehicles may request the core network to sense the same target, which leads to the core network generating a large number of identical sensing results. Moreover, the sensing result can be the point cloud with a large data size. To improve distribution efficiency, the core network distribute large amounts of identical sensing results to multiple vehicles simultaneously.
Sensing result concurrent exposure/distribute to multiple consumers
  The core network should be able to distribute large amounts of identical sensing results to multiple sensing service consumers simultaneously.
Sensing service consumers
!
Sensing request
Sensing request
Sensing request
Sensing results concurrent exposure/distribute to multiple consumers

## Slide 5
Proposed Objectives
Study new use cases for enhancements to 5G wireless sensing, including
    Providing dynamic sensing service quality (KPIs) to service consumers
    Enhancements to sensing results exposure/distribution, e.g. static sensing result exposure/distribution, sensing result concurrent exposure/distribution to multiple consumers, etc.
Identify potential service requirements, KPIs and performance requirements.
Aspects related to security, privacy, regulatory requirements and charging.
Gap analysis between the identified potential requirements and existing 5GS requirements or functionalities.
Notes: Uu口的方案需要再思考一下。

## Slide 6
Thanks