## Slide 1: Supplemental Network Extension (SupNet)
Qualcomm
3GPP TSG- SA1 Meeting # 106 S1-241076
Jeju, Korea, May 27-31, 2024 (revision of S1-240142)

## Slide 2: Motivations & Background
Reducing MNO CAPEX/OPEX for RAN deployment is a constant and increasing target, especially challenging for densified/small cells, indoor, remote areas, ad-hoc hotspots. There is also a growing need for more flexible deployment scenarios (multi-tenant/MNO access), e.g. for verticals industries or enterprises.
A “SupNet Provider” (e.g., real-estate owner, 3rd party RAN provider, other NW operator) can deploy RAN nodes providing supplemental coverage/capacity to other MNOs (PLMN or NPN)
  The entity deploying the NW can be incentivized for contributing to the MNO’s extended coverage & connectivity and validate NW operation, e.g. based on proof of coverage/use
  Spectrum can be licensed/unlicensed, owned by the served MNO or the SupNet Provider
Some example target scenarios are:
  Indoor venues, e.g. factories, shopping malls, commercial/enterprise buildings
  Remote/rural areas with no/limited MNOs coverage
  Ad-hoc events / venues (e.g., music festival, sport venues)

## Slide 3: High-level concept
SupNet provider manages:
  Coordination with MNOs, settlement of coverage extension services/data-offloading requirements
  Operation & configuration functions related to the SupNet RAN nodes
  Handling of Proof-of-Coverage (e.g., from dedicated UEs) for verification/validation of RAN operation
  (optionally, depending on biz model) CN functions e.g., for inter-connecting RAN to MNO core network, or to provide local data offloading
Assisting UE (A-UE) is a UE with new functionality performing Proof-of-Coverage & Reporting
  It can be normal UE or a dedicated UE for Proof-of-Coverage purpose, authorized and configured by SupNet provider
  A-UE performs Proof-of-Coverage operation and reports to SupNet provider (who manages records of Proof-of-Coverage)
MNO requests coverage/capacity extension services from SupNet provider
  MNO provides configuration information/requirement to meet their coverage demand in particular location(s) and/or time
  MNO collects consolidated records of Proof-of-coverage/Proof-of-usage from SupNet provider
SupNet RAN
UE
SupNet provider
Data Network
MNO
Core Network
Data connectivity
Control/OAM
[Legend]
A-UE
Proof of Coverage
Local
offloading
“SupNet provider”:
3rd party/MNO managing the “SupNet RAN”
“SupNet RAN”: owned by SupNet provider or other entity/partner

## Slide 4: Service Scenarios & Flow
Premises owner or 3rd party provisions / installs RAN nodes, in specific locations or areas, and partners with a SupNet provider
Based on served MNO’s demand, SupNet provider configures RAN nodes (for MNO UEs’ access, connection with MNO’s CN, etc.)
SupNet provider configures and collects proof of coverage reports and validates SupNet node operation (service toward MNO)
Served MNO rewards SupNet provider (who can reward SupNet node owner) for the coverage extension services
SupNet node
SupNet Provider
SupNet Provider
Indoor UEs
Indoor UEs
outdoor UEs
outdoor UEs
<Shopping mall>
<Dense urban area>
Indoor UEs
MNO#1
MNO#2
MNO#3
Node owner
Premise owner
Smart city network provider
Enterprise owner
Building owner
Indoor/outdoor UEs
<Rural / Remote area>
Biz relations

## Slide 5: Potential SA1 Gaps
Previous concepts and requirements, including similar scenarios/aspects:
  Neutral Host
  SON
  RAN sharing
  NPN
  PALS
  Residential 5G
  PIN
Gaps: the above do not cover required SupNet functionalities, including
  Configuration, collection and reporting of Proof of coverage by authorized UEs
  Exposure and configuration between parties to provide coverage/capacity service
  Security aspects, e.g. for authorization of SupNet nodes/components and confidentiality of user data.

## Slide 6: Proposal for SA1 – SID Objectives
Study use cases and requirements to support different scenarios where a “SupNet provider”, which could be a network operator or 3rd party, manages supplemental network resources / RAN nodes (deployed by the SupNet provider or an independent party) used to provide extended coverage and/or capacity services to other MNO(s) (PLMN or NPN), e.g. in indoor, hotspot or rural areas.
Aspects and functionalities to investigate should include:
Coordination and exposure between the SupNet provider and the served MNO(s), for the control and settings of the coverage/capacity extension service and policies;
Support of proof of coverage and/or usage for network operation verification, including configuration of participating UEs / entities, reporting to the SUPNet provider and exposure to the MNO(s);
Security and confidentiality aspects, e.g. authorization of network nodes and user data confidentiality;
Other aspects, e.g. charging and regulatory requirements.

## Slide 7: ANNEX Extra slides

## Slide 8: Business drivers (examples)
MNO
NW/UE vendor
SupNet
Provider
Network Participant
(SupNet owner, Users)
Gain: Reduced cost for Coverage/Capacity extension
Gain: Coverage/capacity Service fee
Gain: Selling SupNet node, PoC devices
Gain: Reward for participating in
- Data offloading
- Proof of Coverage / Usage

## Slide 9: Clarifications (1/2)
Setup/Config of Supnet (how/by who)?
  Anyone who buys SupNet node becomes SupNet owner
  SupNet node owner selects SupNet provider and enrolls.
  SupNet provider manages the enrolled SupNet node, and provides incentives for contributing coverage/capacity extension
  SupNet node owner can change SupNet provider at will
UE authorization (how/by who)?
  A-UE:
    A-UE needs to enroll SupNet provider to participate Proof-of-coverage program.
    A-UE is authorized by SupNet provider
    SupNet provider incentivizes A-UE according to its Proof-of-coverage record
  UE accessing to SupNet
    It is a normal UE (if SupNet node serves MNO frequency band) or roaming UE (if SupNet node serves CBRS, or if SupNet node serves PLMN with roaming agreement). No specific handling of authorization is needed.
Clarify what CN functions can be managed by SupNet
  It depends on deployment scenarios.
    thin CN (e.g., only providing gateway to access to MNO’s CN), or
    min CN feature e.g., only providing local data offloading (Session management to establish PDU session for local DN), or basic access and mobility management (if needed)
    full CN if SupNet provider is private network provider.

## Slide 10: Clarifications (2/2)
Relationship with PLMN MNO?
  normal inbound/outbound roaming?
    Same as current roaming architecture and principles.
  What is the MNO role?
    To request coverage/capacity extension to SupNet provider, and provides requirements for coverage/capacity, and radio configuration parameters.
  Clarify diff with RAN sharing or private network, or VMR.
    It is orthogonal. SupNet node can be VMR. Only difference will be whether/how to be connected to MNO’s Core Network.
Reporting of PoC (to who)?
- PoC is managed by SupNet provider
- A-UE sends the report of PoC to SupNet provider.
- user awareness?
- User of A-UE has to be aware as it requires to enroll PoC program of SupNet provider
Difference with RAN Sharing, or Neutral Host?
  See slide 5