## Slide 1
S1-241099, 3GPP TSG #106, 27-31 May 2024, Jeju, South Korea
Discussion on Multi-network Interoperability Enhancement
China Unicom
3GPP 2024

## Slide 2
The early deployments are adopting NSA as a means of fast launching 5G and may evolve towards SA. Based on operators’ different network development progress and strategies, 5G SA networks and NSA networks will coexist and interact in same PLMN or different PLMNs for years.
However, the existing requirements do not support the interoperability of NSA/EPC users accessing 5G SA networks. It is not always guaranteed for 5G subscribers to obtain consistent provision of 5G services in heterogeneous environment with coexisting SA and NSA networks.
Standard capabilities to enable 5G services offering to all 5G (SA and NSA) subscribers are essential to guarantee the user service experience and to fulfill expectations of 5G technology.
To reduce CAPEX/OPEX, carbon emissions/network energy use, and network complexity for operators by only retaining SA networks instead of keeping both NSA and SA networks.
To better rollout 5G roaming for operators.
To offer users an improved connectivity experience.
Background & Motivation
3GPP 2024

## Slide 3: Example Use Case 1
HPLMN supports EPC/NSA networks. VPLMN supports 5GC/SA networks
A 5G services subscriber of the HPLMN roams to the VPLMN
There is 5G roaming agreement between the VPLMN and the HPLMN
UE of the 5G roamer is a SA access capable terminal
3GPP 2024
Benefits
EPC/NSA operators: assure their 5G users of the similar 5G service and user experience as in the home EPC/NSA network when roaming without upgrading their EPC/NSA network
  SA operators:
    save investment and operating costs with CAPEX and OPEX, and reduce complexity of networks by maintaining only SA networks instead of keeping both SA and NSA networks;
    provide an opportunity to 5G SA only operators better rollout 5G roaming with NSA/EPC operators
Roaming
Source: GSMA NG.113 5GS Roaming Guidelines
  The roaming remains undefined where VPLMN has 5GC only and HPLMN has EPC only
  The other way round is EPC roaming
Possible 5GC/EPC Roaming Scenarios

## Slide 4: Example Use Case 2
A PLMN deploys separate 5GC and EPC (e.g., 5GC in major city, EPC in the rest of the PLMN, respectively)
A 5G subscriber’s subscription profile is provisioned in HSS in EPC/NSA area
The subscriber is travelling from the EPC/NSA area to the SA area
UE of the 5G subscriber is a SA access capable terminal
Service continuity is considered
3GPP 2024
Non-Roaming
5G SA
5G NSA
others
others
MME
SGW
AMF
UPF
gNB
eNB
gNB
NSA area core network
SA area core network
Fig. NSA and SA are deployed in different areas within same PLMN
UDM
HSS
5G subscriber
5G subscriber
PLMN
Benefits
  Interoperability between EPC and 5GC is suitable for operators introducing 5G subscription without impacting or migrating those subscription data already provisioned on a legacy HSS.
  To reduce excessive investment and save cost by avoiding implement 5GC network elements all at once towards 5G SA migration.

## Slide 5: Gap Analysis & Proposal
Existing reqs and specs
  TS 22.261 clause 5.1 specified requirements of supporting interworking between 5G systems and interoperability with legacy 3GPP systems
  Stage-2/3 supports non-roaming and roaming interworking between 5GS and EPC/E-UTRAN.
Gaps
  The dedicated entities (i.e., HSS + UDM, SMF + PGW-C, and UPF + PGW-U) are required for the non-roaming and roaming interworking between 5GS and EPC/E-UTRAN defined in stage 2/3. However, there are no such dedicated entities in EPC/NSA region, only HSS and PGW instead.
  The roaming remains undefined where VPLMN has 5GC only and HPLMN has EPC only
  Requirements, service offering capability and mechanisms between 5GC and EPC are remain undefined
3GPP 2024
×
EPC/NSA home region
5G SA Only
visited region
Investigate use case which enable a 5GC/SA network to provide 5G services in the following scenarios:
  when a subscriber of HPLMN supporting only EPC/NSA networks roams to a VPLMN supporting only 5GC/SA networks
  when a subscriber travels within the same PLMN, from an EPC/NSA only area to a 5GC/SA only area
Derive potential requirements from those use cases regarding the following aspects:
  Network access control
  Subscription data retrieval
  Service continuity
  information of subscriber’s type (i.e. subscriber of a 5G SA network or a 5G NSA network)
  Others aspects, if any
Gap analysis between the existing 3GPP requirements and functionalities and identified potential requirements
Proposal

## Slide 6: Thank you
3GPP 2024