## Slide 1: Huawei input to SA1 Call (17th April 2025) on AI Agents in 6G network
HUAWEI
3GPP TSG-SA WG1 Meeting #110 S1-252036
19-23 May 2025, Fukuoka, Japan

## Slide 2
Background
SA1 endorsed AI Agent definition (below) as 6G Study rapporteurs’ proposal in S1-250771[1], which recapitulates all related preceding discussions up to and during SA1#109. The definition is captured in TR22.870v020.
References: [1] S1-250771 AI agent discussion
Al Agent: an automated intelligent entity capable of e.g. interacting with its environment, acquiring contextual information, reasoning, self-learning, decision-making, executing tasks (autonomously or in collaboration with other Al Agents) to achieve a specific goal.
Editor’s Note: This definition could be updated as the study goes on to align with the potential new understand of AI agent.
Quite a few SA1#109 use case contributions (below, incl. resubmission from SA1#108) propose the interest/needs of supporting AI Agents in the 6G network. Some of those contributions were agreed, the remaining ones continue to be discussed (list below).
Prior to SA1#110, an SA1 call has been planned for WG1 to better understand “AI Agents in 6G network”, incl. discussing the following 4 questions identified by the 6G Study rapporteurs. Huawei provides input following the guidance from the SA1 leadership.
Important to note: AI Agent in 6G NW relates to “AI4Net”, and AI4Net in general is much more than just “network optimization”.
6G network need to integrate AI Agent to provide 6G services, because:
Challenges:
a plethora of wide-ranging, novel usage scenarios of the markets need diversified 6G services/capabilities,
the exact demands of them on the 6G services/capabilities (incl. their combination) are difficult to foresee in its entirely (hard to anticipate),
impractical to exhaust all possibilities via traditional pre-defined rule-/template-based approaches;
Necessity:
above situations need to be handled intelligently/flexibly/optimally in real-time by 6G CN at certain autonomy (e.g. dynamic generation and management of services to satisfy users/Apps), actions ensued from reasoning can’t be pre-defined as well as the execution of them,
whilst systemically ensuring network resource/energy efficiency considering NW supporting multiple UEs consuming such dynamic/varied combination of 6G services.

## Slide 3
Discussion (1/2)
Q1a. What is meant by "intent“? Q1b. How does it relate to "AI Agent“? and Q1c. What's the difference compare to SA5 definition?
  Reference to SA5 work:
  Rel-18 TR 28.912 “Study on enhanced intent-driven management services for mobile networks” and TS 28.312 “Intent driven Management Service for Mobile Network phase 2” define features of Intent Management Network (IMN) which allows subscribers to express their network-oriented intents (typically human-readable) about, e.g., delivery of a specific communication service or desired properties of the network.
  TS 28.312 has the following definition:
  “intent: expectations including requirements, goals and constraints given to a 3GPP system, without specifying how to achieve them.”
  But as clause 4.1.2 states, regardless of intent’s user types, the objective of SA5 intent is about the “managed for communication service, or for management of network, or for management of network elements”.
  TS 28.312 clause 4.1.3 (“intent expectations for different types of management needs”) clarifies intent expectation is for “delivering network and service related object (e.g. network, service, slice)” and for “network and service related object (e.g. network, service, slice) performance”. Clause 4.5.1 (“intent expectation”) further clarifies the following:
  “The object may be a 3GPP managed object like a network slice, subnetwork (e.g. radio network) or other objects like a service.”
A1a: In the context of SA1 6G SI, we define Intent: the 3GPP service request from subscriber or third-party application, expressed to the 3GPP network emphasizing the objectives (instead of “how”). It may include requirements (e.g. expressed objectives that would depend on 3GPP services), goals, and information (e.g. constraints) related to the 3GPP service(s).
NOTE: Constraints could be any conditions related to the expressed objectives. E.g. In the context of autonomous driving, it may be the preference for the shortest route, the shortest driving time, or other personalized preferences.
A1b: As Intent is a new form of 3GPP service request from subscriber or third-party application, its objectives must be received in 6G CN, where an AI Agent understands the objectives (situational context-awareness) and translates them into the needed constituent 3GPP services and capabilities. In this process, AI Agents in 6G network reason and self-reflect to decide and plan the most optimal actions to take in order to provide the 6G services.
A1c: Current SA5 work on “intent” focuses on OAM, e.g. intent-driven MnS, management of communication service/network/network elements (incl. sub-network). Differently, “Intent” in the context of SA1 6G discussion is 3GPP service request sent by subscribers or third-party applications of toB users (customers of the 3GPP operators) to consume the 3GPP services in a variety of dynamic and rich context, e.g., for autonomous driving, safe navigation, UAVs, COBOTs, etc.
A2:
Q2. What service AI Agent could provide within 3GPP network? ( -> “What services could AI Agents within 3GPP network provide?”)
Understand and parse Intent (able to interact with subscribers/3rd party apps from toB customers), knowing the situational context of Intent related to the required 6G services; understand the objective and translates it into the 3GPP services and capability requirements.
To optimally support objectives expressed in the Intent, provide multiple 3GPP services and capabilities synergistically orchestrated (e.g., using ISAC, AI, URLLC) considering their interdependency, whilst ensuring (resource, energy, etc.) efficiency of the overall 6G network/system in dynamic environment.
AI Agents in 6G CN may check any previously retained context, using the past findings (e.g. data looked up and memorized, knowledge built from previous interaction with subscribers, or decisions made in similar situations).
6G core network autonomously controls/manages the execution order of various constituent 3GPP services/capabilities concurrently, and manages the coordination of related resource optimization and dynamic adjustment of constituent capabilities/functions in runtime, to ensure the intended QoS of the services are assured.
AI Agents in 6G CN may collaborate with AI Agents in UE.
AI Agents in 6G CN can optimize network traffic to improve network efficiency, QoE, and sustainability.
TR22.870 Clause 6.5 and 6.10 already capture context related to: intent/intention-based request from subscriber to 6G network, where intent is acted upon by AI Agent or ”Intelligent Communication Assistant” in the 6G network.

## Slide 4
Q3. What's the impact on network if AI agent is introduced?
A3:
AI Agents inherently have the unique capabilities (e.g. interacting with environment, acquiring contextual information, reasoning, self-learning, decision-making, executing/solving non-standard and open tasks autonomously or in collaboration with other Al Agents to achieve a specific goal) essential for 6G core network to be able to intelligently and flexibly provide any optimal combination of 3GPP services/capabilities on-demand and in run-time (Quality Assurance) as needed by the subscriber/3rd party app whilst ensuring the resource efficiency from the network perspective.
Current 3GPP system design is rule-based, the basic principle of AI Agent is knowledge-based (generates output according to the knowledge pre-trained and/or retrieved from the knowledge base) which provides flexibility and (resource/energy) efficiency in various dynamic service needs not fully anticipated beforehand.
Currently service request (from UE or 3rd party app) for 3GPP services follows structured and pre-defined input upon which it generates a pre-defined output (i.e., service response). Thanks to the capabilities of AI Agent in 6G CN, apart from what’s explained in A1b (Intent and AI Agent), it is made much easier for operator’s various customers (toC/toB) to request (via easy-to-use Intent-based service request, possibly unstructured) and consume the plethora of 6G services/capabilities deployed in 6G network.
Better support of new types of intelligent devices, e.g. AI Phones and AI-embodied physical devices.
Better support of new types of 3rd party apps or services, which are based on e.g. AI Agent and tools (Agent to Tool such as MCP).
Better provide/expand operators’ services (e.g. currently via IMS) adding beyond connectivity 6G services/capabilities.
Integrating AI Agents in 6G core network comes hand in hand with continuing to ensure mobile telecom services/networks’ reliability and robustness. AI Agents need to be carefully designed and constrained when solving tasks not yet anticipated by designers. Therefore, new functions and systems may be needed to verify reasoning and actions by AI Agents, to ensure quality and operators/customers are confident to trust of their decisions and actions.
The existing 3GPP networks rely on pre-defined and rule-based functions to provide communication service with QoS, which in 6G era may exhibit rigidity and constrained adaptability to accommodate users/3rd party apps’ dynamic and often unpredictable need for combination of heterogeneous (incl. beyond-connectivity) 6G services/capabilities as the 6G services/features burgeon with immense potential and diversity. This may render the current architecture insufficient (even ill-equipped). AI Agents’ capabilities integrated in 6G network dramatically increases the operators’ ability to monetize the investment while enabling customers to consume 6G services more easily/intuitively, further contributing to social and economical goals.
Discussion (2/2)
Q4. Which new type of service /use case can be performed by an AI Agent compared with traditional AI model/algorithm e.g. in the NWDAF.
A4:
Current NWDAF is a good starting point to utilize AI in 5G CN, but its service is limited to perform NW/UE analytics / predictions using traditional AI model. Using just AI models/algorithms, NWDAF are designed / trained to perform only pre-defined tasks, and cannot adapt to new conditions and requirements, nor make decisions and take actions autonomously to reach intended goals/objectives.
NWDAF does not have the capabilities mentioned in e.g. A3a, therefore it can’t provide services that AI Agent can, e.g. assemble and customize the 3GPP services based on reasoning result, execute tasks autonomously and perform closed-loop control for the execution, e.g. optimizing and adjusting the 3GPP services according to the real-time feedback of network.
NWDAF has hardly any insight in why its output is needed or how it’s used by e.g. NFs/Apps. NWDAF is not involved in further interaction with the 3GPP network control.
NWDAF is rule-based, supporting standard pre-defined logical functions, such as collecting data from standard data resources defined by 3GPP (e.g. NFs, AFs, OAM), providing data analysis, model training and model inference services based on standardized events (e.g. slice load analysis, service experience analysis, etc.).
AI Agents in 6G CN will be involved in providing 6G services to satisfy a plethora of wide-ranging usage scenarios whose needs for (varied combo of) 6G services are impractical to exhaust via traditional pre-defined rule-/template-based approaches. It is imperative to incorporate in 6G network AI Agents capable of handling such situations in real-time at certain autonomy (e.g. dynamic generation/management of services, NW control) whilst ensuring network resource/energy efficiency.

## Slide 5
THANKS