## Slide 1
Discussion Paper on AI Views
Qualcomm Technologies
S1-252147, 3GPP TSG #110, May 19 - 23 May 2025, Fukuoka, Japan

## Slide 2: AI Aspects in 6G (1)
As mentioned in TR 22.870 Clause 6.0, SA1 scope of AI address in TR includes the following:
  AI for 6G System refers to the use of AI capabilities to support the network and devices in providing 3GPP services.
  6G System for AI focuses on how the system supports and enables AI applications by leveraging 6G system functionalities to provide different services.
Also, current “AI Service” definition is the following:
  AI service: a 6G service (e.g., AI model inference) to support AI-related activities, which is provided by 6G core network to the 6G user, considering the required quality of the service (e.g., inference accuracy, latency).
    NOTE 1: The above term does not imply any architectural assumption, e.g. whether 6G CN/RAN is a new or evolved CN/RAN (compared to 5G).
    Editor’s Note: The definition of AI service is FFS.
Observation 1a:Current definition of AI service is limited to “6G system for AI” with the following features:
  Service provided to the user (not including 3rd party application)
  Service provided by the core network (excluding cases where the entire 6G system (excluding UE) are involved in providing the service)
  The phrase “AI-related activities” is unclear

## Slide 3: AI Aspects in 6G (2)
Proposal 1a: Definition of 6G System for AI Service
  6G System for AI - AI service: a service where the 6G system provides AI capabilities to a subscriber or 3rd party application. The 6G system may also expose AI capabilities provided by a 3rd party service provider to a subscriber.
  Examples of this type of service includes:
    providing AI model training and inference to 3rd party AI applications such as Generative AI and AI agent applications.
    providing AI-based immersive services or AI-based communication assistant service to subscribers.
Observation 1b:
  In AI for 6G systems scenarios, AI capabilities can be used within the 6G systems to provide 6G services (e.g. communication, sensing, compute and AI services).
Proposal 1b: Definition of AI for 6G System
  AI for 6G System: is the use of AI capabilities (e.g. AI model inference, Generative AI, AI Agents) within the 6G systems to facilitate aspects such as:
    service orchestration and delivery,
    network management and orchestration,
    energy savings in the UE and/or the network.
Observation 2:
  It is important to note that 6G System for AI (i.e., AI services) or AI for 6G System can be implemented using different types of AI capabilities e.g. AI model inference, AI assistant, AI agent capabilities, Gen-AI capabilities, etc.
  Note: Some use cases may include both AI service and AI for 6G System.

## Slide 4: AI Agents (1)
SA1 agreed to define AI agents as:
  Al Agent: an automated intelligent entity capable of e.g. interacting with its environment, acquiring contextual information, reasoning, self-learning, decision-making, executing tasks (autonomously or in collaboration with other Al Agents) to achieve a specific goal.
  Editor’s Note: This definition could be updated as the study goes on to align with the potential new understand of AI agent.
Observation 3:There is currently no connection between AI services/AI for 6G System and AI agents.
Proposal 3:
      Al Agent: an automated intelligent entity capable of e.g. interacting with its environment, acquiring contextual information, reasoning, self-learning, decision-making, executing tasks (autonomously or in collaboration with other Al Agents) to achieve a specific goal.
      Note:
        - AI service may be provided to AI applications (e.g. AI agent applications)
        - AI for 6G System aspects may be implemented using AI agents.
Editor’s Note: This definition could be updated as the study goes on to align with the potential new understand of AI agent.

## Slide 5: AI Agents (2)
Based on some of the AI agent related discussions/use cases presented in SA1 meeting #109 and the offline meeting, some of the functionalities of an AI agent include:
  Using intent-based approach to express goals, requirements and constraints
  Learning, reasoning and Decision-making leveraging AI capabilities
  Execution of tasks/functions/procedures using AI capabilities.
Observation 4: Current SA1 definition of AI agents does not include “intent” and no definition of intent has been agreed.
Proposal 4: SA1 should define connection between AI agents and intent as following:
    Intent: “Intent are expectations including requirements, goals and constraints given to a 3GPP system, without specifying how to achieve them” derived from TS 28.312. Intent could also be expressed through multimodal inputs such as voice, text, and video. AI agents may express requests through intent and/or have the capability to interpret intent.

## Slide 6: AI Agents (3)
In #SA1 109, some companies presented use cases leveraging AI agents to:
  provide AI services to subscribers and applications e.g. party planning services and personal communication assistant
  provide AI for 6G System within the 6G systems e.g. QoS Assurance for special events and network orchestration and management.
  provide AI services and AI for 6G System e.g. AI agents-based vehicular navigation application requesting 6G services from AI agents in the network.
Many of the use cases discuss the benefits of using AI agents such as:
  providing flexible service delivery in dynamically changing applications and environments
  enabling efficient execution of complex and multi-step network operations.
While many benefits come with using AI agents, it is important to keep in mind that AI agents could also introduce more ambiguity into the 6G system through:
  intent-based service request
  replacing existing rule-based functions, interfaces and procedures with AI-based ones.

## Slide 7: AI Agents (4)
Observation 5: While some use cases might benefit from AI agent implementation, others might be severely impacted by AI imperfections/hallucinations, specifically, some use cases that involve replacing interfaces, functionalities or procedures in the 6G system by AI agents.
Proposal 5:
  SA1 needs to carefully consider use cases and requirements that have the potential to replace interfaces, functionalities or procedures in the 6G systems by AI agents (i.e., AI for 6G system aspects).
  SA1 should capture AI agents as one implementation of AI capabilities in the 6G systems for AI or AI in 6G systems.
  SA1 should capture functional requirements and avoid specifying solutions. Architectural and design aspects should be left to downstream groups.

## Slide 8: Proposed Revision to Requirements in TR 22.840
Observation 6:
  Many of the approved AI-agent related PRs in SA1 #109 meeting are drafted specifically for AI agents in a user’s device or 3rd party application.
  Given that an AI agent application is one implementation of AI applications, it is desirable to avoid focusing requirements on one implementation, but we should generalize the PRs to AI applications and highlight AI agent applications as an example.
Proposal 6:
  We proposed to use the phrase “AI applications (e.g., AI agent applications)” instead of “AI agent applications” in AI agent application related PRs in Clause 6.
See slide 7, 8 and 9 for details.

## Slide 9: Proposed Revised Requirements (1)
6.5.6 Potential new requirements needed to support the use case
[PR 6.5.6-1] Based on operator policy, the 6G network shall be able to support secure means to expose its services to the authorised third-party AI application (e.g. AI agent application) by intent if needed.
Editor’s Note: the meaning of “intent” is FFS
6.6.6 Potential New Requirements needed to support the use case
[PR 6.6.6-1] Based on regulatory requirements, operators’ policy and user consent, 6G network shall support trusted network access for 3rd party AI applications (e.g., AI agent applications) and support a mechanism to expose 3rd party AI agent application’s attributes (e.g., related users, sensing capabilities, AI capabilities) to other 3rd party AI agents applications.
[PR 6.6.6-2] Based on regulatory requirements, user consent, operators’ policy and agreement with authorized 3rd party, the 6G network shall be able to support security identification for 3rd party AI applications (e.g., AI agent applications) provided by authorized 3rd party associated with a user (e.g., AI agent applications belonging to a customer).

## Slide 10: Proposed Revised Requirements (2)
6.7.3 Potential New Requirements
[PR 6.7.3-1] Based on user consent and operator policy, the 6G system shall provide a suitable means for an AI application (e.g. AI agent application) on a UE to invoke some 3GPP services.
6.8.6 Potential New Requirements needed to support the use case
[PR 6.8.6-1] Based on user consent and operator policy, Tthe 6G system shall support hosting of large amounts of AI applications (e.g. AI agent applications) managed and controlled by the 6G core network and/or multiple AI applications (e.g. AI Agent applications) on a UE.
Editor’s Note: FFS whether to split the above requirement into two requirements.
Editor’s Note: terminology for different types of AI agents is FFS.
NOTE: The term 6G core network does not imply any architectural assumption, e.g. whether 6G core network is a new or evolved core network (compared to 5G).
[PR 6.8.6-2] Based on user consent and operator policy, Tthe 6G system shall support secure interoperability between AI applications (e.g. AI Agent applications) and between AI Agents and to achieve a collaborative task.
Editor’s Note: Additional requirements for collaboration between AI Agents FFS.

## Slide 11: Proposed Revised Requirements (3)
6.10.6 Potential New Requirements needed to support the use case
[PR 6.10.6-1] Subject to operator policy and user’s consent, 6G network (e.g. in conjunction to IMS) shall be able to provide intelligent communication assistant service to users.
[PR 6.10.6-2] The 6G network shall support charging information collection for the intelligent communication assistant service.
NOTE: Intelligent Communication Assistant: The A virtual intelligent communication assistant locateds in operator network and interactings with the users through voice, video, text, gestures or other modalities. The assistant can be customized for each particular user by accessing user data stored in the network, with user’s consent. It can provide various communication services and support individual users based on user’s intention and requirement. One subscriber can have one or more Intelligent Communication Assistants.
6.12.6 Potential New Requirements needed to support the use case
[PR 6.12.6-1] Subject to operator’s policy, the 6G network shall be able to expose information from the network to authorized 3rd party AI applications (e.g. AI agent applications) by means suitable for prompt augmentation.
Editor’s Note: definition of prompt augmentation is FFS

## Slide 12: Proposed Revised Requirements (4)
Observation 7: The AI service in PR 6.9.6-1 is provided to the user or 3rd party application not the UE. Also, use consent is required.
Proposal 7:
[PR 6.9.6-1] Subject to operator’s policy and user consent, the 6G network shall be able to provide AI service (e.g., AI model inference) to a user or 3rd party application on the UE.

## Slide 13: THANK YOU