## Slide 1
Discussion on data service
© 3GPP 2024
Source: Huawei, China Telecom, China Mobile
Agenda item: 8.1.2
Document for: Discussion

## Slide 2
Motivation of new services and data
        Services beyond communication : 6G network will provide both communication service and services beyond communication (e.g., AI service, sensing service, etc.). Various types of data will be originated inside 3GPP system, such as sensing data, AI data, network operation data, NF/UE context data, and positioning data, etc.
        For example, sensing data from large numbers of Base Stations in a wide area can be consumed by massive UEs/vehicles within the same service area, e.g. for XR rendering or automatic driving. Moreover, new services (e.g. AI, sensing) bring new data traffic characteristics, e.g. for joint training/inference, sensing data fusion.
Diversified data providers and consumers: Various types of data are exchanged between/among different services, e.g., AI service can use sensing data collected from another sensing service. Moreover, various types data are not only used by UEs and 3rd parties, but also by 6G internal entities (e.g. NFs, Base Stations, etc.).
        For example, sensing data originated from Base Stations and UEs can be utilized/consumed by CN NFs in case of sensing-assisted communications, and the support of vertical applications.

## Slide 3
Examples of use case#1
Data originated by 6G system can be utilized by other services provided by 6G system or OTT Application.
Multiple data providers:
  For example, different data involved in sensing service, AI service, positioning service, context management service can be used jointly for a single application such as XR rendering.
Multiple data consumers:
  For example, sensing data collected by 6G system can be consumed independently by AI services or communication services or third parties.
Data consumers
Data providers
AI data
Positioning data
gNB Sensing data
AI service
Sensing service
OTT service
Data service
UE Sensing data

## Slide 4
Examples of use case#2
Data consumers
Data providers
Automatic driving
Traffic monitoring
Intrusion detection
Weather monitoring
gNB based sensing
UE based sensing
In order to a high-accuracy and wide-area sensing capability, different sensing data collected by 6G system can be utilized by different third parties.
Multiple data providers:
  For example, different sensing data collected from Base Stations and UEs can be aggregated and jointly processed for automatic driving application.
Multiple data consumers:
  For example, sensing data collected by 6G system can be consumed and independently processed for multiple applications or verticals such as traffic monitoring or intrusion detection.
3GPP Sensing data
Data service
3GPP Sensing data

## Slide 5
Data service
AI data
Sensing data
Positioning data
…
Data service: a service offering multiple types of data (e.g. AI related data, 3GPP sensing data, positioning data) originated or processed inside the 6G system, which is provided by the 6G system to the data consumer.
NOTE: the data consumer could be trusted third-party or UE or network function
Data exchange
Data exchange
Data exchange
data
Data consumers
Network operation data
NF context data
Data exchange
Data exchange
Data providers

## Slide 6
Gap analysis
SA1
SA5 focuses on data management from OAM domain [TS 28.552, TS 28.554].
SA5 focuses on statistics data for network performance, instead of data with high real-time requirements, such as autonomous driving.
5G MDAF [TS 28.533] utilizes non-real-time network management data, which is collected from the network (including e.g. network slicing and/or network function) and makes corresponding analytics based on the collected information.
In TS 22.261, the requirements are specified for efficient user plane, in which user plane paths can be selected or changed to improve the user experience or reduce the bandwidth pressure.
Compared to 5G system, 6G new types of data in wide range and huge amount are originated within 6G system, which is different from application traffic data delivered in the traditional data transmission pipelines.
SA2
5G NWDAF/DCCF/ADRF/MFAF mainly focus on data collection and management CN NFs [TS23.288].
SA2 doesn’t consider efficient data collection, storage, sharing, reuse, distribution, and delivery among various data sources and data consumers to fulfil the requirements introduced by communication services and new traffic patterns introduced by 6G new services beyond-communication.
The low efficiency of existing massive data transmission e.g. that between NWDAF/DCCF/ADRF/MFAF and NFs, should be addressed to meet the requirements of wide range of data coordination among multiple scenarios, e.g., for joint AI training/inference, sensing data processing and network digital twin.
SA5

## Slide 7
Thank you