## Slide 1: Motivations for Multi-hop multi-path relay for direct device connection
ZTE Corporation
3GPP TSG-SA WG1 eMeeting #98-e
E-meeting, 9th – 9th May 2022
S1-221106

## Slide 2
Motivations
For smart mine scenario, the industrial monitoring and remote control are typical use cases. In these scenarios, sensors, cameras, controllers deployed within a mining area may interact with each other. In addition, the operators usually control these devices directly on the site. So the direct device connection is expected to be applied to these scenarios.
Challenges: to meet the following requirements simultaneously:
  The operators with hand-held UE need to remotly control the hydraulic support, tunnel-boring machine, coal cutter and drag coneyer, which requires the real-time, and high reliability between UEs within mining area.
  The underground tunnel is long and narrow, which can be as long as one hundred kilometers. It reuiqres complex networking to support extended transmission range.
  Fault tolerance and robustness should be guaranteed when link failure or system fault happens.
  The communication is usually separated from the public network to ensure privacy and security.

## Slide 3
Multi-hop multi-path relay for direct device connection
Multi-hop multi-path relay for direct device connection: combine the multi-hop and multi-path relay forwarding to enable long distance direct communication and provide high reliability and energy efficiency for the direct device connection.
Benefits
Extended transmission range
  multi-hop relay forwarding
High reliability
  Multiple available relay paths and routing path switch
Enhanced privacy and security
  Local forwarding restricted to a set of UEs
Low deployment cost
Notes: Extended transmission range
  Direct traffic is delivered via the hybrid multi-hop Uu and PC5 forwarding
High reliability
  Network node is more reliable for relaying
  Multiple available paths and path switch
Low latency
  Data traffic not traverse 5GC and even CU
Enhanced privacy and security
  Local forwarding is restricted to a set of UEs within the private group
Low deployment cost

## Slide 4
State of Art
Among existing functionalities and requirements, some partially address the direct device connection related use cases for cyber-physical control applications, V2X services and mission critical services as following table. Only single hop UE-to-UE relay for direct device connection is mentioned to extend the direct communication range.
The multi-hop and multi-path relay for direct device connection has not yet been fully explored.
Existing Service requirements of UE-to-UE relay
TS No. | Title | UE-to-UE relay service requirements
22.278 | Service requirements for the Evolved Packet System (EPS) | ProSe Communication can also take place over a ProSe UE-to-UE Relay, a form of relay in which a Public Safety ProSe-enabled UE act as ProSe E-UTRA Communication relay between two other Public Safety ProSe-enabled UEs.
22.104 | Service requirements for cyber-physical control applications in vertical domains | 5G system shall be able to support direct device connection via an UE to UE relay with respective service performance requirements related to cooperative carrying between UEs out of transmission range of each other.
22.185 | Service requirements for V2X services | [R-5.2.1-001] The E-UTRA(N) shall be capable of transferring messages between two UEs supporting V2V/P application, directly or via an RSU, with a maximum latency of 100ms. NOTE: RSU is a term frequently used in existing ITS specifications, and the reason for introducing the term in the 3GPP specifications is to make the documents easier to read for the ITS industry. RSU is a logical entity that supports V2X application logic using the functionality provided by either a 3GPP network or an UE (referred to as UE-type RSU).
22.280 | Mission Critical Services Common requirements | [R-7.15.1-001] The Off-Network MCX Service shall provide a means by which the MCX User of a (source) UE can make a Private Communication to the MCX User of a (target) UE via a ProSe UE-to-UE Relay.[R-7.15.2-001] An MCX Service Administrator or authorized user shall be able to configure a ProSe-enabled UE, authorized to act as a ProSe UE-to-UE Relay, to relay any received MCX Service transmissions for one (or more) specified MCX Service Groups.

## Slide 5
Objectives
The objective of this study item is to study use cases and potential new service requirements for 5G system support of multi-hop multi-path relay for direct device connection：
  - Multi-hop scenarios related with direct device connection to support extensive range communication;
  - Multi-path scenarios related with direct device connection to support high reliability;
  - Configuration and management of multi-hop and multi-path assisted direct device communication service:
    Configuration and management of multi-hop and multi-path assisted direct device communication service.
    Multi-hop and multi-path configuration for QoS assurance and service continuity
  - Aspects related to security and charging.
  - Gap analysis between the identified requirements and existing 5GS requirements or functionalities.