## Slide 1: Roll-back with TAU/RAU Reject for PMIP
NTT DOCOMO

## Slide 2: Roll back with SGW Change: PMIP Problem
UE
New eNB
Old MME
NewMME
Old SGW
PGW
PCRF
HSS
New SGW
1. TAU Request
2. TAU Request
3. Context Request
4. Context Response
5. Context Ack
6. Create Session Request
9. PBU
10. PBA
11. Create Session Response
12. Update Location Request
15. Update Location Ack
13. Cancel Location Request
14. Cancel Location Response
7. GW CS Establish Request
8. GW CS Establish Response
16. Subscription based Reject
17. TAU Reject
18. Delete Session Request (SI = 1, OI = 0)
21. Delete Session Response
19. GW CS Terminate Request
20. GW CS Terminate Response
22. TAU Request
24. Delete Session Request (SI = 1, OI = 0)
27. Delete Session Response
28. Create Session Request
33. Create Session Response
26b. No GW Control Session for the UE. Issue#2
25. GW Control Session Termination Request
26. GW Control Termination Response
29. GW Control Session Establishment Request
30. GW Control Establishment Response
23. TAU Request
0a. GW Control Session
0b. IPCAN Session
8a. Primary GW Control Session
8b. Non-primary GW Control Session
Existing
SI = Scope Indication Flag;
OI = Operation Indication Flag
31 PBU
32. PBA
20b. PCRF clears primary GW CS. Issue#1
Another eNB
Start Timer
Cancels Timer

## Slide 3: CT4 proposal to PMIP problem in LS: C4-131514
When the serving SGW is changed by the target MME/SGSN, ….
….
  Target MME/SGSN: The target node should send Delete Session Request message ("Scope Indication =1", "Operation Indication=0") to new/target SGW. Additionally, the target shall release local resources corresponding to the UE session.
  Source MME/SGSN: If the UE comes back to the source node while the "context guard timer" is running, the source node shall send Delete Session Request ("Scope Indication =1", "Operation Indication=0") to release the UE session at the source/old SGW. Subsequently, the source node shall send Create Session Request message corresponding to the TAU/RAU with SGW change scenario to the same SGW or newly selected SGW. This will ensure successful re-establishment of the S5/S8 tunnel between the selected SGW and the PGW.
The above rollback behaviour is applicable for the GTP based S5/S8 interface.
For PMIP S5/S8 interface, for the behaviour specified in A, concern was raised that the PCRF may release the IP-CAN session if Gxc session is released by the target SGW (due to the target MME/SGSN sending Delete Session Request message in A.1) (Issue #1 Step 20a in previous slide). Assuming this is a valid concern, the target MME/SGSN should delay the sending of the Delete Session Request message to avoid the releasing of the Gxc session, to let sufficient time for the source MME/SGSN to recreate the UE session at the old/newly selected SGW. Rest of the behaviour is applicable for the PMIP based S5/S8 interface, without any change.

## Slide 4: Additional PCC Aspects
23.203 or CT3 specs (29.212, 29.213) have not really specified the behavior of the PCRF for the scenarios in Slide #2:
  What is the PCRF behavior if primary BBERF session is deleted (Step 20b)?
    Does the PCRF consider the non-primary BBERF session as the primary one? Does the PCRF wait for a time and then delete the IP-CAN session?
  What happens if there is no GW Control session for the UE (Step 26b)?

## Slide 5: CT4 Proposal: Roll back with SGW Change with Old SGW being reselected: PMIP
UE
New eNB
Old MME
NewMME
Old SGW
PGW
PCRF
HSS
New SGW
1. TAU Request
2. TAU Request
3. Context Request
4. Context Response
5. Context Ack
6. Create Session Request
9. PBU
10. PBA
11. Create Session Response
12. Update Location Request
15. Update Location Ack
13. Cancel Location Request
14. Cancel Location Response
7. GW CS Establish Request
8. GW CS Establish Response
16. Subscription based Reject
17. TAU Reject
18. Delete Session Request (SI = 1, OI = 0)
21. Delete Session Response
19. GW CS Terminate Request
20. GW CS Terminate Response
22. TAU Request
24. Delete Session Request (SI = 1, OI = 0)
27. Delete Session Response
28. Create Session Request
33. Create Session Response
26b. Clears up the non-primary GW Control
25. GW Control Session Termination Request
26. GW Control Termination Response
29. GW Control Session Establishment Request
30. GW Control Establishment Response
23. TAU Request
0a. GW Control Session
0b. IPCAN Session
8a.Primary GW Control Session
8b. Non-primary GW Control Session
Existing
SI = Scope Indication Flag;
OI = Operation Indication Flag
31 PBU
32. PBA
Delay
32b. Primary GW Control Session
Start Timer
Cancels Timer
Another eNB

## Slide 6: Comments on Previous Flow
It works, only if the following condition is met
  The new MME delays sending Delete Session Request, sufficiently, i.e atleast till the time that the UE goes back to old MME and old MME sends Create Session Request to the SGW.
However, if the delay is not long enough, (i.e the UE is not able to do TAU at an appropriate cell within the delay-time window) we will have the two issues highlighted on Slide #2.
  This will lead to unspecified behavior of PCRF.
  It is not clear if the PCRF will be able to recover from loss of primary BBERF session. So a delayed TAU could be successful at a later time, but PCRF may reject the setup of the new GW Control session, or even tear down the IP-CAN session before the delayed TAU occurs.
Even with the CT4 proposal, specification is needed of how PCRF handles scenario when primary GW Control Session is deleted, eg during a handover.

## Slide 7: Proposal-2: PCRF Handling of primary GW Control Session Deletion
PCRF keeps the IP-CAN session for a certain amount of time. When a new GW control session is established or a non-primary GW Control session becomes a primary GW Session (eg. RAT Change reported by PCEF which matches the RAT provided by non-primary BBERF), the PCRF cancels the timer and links the Gx to the new Gxx session. However, if during the wait period, there is any changes to QoS rules to be made, then the PCRF goes ahead and deletes the IP-CAN session (since this is an error scenario, there is no BBERF to enforce the new QoS rules).
  This can be captured in 23.203.
The Proposal-2 would not require to implement the change proposed by CT4 to MME.
It provides a solution to both 20b and 26b in Slide 2.

## Slide 8: PROPOSAL-2:Roll back with SGW Change: PMIP
UE
New eNB
Old MME
NewMME
Old SGW
PGW
PCRF
HSS
New SGW
1. TAU Request
2. TAU Request
3. Context Request
4. Context Response
5. Context Ack
6. Create Session Request
9. PBU
10. PBA
11. Create Session Response
12. Update Location Request
15. Update Location Ack
13. Cancel Location Request
14. Cancel Location Response
7. GW CS Establish Request
8. GW CS Establish Response
16. Subscription based Reject
17. TAU Reject
18. Delete Session Request (SI = 1, OI = 0)
21. Delete Session Response
19. GW CS Terminate Request
20. GW CS Terminate Response
22. TAU Request
24. Delete Session Request (SI = 1, OI = 0)
27. Delete Session Response
28. Create Session Request
33. Create Session Response
25. GW Control Session Termination Request
26. GW Control Termination Response
29. GW Control Session Establishment Request
30. GW Control Establishment Response
23. TAU Request
0a. GW Control Session
0b. IPCAN Session
8a. Primary GW Control Session
8b. Non-primary GW Control Session
Existing
SI = Scope Indication Flag;
OI = Operation Indication Flag
31 PBU
32. PBA
Another eNB
Starts Timer
Cancels Timer
20b. PCRF clears primary GW CS and starts timer

## Slide 9: Comments on Proposal-2
It works without any PMIP specific MME changes.
Works as long as the timer used by the PCRF is long enough for the UE to recover and create a new GW control session.
  Unlike in the MME or SGW, the PCRF can have a longer timer value.
Can also be used for inter technology HO with PMIP, where the following can be a not-so-rare scenario:
  The UE moves to a non-3gpp technology,
  Then aborts in short duration, eg due to radio conditions or subscription.
  The non-3GPP technology BBERF deletes GW Control session.
  UE returns back to 3GPP and does handover attach.
  But PCRF in the meantime has deleted the IP-CAN session.

## Slide 10: Proposal
Capture changes to 23.203 as in CR proposed by DOCOMO. S2-141050