## Slide 1
Discuss and Proposed Way Forward of NFV/SDN in EPC
China Mobile, CATR, ??
S2-141807
SA WG2 Meeting #103
19 - 23 May 2014, Phoenix, Arizona, USA

## Slide 2
Some Gap Analysis from NFV
Aspects of 3GPP specifications can be considered for gap analysis
Mobile Core network Architecture and system specifications.
Mobile network management specifications.
1. A potential enhancement mechanisms in order to keep information persistency
It may be beneficial to exchange information between TDF and PCRF/OFCS/OCS in order to synchronize usage monitoring and charging related data or to close a Charing Data Record (CDR)
2. In case a PCRF instance is terminated, All relevant Diameter sessions for the same IP-CAN session are still handled by a single PCRF.
This may require a study of potential enhancements or modifications to the PCRF discovery and selection.
3. In case a TDF instance is terminated and replaced by a new instance with a different IP address
it should be studied whether some additional mechanisms to report the TDF IP address change to other network nodes, such as PCRF/OCS/OFCS, should be introduced. This question is not unique but applies in general to any communicating entities in vEPC
Scenarios are identified when VNF instances are terminated…

## Slide 3
Some Other Possible Key Issues
Simplify existing load balance/overload control mechanism works in virtualization environment
  MME Pool/S1-Flex is simplified if MMEs are realized in the same virtual platform by VMs and signalling load are handled by load balancer
  Such load sharing can also be used for SGW to reduce SGW relocation signalling
Optimize signalling when network functions run on virtual machines in the same virtualization platform
  S11/S5/Gx interface are in the same DC
Other considerations
  Network sharing may be simplified when EPC is virtualized
Networking/Procedure/Signaling simplification when EPC is virtualized

## Slide 4
Need For Virtualization Migration Guidance-1
NFV is to implement telecom devices with general high volume standard storage, switches, and processors
While, existing control plane and data plane network elements are generally implemented in different platform
  Control plane NE are computing intensive, e.g., MME, therefore, they are implemented in ATCA platform
  Forwarding plane NE, e.g., PGW/SGW, handles data forwarding, therefore are implemented in router platform
How to realize the virtualized EPC
  Control plane
    To improve the signaling handling when NE are virtualized
  Forwarding plane
    CPU capability is improving but still cannot comparable with dedicated data forwarding processors
How to virtualize the control plane and data plane network element need to be investigated

## Slide 5
Need For Virtualization Migration Guidance-2
How to achieve teleco-grade virtualization
3GPP network elements such as MME/SGW/PGW are built with high availability. Namely, some blades are used to achieve N+1 or N+M reliability. When one of the blades encounter problems, the standby blade will work in few mil seconds.
  When different function blocks/blades are virtualized, it should still have such quick response when failure happens to ensure the user seamless experience, e.g., VoLTE or Video

## Slide 6
Proposed Way Forward
Study implementation guideline of vEPC
Study key issues and mechanism enhancement of realizing vEPC
Keep current architecture and interface the same as current topology
Start to study scenario & requirement of architecture optimization (C/U plane separation)
In R13:
In R14:
Functional block decomposition/composition is investigated to come out an efficient future proof architecture
It is suggested SA2 agree on the above and send LS to SA plenary