## Slide 1
SA WG2 Meeting #108 S2-150780
13 - 17 April 2015,San Jose Del Cabo, Mexico (revision of S2-15xxxx)
Source: Ericsson
Title: Way forward on DÉCOR Proposals for SA2#108
Document for: Approval
Agenda Item: 6.3
Work Item / Release: DÉCOR/Rel-13

## Slide 2: Key updates in Ericsson provided CRs compared to DECOR baseline CRs in SA2#107
Load balancing and Load re-balancing
SGSN Group ID
UE-NW GUTI mismatch
PGW selection over S8 (roaming case)

## Slide 3: Load balancing and Load re-balancing Solution used in 23.401 CR#2844
One common solution for all RATs
  Load balancing done by RAN considering DCNs
  Load re-balancing triggered by CN, using the load balancing in RAN (existing principle)
Idle mode UE
  Use the NAS message Reroute procedure at next TAU/RAU to load balance within the DCN. This avoids signaling impact on the Default DCN.
  Use the MMEGI/SGSN Group ID for selecting a new MME/SGSN within the DCN
    The MMEGI and SGSN Group ID identifies a DCN, i.e. the group of nodes serving the DCN in the area
    Simple configurations and hence reduced risk for misconfigurations
Connected mode UE
  Force a release of the connection and initiate an immediate TAU/RAU
  Use the idle mode procedure at the subsequent TAU/RAU.
    This avoids signaling impact on Default DCN.

## Slide 4: SGSN Group ID Solution used in 23.401 CR#2844
In discussions triggered by March CC, it was seen that
  An NRI coordination can achieve direct DCN selection in many cases (i.e. reducing the number of redirections at some DCN selection cases, at the cost of NRI space).
  When NRI coordination cannot be used (or isn’t used) and redirection is required, a SGSN Group ID is preferred compared to using NULL-NRI (i.e. NRI space saved, alignment with LTE, simplified configuration and reduced risk of misconfigurations).
23.401 CR#2844 uses:
  GERAN
    Use a SGSN Group Id in redirection and in BSC NNSF
  UTRAN
    Use a SGSN Group Id in redirection and in RNC NNSF
  E-UTRAN
    Use MMEGI in redirection and in eNB NNSF (as concluded in the TR)

## Slide 5: UE-NW GUTI mismatch Problems to be solved
Avoid UE-NW GUTI mismatch to happen
  Or there will be an increased re-attach load and other potential side effects when UEs are moving into DCN

## Slide 6: UE-NW GUTI mismatch Solution used in 23.401 CR#2844
Avoid HSS registration and subsequent Cancel Location in first MME/SGSN
  The UE and network registrations remains in sync since there is no change
  Follows the principle in a MOCN shared network where the UE is not registered by a redirecting node
  Normal scenario is a reroute out from first MME/SGSN, hence a common case
Pros
  Network and UE registration remains synchronized
  Minimal network impact
Cons
  Adds decision logic to HSS
  Update Location is used twice for the corner case when UE remains served by the same first MME/SGSN.

## Slide 7: PGW selection over S8 (roaming case); Problems to be solved
Operators may have different deployments of Dedicated CN
Configuration to support DCN over S8 should be small
Dependency between operator deployments should be minimized
PGW selection should be fast / efficient

## Slide 8: PGW selection over S8 (roaming case); Solution in 23.401 CR#2844 & 23.060 CR#1957
DNS can be used, but the details how DNS is used is removed
  The details of how DNS is used to retrieve a related PDN GW resource should be investigated and decided in stage 3 (CT4)
PGW selection can also be done in HPLMN
  As part or Create Session
  UE Usage Type is included in the Create Session Request
  Pros
    No dependency between VPLMN and HPLMN at interpretation of UE Usage Type values
    Leverage on existing GTP functionality
  Cons
    PGW impact

## Slide 9
End of presentation