## Slide 1: Migration path to NR/NGC
NTT DOCOMO
SA WG2 Meeting #116 S2-163693
11 - 15 July 2016, Vienna, Austria
Document for: Discussion
Agenda Item: 6.10.18
Work Item / Release: FS_NextGen / Rel-14

## Slide 2: Introduction
  Not everyone seems comfortable with Option 3. This doc shows DCM’s migration path, attempts to resolve concerns, and points to a real issue.

## Slide 3
Evolved Packet Core
(EPC)
LTE
(eNB)
UE
(LTE)
C-Plane
U-Plane
1. Current situation

## Slide 4
Evolved Packet Core
(EPC)
2. NR introduced
LTE
(eNB)
NR
(newNB)
UE
(LTE & 5G)
C-Plane
U-Plane

## Slide 5: Rationale for introducing NSA-NR
  A likely scenario is to introduce NR using frequencies higher than those being used for LTE.
  In this case, NR coverage is expected to be smaller than existent LTE coverage, especially for frequencies above 6 GHz.
  So, when considering use cases like eMBB requiring mobility, NSA-NR becomes attractive as the existent LTE layer can be leveraged to provide coverage/mobility, and NR can be used to provide U-plane boost.

## Slide 6: Rationale for using EPC (instead of NGC) when introducing NSA-NR
NSA-NR connected to EPC
(i.e. Option 3)
RAN: Introduce NSA-NR
  New design issues, development and testing required NR lower layers
CN: Reuse existent CN-RAN interface and CN-UE interface
  Limited (or no) new design issues, development and testing required for higher layers
Just build new Node B.
NSA-NR connected to NGC
(i.e. Option 7)
RAN: Introduce NSA-NR
  New design issues, development and testing required NR lower layers
CN: Possibly introduce new CN-RAN interface and CN-UE interface
  New design issues, development and testing required also for higher layers
Build new Node B and NGC
Option 3 provides the following benefits compared to Option 7:
NR can be introduced with less cost
NR can be introduced in a more stable manner
NR can be introduced earlier

## Slide 7
Evolved Packet Core
(EPC)
3. NGC introduced?
LTE
(eNB)
NR
(newNB)
UE
(LTE & 5G)
C-Plane
U-Plane
ＮNext Gen Core (NGC)ＧＧ
How to introduce?

## Slide 8: How to introduce NGC ?
  What is NGC in relation to EPC - 3 patterns exist.
    NGC is EPC evolution
    NGC includes EPC as a slice
    NGC replaces of EPC
EPC is currently working well to provide certain use cases, e.g. MBB services. When introducing NGC, its relation to EPC and the associated investments need to be justified.
Motivations for NGC should be made clear in the SI.
  NGC will enable new services?
  If NGC is going to replace EPC, what is the benefit/justification?
By paying attention to the above, EPC and NGC could be used in a balanced manner.

## Slide 9: Does supporting Option 3 bring (additional) technical concerns?
We don’t think so...
Coming back to Option 3
NGC in relation to EPC | (Additional) technical concerns due to Option3?
NGC is EPC evolution | N/A (since NGC is EPC evolution)
NGC includes EPC as a slice | N/A (since NGC includes EPC)
NGC replaces EPC | UE complexity Regardless of the support of Option3, UEs would need to support EPC protocol in order to operate in areas/network not supporting NGC. So Option3 will not incur additional UE complexity.
 | Interworking Regardless of the support of Option3, unless all eNBs are upgraded to support NGC connectivity at once nation-wide, interworking between EPC and NGC would be needed. So Option3 will not incur additional complexity for migration and interworking.

## Slide 10: Conclusion
  Option 3 has a possibility to introduce New Radio with less cost and in a more stable manner. And support of Option 3 will not incur additional technical concerns.
  NGC should be studied in relation to EPC. (3 alternatives)
    It is to be clarified what NGC brings.