## Slide 1: Drafting Session on Interworking and Migration
Tuesday, Feb 14 Lunch

## Slide 2: Goal
Get to some principle level agreements/reduce extended discussions in the main session.
Key ISSUES:
Single Registration/Dual Registration co-existence
  Does network provide indication to UE about which mode is selected?
    If so, is this (a) Nx support, or (b) single/dual registration mode support?
    If so, is this PLMN wide or 5G registration area wide?
Which flow to use for 5GC<-> EPC HO?

## Slide 3: Single/Dual registration definition (S2-170935)
In single-registration mode, UE has only one active MM state machine and is either in N1 mode or in S1 mode (when connected to 5GC or EPC, respectively). Similarly, the network keeps only one active MM state machine that is synchronised with the MM state machine in the UE and is located in either the AMF or in the MME. UE maintains one common registration for EMM and NMM indicating whether the UE is registered for packet services or not.
In dual-registration mode, UE can handle independent MM state machines: one MM state machine in N1 mode (i.e. for UE’s connection to 5GC) and one MM state machine in S1 mode (i.e. for UE’s connection to EPC). In this mode, the UE may be registered to 5GC only or EPC only or to both.
Mostly OK, can be edited in revisions.

## Slide 4: Mode Selection
Selected Mode provided by network to UE (open S2-170934, pg 9-11):
  QCOM (single/dual), NTT DOCOMO (single/dual), Intel (nx/no nx), LGE (nx/no nx)
    Reason: TAU Reject for single-registered UE on NGS->EPS HO. All sessions terminated on HO.
Selected Mode not provided by network to UE
Way forward:
Nx support is not needed to be provided to UE.
Single or dual mode is provided to the UE on 5GC registration
FFS: If this indication is also needed on EPC/EUTRAN Attach
Scoped on Accepted 5GC Registration area
Can be updated at next 5G Registration update. Valid in 5G Registration area.

## Slide 5: What modes MUST the UE support
For UE supporting EPC/5GC and require seamless session continuity, the UE must support dual-registration and single-registration
Must support single-registration
  Nokia
Way forward:
UE signals capability and network decides
    FFS: The need for mandating UE to support of one option or other.
    FFS: The need for mandating network to support of one option or other.

## Slide 6: Which QoS flows should be prepared during HO? (NGS -> EPS)
Default-QoS flows only
  S2-170919
Default & GBR +All QoS flows triggered by PGW/PCRF during HO
  S2-171013
Default & GBR QoS flows only with context mapping
  S2-170737
All QoS flows triggered by PGW/PCRF during HO
  Huawei.
We need to down select at minimum

## Slide 7: Background: Relevant papers
- | - | - | Co-existence of single and dual registration mode | - | -
6.5.9 | S2-170918 | P-CR | 23.501: Way forward for NGC-EPC interworking: General | Intel | 
6.5.9 | S2-170934 | DISCUSSION | Interworking Way Forward Discussion | NTT DOCOMO | 
6.5.9 | S2-170743 | P-CR | 23.501: Mobility between 5GC and EPC for interworking scenarios | Qualcomm Incorporated | 
6.5.9 | S2-171004 | DISCUSSION | Way forward for interworking | LG Electronics | Rel-15
6.5.9 | S2-171188 | P-CR | NGC-EPC Interworking Mode Selection | Samsung | 
6.5.9 | S2-171012 | P-CR | TS 23.501: P-CR for Feature description for interworking between 5GS and EPS | Nokia | 
6.5.9 | S2-170935 | P-CR | 23.501: Proposal for NGC-EPC interworking | NTT DOCOMO | 
Handover for single registration mode (23.502) |  |  |  |  | 
6.5.9 | S2-170804 | P-CR | 23.501: 5GC-EPC interworking | Ericsson | 
6.5.9 | S2-170919 | P-CR | 23.502: NGC-EPC interworking with 'single registered' operation (with NGx) | Intel | 
6.5.9 | S2-170967 | DISCUSSION | Way forward for Nx based interworking procedures | Huawei | Rel-15
6.5.9 | S2-171096 | DISCUSSION | Discussion on the interworking architecture and solution | ZTE | 
6.5.9 | S2-170936 | DISCUSSION | Nx-based interworking procedures from QoS point of view | NTT DOCOMO | 
6.5.9 | S2-170937 | P-CR | TS 23.502: Nx-based Handover procedure | NTT DOCOMO | 
6.5.9 | S2-170805 | P-CR | 23.502: 5GC-EPC interworking | Ericsson | 
6.5.9 | S2-171013 | P-CR | TS 23.502: P-CR for Single Registration-based Interworking from EPS to 5GS procedure | Nokia | 
6.5.9 | S2-170982 | DISCUSSION | PDU Session ID allocation when UE handover from EPS to NGS | Huawei, HiSilicon |