## Slide 1: FS_Vertical_LAN/TSN Drafting Session
Devaki Chandramouli (Rapporteur)
Nokia, Nokia Shanghai Bell
S2-1813053

## Slide 2
Key issue 3.1
FS_Vertical LAN
Architecture Conclusion – S2-1811770 (Samsung), S2-1811826 (Nokia, QCOM, Ericsson)
S2-1811770 proposes to specify all architecture options – Link model (Solution #7), Bridge model (Solution #8), Integration model (Solution #10)
S2-1811826 proposes to specify Bridge model (Solution #8)
Way forward:
  S2-1811826 revised to consider the two points below.
  Solution 8 with updates related to N6 (Translator)/N60.
  Add deployment recommendation in an annex:
    Mapping of QoS flows from multiple UE(s) to backhaul streams (e.g. TSN) – potential description in the annex
S2-1813053

## Slide 3
Key issue 3.1 – QoS part
FS_Vertical LAN
QoS conclusion – S2-1811770 (Samsung), S2-1812295 (ZTE), S2-1812193 (Nokia)
S2-1811770 proposes to specify QoS updates for all architecture options – Link model, Bridge model, Integration model
S2-1812295 proposes to adopt the merged solution (#16/#17) as way forward for the key issue#3.1
S2-1812193 proposes the principles to be considered for QoS framework as part of normative work.
Question:
  Should we agree on a specific solution to be progressed for QoS improvements as part of the conclusion? (or)
  Should we specify the agreeable principles as part of the conclusion and specify the actual improvements (e.g. additional parameters needed for deterministic QoS support/TSC scheduled transmission in the 5GS) as part of normative phase?
Way forward:
  Agree that 5GS QoS is reused with enhancements during the normative phase in order to support time sensitive communication. QoS requirements coming from CP/UP should be considered
S2-181xxxx

## Slide 4
Key issue 3.2 – TSN Synchronization
FS_Vertical LAN
TSN Synchronization – Samsung, Huawei, Nokia/QCOM, Ericsson
Nokia, QCOM - S2-1811829 (solution update), S2-1811830 (conclusion for solution #11 merged Option 2/3)
Ericsson proposals - S2-1812418, S2-1812419, S2-1812420, S2-1812417 (solution updates)
Huawei proposals - S2-1812413, S2-1812219 (solution updates – solution #19)
ZTE - S2-1812296 (conclusion proposal – solution 11 option 2/3)
Samsung - S2-1811770 (conclusion proposal)
Can we consider further merge?
Way forward:
  Narrow down the solution options (e.g. merge solutions that are similar). Identify System level impacts.
  Send an LS to RAN1/2 for further feedback on the solution options. Explain the impact from SA2 (e.g. UE to UPF) perspective.
S2-1813053

## Slide 5: BACK UP

## Slide 6: TSN Sync comparison
Huawei (S2-1812413) –
Two pre-conditions are as follows:
1. It is assumed UPF is synchronized with TSN GM T1, using mechanism defined by IEEE 802.1AS.
2. It is also assumed UE, NG-RAN, UPF are synchronized with 3GPP GM T2.
In order that UE can be synchronized with TSN GM, when the UPF receives the gPTP message from TSN GM, it forwards the gPTP message to the UE using the PDU session user plane.
When UPF sends gPTP packet to the downlink direction, it marks time stamps at both PDU layer (T) and layer (t).
For the UL transmission, UE sends the gPTP packet to the UPF, using the similar approach as DL packet handling.
NOTE: The transport layer can be GTP layer between UPF and RAN, and PDCP layer between RAN and UE, which requires RAN mark the time stamp on PDCP layer using the same value of GTP layer time stamp received from UPF.
Nokia, QCOM, ZTE (S2-1811830, S2-1812296) –
In this option, the 5G RAN utilizes its fine-frame structure (e.g. below PHY symbol level) to convey precise timing to the UE.
The 5G RAN receives the TSN timing information via direct connectivity with the TSN master clock, e.g. via underlying transport network by having an embedded TSN client within the gNB (this option does not use UE specific 802.1AS messages).
UPF is synchronized with TSN master clock with embedded PTP slave entity. In this option, the 5G system appears as an 802.1AS compliant entity, i.e. time aware relay, that allows 5G system to use 802.1AS standardized signalling to exchange time information with neighbouring entities.
External TSN clock is made available for UEs when gNB is synchronized with TSN GM through underlying PTP capable transport network by using (g)PTP.
S2-1813053

## Slide 7: TSN Sync comparison
Ericsson (S2-1812420) –
An alternative option can be an implementation with 5G blackbox model as described by Solution#8. In such an implementation, the entire 5G system can be kept untouched, therefore there will have minimal impact on the 5G system nodes.
The translator/adaptor function located at the edge of 5G system, can take care all 802.1AS related functions. For example, the (g)PTP support, time stamping can be all implemented in the translator. The translator function can be implemented either as part of UPF/UE, or as a stand-alone entity.

## Slide 8: Consideration for TSN Synchronization
In many PTP implementations 125 ms sync interval has been chosen. It could be also considered as minimum for Stratum 4 clocks with 4.6ppm error with synchronicity target if <1µs => Possible synch message rate values are in steps of 2^n.
If 1 step approach is used then there would be 3 messages or 4 messages total as in figure, transmitted with mentioned rate.
These messages fly between UPF and UE through N3 and Uu. So if there are 60 UEs in cell it means up to 1920 PTP messages per second in solutions that
Scheduling of UL needs to be aware of clock drift so that relay request messages are not lost.
Whilst in #11 Option 2&3, SIB broadcast is sent with 160ms period reaching all UEs by one shot.
“Which one is more complex 6.25 messages per second or 1920 messages per second”?