## Slide 1
SA WG2 Meeting #129 Bis
26th - 30th Nov., 2018, West Palm Beach, USA
Source: Nokia, Nokia Shanghai Bell
Title: Usage monitoring for multiple PCF deployment of the same DNN and S-NSSAI
Document for: Discussion
Agenda Item: 6.5.6
Work Item / Release: 5GS_Ph1/Rel-15
S2-1813325

## Slide 2
Problem Statement
If multiple PCFs are deployed in a [DNN, S-NSSAI], when usage monitoring is applied, “Remaining allowed usage subscription information” stored in the UDR may be retrieved and updated by multiple PCFs, thus the sum of the usage controlled by all the PCFs in a [DNN, S-NSSAI] may be over the retrieved “Remaining allowed usage”, as there’s no PCF interaction.

## Slide 3
Way forward Options
Option 1:
Define a solution in R15 to enable the same PCF is selected for all PDU sessions of the same [DNN, S-NSSAI] for the UE when usage monitoring is required for this UE (see next page for the solution)
Option 2:
Define a solution in R15 to enable sharing of allowed usage per [DNN,S-NSSAI] by multiple PCFs, each of them handling a SM Policy assoication to the [DNN, S-NSSAI]. No restrictions to select the same PCF.
Option 3:
Ensure only one PCF is selected per [DNN, S-NSSAI] by operator configuration (e.g. using NRF configuration or SMF local configuration) in R15.
Develop a solution in R16.

## Slide 4
AMF
PCF 2
SMF
BSF
SUPI,
IP,
DNN,
S-NSSAI,
PCF 2 ID
Solution to select the same PCF for multiple PCF sessions of the UE in the same [DNN, S-NSSAI]
PCF registers itself to the BSF once IP address is allocated for the PDU session.
When PCF registers itself to the BSF, and BSF discovered that for the same [SUPI,DNN, S-NSSAI] there is already a PCF registered, it returns a PCF ID to the PCF.
If usage monitoring is required for the SUPI, the PCF provides the PCF ID to the SMF for it to reselect a PCF.
SMF terminates the SM policy association with the PCF and establishes SM policy association with the PCF based on the received PCF ID.
Note: PCF can identify whether usage monitoring is required from the PCC policy data retrieved from the UDR
SUPI,
DNN,
S-NSSAI,
PCF 1 ID
SUPI,
DNN,
S-NSSAI,
PCF 1 ID
PCF 1
Con:
PCF redirection may be required (SMF terminates the current SM policy association and establishes a new SM policy association)