## Slide 1: Drafting Session 23.742 eSBA Key Issue #3 Conclusions
October, 2018

## Slide 2: Agenda
Agree on scope of drafting session
  Identify any principles which are missing from the 9 points.
  Introduce / agree most contentious points to discuss.
Discuss / Agree on Service Framework Functionality
  Discuss point 2 (functionality for service framework)
Discuss / Agree on Service Framework Compatibility and Extensibility
  Discuss point 4 (backward/forward compatibility, flexibility and extensibility)
Discuss / Agree on Service Framework Topology
  Discuss points 7 & 8 (topology, SF domain/scope)
Discuss / Agree Other Points Which Require Clarification
  Time permitting

## Slide 3: Service Framework Functionality Common Service Framework functionalities include, but are not limited to:
Service Registration Management
  Extension of R15 SBA (ie. NRF)
  Handling of addition, removal and replacement of NF service instances
    When new selectable peers become available or existing peers disappear from the system.
Adaptation Function
  Adapt 3GPP SBI to the Service Framework.
  Implementation not specified by 3GPP.
  Enable backward and forward compatible extension of R15 SBI
Discovery of communication peers
  Maintain compatibility with R15
  Enable separation of business logic and discovery in NF.
Selection of communication peers
  Includes load-balancing between selectable communication peers.
  Enable separation of business logic and selection in NF.
Communication Service
  Reliable delivery of messages (request and response) between communication peers
  Congestion / overload control
Authorization Management
  Policy enforcement, authorization of the message delivery.
Service Monitoring
  Enables load balancing, circuit breaking, etc.
Notes: This is the functionality allocated to the SF.
Taken from Point 2 with changes:
  Clarified name/wording of the functionality
  Aligned with functions shown in the SF figure.
  Added Adaptation Function to clarify its role.
  Re-ordered functions in the list.
Objective is to agree what the SF is expected to do.

## Slide 4: Service Framework Compatibility and Extensibility
Interface between the NF services and the Service Framework: the selected solution shall use the SBIs used by consumers and producers in SBA.
  In case of service discovery and/or NF service selection delegated to the Service Framework (aka implicit mode of discovery), the 3GPP SBIs may be enhanced to provide additional information (ie SBI additional parameters) that can be consumed by the service framework.
    Enhancements to the SBIs shall be conditionally required based on the functionality being invoked by the request.
    Any additional parameters required to support the enhanced Service Framework functionality (ie. Service discovery) should be located in the http headers or the URI as opposed to the body of the message. This precludes having the Service Framework parse the body of the request for the parameters.
  Impacts on existing Services and Interfaces (backward compatibility): The service framework is compatible with R15. The R15 consumer is not aware of a R16 service framework existence, other than have it configured as its HTTP outbound proxy.
  Impacts on existing Services and Interfaces (forward compatibility): Delegation of service discovery to the service framework can be achieved by means of configuration, i.e. the service consumer can be configured to skip service discovery and simply send the actual service request to the service framework. In case the discovery is skipped additional parameters needed for NF service selection may be needed.
  Impacts from conclusions to key issue 4 (reliability): Several of the proposed solutions for key issue 4 introduce a set concept to identify groups of services and/or NF. These sets represent a discoverable entity. Dependent on the selected solution to key issue 4, the Service Framework should support discovery and selection of sets. Any enhancements required to the discovery function to support sets shall apply to both explicit and implicit modes of operation (ie. A Rel-16 NF which invokes explicit discovery will be able to discover sets for use in producer selection).
Notes: This is how the SF interfaces with the NF.
Taken from point 4 – changes TBD
  Backward compatibility
    No changes to R15 SBI
  Forward compatibility
    Use of R16 SF Enhancements is conditional (ie. NF can continue to use R15 SBI and procedures)
    Allows interoperation between R15 and R16 NF
  Extensibility
    New features introduced without impacting older NF
Objective is to agree on how the SF enables a path forward for Service Based architecture.

## Slide 5: Service Framework Topology
Network slicing:
  The Service Framework, based on operator preferences, may be deployed at three levels at a minimum:
    PLMN level (one SF for the PLMN)
    Slice common level (one SF for the PLMN level and another SF for all NS)
    Slice level (one SF for the PLMN level and another SF for each NS)
Roaming support:
  The SEPP communicates with the Service Framework using the 3GPP SBI.
    The SEPP is one of the services shown in the PLMN level.
  The interactions between NF services and the SEPP for roaming procedures are handled by the Service Framework.
Notes: This is the topology of the SF when deployed in a network
Taken from points 7 and 8 – changes TBD
Objective is to agree on:
  Scope / domain of an instance of SF
  Levels of hierarchy at which an SF can be deployed.

## Slide 6: Discussion on Remaining Points
As time permits, discussion regarding terminology / clarification of remaining points.