## Slide 1: Source: Ericsson Title: Resource Release at 5GS to EPS handover with N26 Document for: Discussion/Agreement Agenda Item: 6.5.9 Work Item / Release: 5GS_Ph1
SA WG2 Meeting #133 Reno, Nevada, USA, 13-17 May 2019
Tdoc S2-1905091

## Slide 2: Discussion (1/3) Resource to be released at 5GS when 5GS to EPS handover (with N26) is completed
In Non-roaming and LBO roaming, the following resource needs to be released:
NG-RAN resource
Indirect data forwarding tunnel(s) if any
MME
AMF
SGW
NG-RAN
eNB
S5
N11
PGW-C
SMF
UE handover
MME
AMF
SGW
NG-RAN
eNB
S8
N16
UE handover
V-SMF
PGW-C
SMF
Home routed roaming
Non-roaming and LBO roaming
V-UPF
N11
N26
N26
UPF
N4
N4
UPF
N4
1
2
1
2
In Home routed roaming, the following resource needs to be released
NG-RAN resource
SM Context in V-SMF and the indirect data forwarding tunnel(s) if any
Indirect DF tunnel(s) if any
SM context, and Indirect DF tunnel(s) if any
2
1
2
1

## Slide 3: Observations (1/2)
TS 29.502 (v15.3.0) has the following:
  5.2.2.4 Release SM Context service operation
  The Release SM Context service operation shall be used to release the SM Context of a given PDU session, in the SMF, or in the V-SMF for HR roaming scenarios, in the following procedures:
  …
  2a. On success, the SMF shall return a "204 No Content" response with an empty payload body in the POST response.
  If the POST request contains a vsmfReleaseOnly indication (i.e. for a 5GS to EPS Idle mode mobility or handover, for a Home Routed PDU session with assigned EBI(s)), the V-SMF shall release its SM context and corresponding PDU session resource locally, i.e. without signalling towards the H-SMF.
[Observation-1] Stage 3 has specified that AMF uses Nsmf_PDUSession_ReleaseSMContext to remove the SM context in V-SMF with vsmfReleaseOnly indication .
TS 23.502 (v15.5.1) has the following:
  4.11.1.2.1 5GS to EPS handover using N26 interface
  …
  10a. If indirect data forwarding applies, the AMF sends the Nsmf_PDUSession_UpdateSMContext Request (Serving GW Address(es) and Serving GW DL TEID(s) for data forwarding) to the PGW-C+SMF, for creating indirect data forwarding tunnel. If multiple PGW-C+SMFs serves the UE, the AMF maps the EPS bearers for Data forwarding to the PGW-C+SMF address(es) based on the association between the EPS bearer ID(s) and PDU Session ID(s). In home-routed roaming case, the AMF requests the V-SMF to create indirect forwarding tunnel.
[Observation-2] Indirect data forwarding tunnel(s) are established using the same SMF as for the PDU Session, which means
  in HR roaming, when the SM context in the V-SMF is released, it means the indirect data forwarding tunnel(s) if any are also released, i.e. no separate signaling is needed for release of indirect data forwarding tunnel(s)
  NOTE: TS 23.401 states “Indirect forwarding may be performed via a Serving GW which is different from the Serving GW used as the anchor point for the UE”, therefore separate signaling is need to release the indirect data forwarding tunnels.

## Slide 4: Discussion (2/3)
TS 23.502 (v15.5.1) has the following:
  4.11.1.2.1 5GS to EPS handover using N26 interface
  ….
  12d. The AMF acknowledges MME with Relocation Complete Ack message. A timer in AMF is started to supervise when resources in the in NG-RAN and PGW-C+SMF shall be released.
[Observation-3] A timer in AMF is started to supervise when resources in RAN and in PGW-C+SMF in the 5GS side shall be released when 5GS to EPS handover is completed, but it’s unclear what resource in PGW-C+SMF should be released.
TS 23.502 (v15.5.1) has the following:
  4.11.1.2.1 5GS to EPS handover using N26 interface
  …
  21. If indirect forwarding was used, then the expiry of the timer at AMF started at step 12c triggers the AMF to invoke Nsmf_PDUSession_UpdateSMContext Request service operation with an indication to release the forwarding tunnels of the V-SMF, in order to release temporary resources used for indirect forwarding that were allocated at step 10. The V-SMF returns Nsmf_PDUSession_UpdateSMContext Response message.
[Observation-4] Step 21 is a bit confusing (1) No timer was started in step 12c ; (2) Nsmf_PDUSession_UpdateSMContext releases only resource for indirect forwarding tunnels, but the release of SM context in V-SMF is not mentioned.

## Slide 5: Proposal
In home routed roaming, the SM context in the V-SMF shall be released. Per [Observation-1], Nsmf_PDUSession_ReleaseSMContext is used.
  [Proposal-1] For home routed roaming, it’s proposed that the source AMF use Nsmf_PDUSession_ReleaseSMContext at expiration of the timer started at step 12d to release the SM context in V-SMF. The indirect data forwarding tunnels if any are released together.
For non-roaming or LBO roaming, the PGW-C+SMF is aware of the completeness of PGW-C+SMF (i.e. when Modify Bearer Response is sent),
  [Proposal-2] It’s proposed that the PGW-C+SMF, when getting to know that 5GS to EPS handover is complete, release the indirect data forwarding tunnels (if any) which may be after some delay.
  23.502 CR1337 (S2-1905092) and 23.502CR1338 (S2-1905093)

## Slide 6
THANK YOU !