## Slide 1: Discussion on notification of Alternative QoS profile
Sunghoon Kim
Samsung

## Slide 2: How it works
SA2 agreed and concluded solution during study phase that
  V2X Application Server (acting as AF) provides Service Information to PCF (via NEF) including multiple alternative service requirements
  PCF determines Alternative QoS Parameters based on the requested service requirement from the V2X AS, and send it as PCC rule to the SMF
  SMF derives Alternative QoS Profile based on the Alternative QoS Parameter set. In addition to the target QoS profile, the SMF provides one or more Alternative QoS Profiles to the NG-RAN
  In the NG-RAN, in case the target QoS profile cannot be guaranteed by the NG-RAN, the NG-RAN can notify the QoS that can still be guaranteed by referring to one of the Alternative QoS profile(s)
Open issues
  How SMF to set alternative QoS Profiles
    Priority order?
    including original QoS profile in order to cover the case that better QoS profile can be guaranteed.
  How NG-RAN to determine and notify the guaranteed QoS parameter
    How NG-RAN determines to notify regarding Alternative QoS Profiles? If one of QoS parameters cannot be guaranteed? Or all of QoS parameters in the profile cannot be guaranteed?
    When it notifies, Index of Alternative QoS Profile? Or value for GFBR, PDB, or PER that guaranteed?

## Slide 3: How SMF to set Alternative QoS Profiles
Priority order (as per proposal from Huawei in the last meeting S2-1906789)
  Priority order of Alternative QoS Profiles was proposed in order to reflect what V2X AS prefers for adjusting their service.
  For example, if V2X AS considers that GFBR is more important than PDB/PER, Alternative QOS Profiles can be set as
  [current QoS] GFBR = 3Mbps, PDB = 10ms
  [ Alt. QoS #1 ] GFBR = 2Mbps, PDB = 30ms
  [ Alt. QoS #2 ] GFBR = 1Mbps, PDB = 10ms
  [ Alt. QoS #3 ] GFBR = 1Mbps, PDB = 30ms
  In terms of PDB, #2 is better QoS profile than #1, but it reflects that V2X AS prefers #1 than #2. If current GFBR goes down to 2Mbps, the NG-RAN determines to notify #1.
  However, NG-RAN does NOT have to know preference of the alt. QoS Profiles, because anyway PCF will take a decision to modify QoS parameter based on the notification from NG-RAN. PCF stores such logic inside and can consider which QoS parameter would be better based on the requested service information from the V2X AS. For example, if NG-RAN notifies current GFBR value (=2Mbps) and PDB (=10ms), the PCF take this information into account for modifying PCC rule along with the requested information from the V2X AS. Therefore, no clear benefit can be seen If NG-RAN is influenced for the application level preference.
Proposal 1: It doesn’t have to be in priority order, as final decision for QoS modification will be made by PCF. The order of Alternative QoS Profile(s) is up to implementation. NG-RAN just uses Alternative QoS Profiles as a filter to determine which value should be notified. It is proposed to keep the logic of application preference only inside of PCF, not to NG-RAN.

## Slide 4: How SMF to set Alternative QoS Profiles
Whether to include target QoS Profile in the Alternative QoS Profiles
  It is important to cover the case if network situation is going better so that NG-RAN can support original QoS Profiles. In order to enable such ‘upgrade’ of QoS profile, the Alternative QoS Profiles should include the original QoS profiles or better QoS profiles when the PCF performs QoS modification.
  For example,
  1. NG-RAN notifies Alternative QoS profile #2 that can be supported
  2. PCF decides to modify QoS parameters regarding the Alt. QoS Profile #2. During QoS modification procedure, PCF provides Alternative QoS parameters which including original QoS parameters to the SMF, and the SMF derives Alternative QoS Profiles.
  3. As a result, updated Alternative QoS profiles includes the original QoS profile.
Proposal 2: It is required to add requirement for the case of improvement of QoS profile.

## Slide 5: How NG-RAN to determine and notify the guaranteed QoS parameter
For example, if target QoS Profile and Alternative QoS profiles are set as following:
  [current QoS] GFBR = 3Mbps, PDB = 10ms
  [ Alt. QoS #1 ] GFBR = 2Mbps, PDB = 30ms
  [ Alt. QoS #2 ] GFBR = 1Mbps, PDB = 10ms
  [ Alt. QoS #3 ] GFBR = 1Mbps, PDB = 20ms
  Question 1: value in the Alt. QoS Profile is upper bound or lower bound?
  It should be lower bound as it is for guaranteed value based on current network status.
  Question 2: If GFBR goes to 2.5Mbps (but PDB is same), what NG-RAN should do?
  Option 1) NG-RAN notifies #1 (because current GFBR value is closer to #1)
  If PCF receives #1, PCF does NOT know PDB=10ms still can be supported. Therefore, the QoS modification may unnecessarily downgrades the PDB value to 30ms. (even though NG-RAN can support 2.5Mbps with PDB=10ms!)
  Option 2) NG-RAN notifies #2 (because PDB = 10ms)
  If PCF receives #2, PCF does NOT know GFBR=2.5Mbps can be supported. Therefore, the QoS modification may unnecessarily downgrades the GFBR value to 1Mbps. (even though NG-RAN can support 2.5Mbps with PDB=10ms!)
  Option 3) NG-RAN notifies #1, but also current PDB value (=10ms)
  PCF knows current NG-RAN status better than option 1/2. PCF can decide to support 2Mbps with 10ms PDB.
Proposal 3: NG-RAN uses the Alt. QoS Profiles as filter. If all values are met to the Alt. QoS Parameter, NG-RAN can notify the index of the Alt. QoS Profile. If not all values are met to the Alt. QoS parameter, NG-RAN needs to indicate the value that can be supported.
NOTE: Sending index only may save the size of the QoS notification message, but as it is inside CN signaling, the benefit is marginal.

## Slide 6: Proposal
Proposal 1: Alternative QoS Profiles doesn’t have to be in priority order, as final decision for QoS modification will be made by PCF.
Proposal 2: Adding requirement to PCF/SMF operation in order to cover the case of improvement of QoS profile (e.g., Alternative QoS profiles should include original QoS profile or better QoS parameter value if requested)
Proposal 3: NG-RAN uses the Alt. QoS Profiles as filter. If all values are met to the Alt. QoS Parameter, NG-RAN can notify the index of the Alt. QoS Profile. If not all values are met to the Alt. QoS parameter, NG-RAN needs to indicate the value that can be supported.
Based on the agreement on the group, the outcome should be captured in corresponding CRs.