## Slide 1: FS_MUSIM Status Report
Sašo Stojanovski
Intel Corporation

## Slide 2: FS_MUSIM status after SA2#141E (1/2)
WI Code | Work Item Title | WP | Target Date | WID#
FS_MUSIM | Study on system enabler for Multi-USIM devices | 80% > 84% | Dec, 20 | SP-200091
General
  FS_MUSIM TR 23.761 v1.1.0 is available here.
  Evaluations on all three key issues have been updated.
  Several solutions have been updated (#1, #3, #14, #15, #24)
Key Issue 1 (Handling of MT Service):
  One new solution agreed (Sol#28: “Important service paging cause”; initially proposed as a variant of Sol#1)
  Show-of-Hands on Paging Cause indicated the following support: Multiple Paging Causes (19 companies), One Paging Cause (19 companies), No Paging Cause (8 companies), Postpone the decision (10 companies). There was no SoH on objections for each option. No decision could be made
  Interim conclusions agreed that no MMI interaction shall be required for the UE respond to paging (then a list of Editor’s notes)
  Next Steps: Draw final evaluations and conclusions in SA2#142E.
Key Issue 2 (Enable Paging reception):
  No progress in this meeting on interim conclusions due to RAN dependency
  Next Steps: Draw final evaluations and conclusions in SA2#142E.
Key Issue 3 (Co-ordinated leaving):
  Interim conclusions updated for NAS leaving (EPS case) with clarification of assistance information content.
  No progress on 5GS leaving due to RAN dependency.
  Next Steps: Draw final evaluations and conclusions in SA2#142E.

## Slide 3: FS_MUSIM status after SA2#141E (2/2)
  RAN impacts and dependencies:
  All three key issues may potentially lead to solutions with RAN impact and may require RAN coordination.
  Feedback from RAN2 and RAN3 (requested from SA2#140E) is needed for SA2#142E to conclude the study.
  SA3 dependencies:
  Feedback from SA3 (requested from SA2#140E) is needed for SA2#142E to conclude the study (namely on Busy indication, any Paging cause privacy).
Contentious Issue:
  Paging cause and paging filtering have been the cause of significant debate in SA2#141E. It is expected that the debate will be resolved in SA2#142E.
Focus for the Next Meeting (SA2#142E):
  Ahead of SA2#142E: Organize a conference call (if feasible) to discuss Way Forward proposals to finalize the conclusions.
  During SA2#142E:
    Focus on finalizing the conclusions.
    No new solutions (except if proposed as a Way Forward proposal to enable conclusions)
Overall Plan:
  SA2#142E: Final evaluations and conclusions. TR 23.761 and WID expected to be sent to SA#90 plenary for approval.
Risks:
  Due to RAN and SA3 dependencies, completion of the study may not be possible in Q4 for all key issues.