## Slide 1: The discussion on AIML for 5GS Service to enable 5GC and Air interface Intelligence
Vivo, China Mobile
Notes: 1

## Slide 2: Background and Motivation
The convergence of communication network and AI technology already made some progress. Up to now, the 5GS including both RAN and SA2 has studied and/or specified the AI-enabled network architecture and leverage AIML to enable 5GC and Air interface Intelligence.
Based on the above, the work of AI/ML for 5GS in Rel-19 is proposed to expand the scope of network AI services to leverage AI/ML technologies to enable 5GC and Air interface Intelligence(which has been studied/concluded in RAN groups) by providing network automation and improving the efficiency of 5G network architecture.
In order to leverage AIML technologies to enable 5GC and Air interface Intelligence, this study item is to focus on following two parts:
    Part B: AI/ML alignment and convergence for Air Interface and 5G Core network
    Part A: Architecture enhancement to support 5G Core Intelligence
The following slides focus on Part B: AIML convergence for RAN and SA2 and see joint discussion paper S2-2306503 from China Mobile/vivo for Part A: Architecture enhancement
Notes: S2-S2-2306503

## Slide 3
xxx
RAN Progress Summary and potential SA2 impacts
(High level)

## Slide 4
xxx
RP-221348.zip New SID on Artificial Intelligence (AI)/Machine Learning (ML) for NR Air Interface is approved in RAN#96 with following objectives (high level):
  Use case study: CSI feedback enhancement, Beam management, Positioning accuracy enhancements
  AI/ML framework and terminology
  Network-UE collaboration levels
  Performance evaluation methodology and KPIs
High level progress summary and future plan
  Complete AI/ML model, terminology and description to identify common and specific characteristics for framework investigations, since main aspects of lifecycle management have been deeply discussed
  Evaluate performance benefits of AI/ML based algorithms for the agreed use cases in the final representative set, since various performance results have been provided for not fully aligned scenarios and use cases
  Assess potential specification impact, specifically for the agreed use cases in the final representative set and for a common framework
Introduction of Study on AI/ML for NR Air Interface in RA1

## Slide 5
xxx
AI/ML framework and terminology
  SA2 Impacts: alignment btw SA2 as AI/ML framework and terminology has been defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Lifecycle management of AI/ML model: e.g., data collection, model training, model deployment, model transfer, model inference, model monitoring, model updating, Model selection/activation/deactivation/switching/fallback, UE capability
  SA2 Impacts: alignment btw SA2 as Lifecycle management esp. data collection, model training, model inference, model monitoring defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Use case study
  CSI feedback enhancement: CSI compression, CSI prediction
  Beam management: spatial domain beam prediction, temporal domain beam prediction
  Positioning accuracy enhancements: direct AI/ML positioning, AI/ML assisted positioning
    SA2 Impacts: LCS architecture enhancement needed and related with ML Model delivery and UE data collection (positioning specific)
Network-UE collaboration levels (SA2 impacts: ML model transfer and mode ID/analytics ID concept)
  Level x: No collaboration
  Level y: Signaling-based collaboration without model transfer
  Level z: Signaling-based collaboration with model transfer
Performance evaluation methodology and KPIs
  SA2 impacts: alignment btw SA2 regarding ML Model performance monitoring in R18 eNA_ph3 KI#1 and potential R19 enhancement
RAN Progress (1/3)

## Slide 6
xxx
Model performance monitoring
  Model monitoring methods
    Monitoring based on inference accuracy, including metrics related to intermediate KPIs for AI/ML model (comparison between model output and label, e.g., NMSE, SGCS)
    Monitoring based on system performance, including metrics related to system performance KPIs (e.g., BLER, throughput)
    Monitoring based on data distribution, including Input-based and output-based
  Model monitoring KPIs, including accuracy and relevance, overhead, complexity, latency
  SA2 impacts: alignment/convergence btw SA2 regarding ML Model performance monitoring in R18 eNA-Ph3 KI#1 and potential R19 enhancement
Model transfer/delivery
  Model transfer format
    Proprietary-format
    Open-format, including parameter-only updating, both parameter and structure updating
    SA2 impacts: alignment/convergence btw SA2 regarding in R18 eNA_ph3 KI#5 Enhance trained ML Model sharing and previous work in R17 eNA_ph2 for trained ML Model sharing
  Model transfer/delivery signaling, including CP-based and UP-based
    SA2 impacts: alignment btw SA2 or enhancement in SA2 regarding UP solution DCAF/EVEX UE data collection defined in R17 eNA_ph2 in SA2
RAN Progress (2/3)

## Slide 7
xxx
Model/Functionality Identification
  Model ID concept, including logical model ID and physical model ID
  Relationship between UE feature, functionality, model, applicable conditions
  Model description information
  SA2 impacts: alignment btw SA2 or enhancement in SA2 regarding ML Model ID definition/analytics ID since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
Model training types for two-sided models
  Type 1: Joint training of the two-sided model at a single side/entity, e.g., UE-sided or Network-sided
  Type 2: Joint training of the two-sided model at network side and UE side, respectively.
  Type 3: Separate training at network side and UE side, where the UE-side CSI generation part and the network-side CSI reconstruction part are trained by UE side and network side, respectively.
  SA2 impacts: alignment btw SA2 or enhancement in SA2 to support ML Model deliver to UE regarding ML Model delivery within core network ,which is already supported in R17/18 eNA but not involve UE.
RAN progress (3/3)

## Slide 8
xxx
RAN Progress Summary and Potential SA2 impacts
(Detailed Analysis)

## Slide 9
Summary of AI/ML framework and terminology in SA2 and RAN
Vivo view: Alignment/convergence btw SA2 and RAN as AI/ML framework and terminology has been defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
SA2 R18 eNA_ph3
RAN1 FS_NR_AIML_Air
Since R16, Data Collection feature permits NWDAF to retrieve data from various sources and Network Data Analytics Exposure is defined in TS 23.288.
Terminology such as ML Model ID/Analytics ID and Analytics logical function and Model Training logical function
Data collection has large impact on other modules of AI/ML framework. Collections of training data, inference data and monitoring data would have different requirements and procedures..
Terminology such as AI/ML Model, data collection, AI/ML model training, model identification, functionality identification

## Slide 10
Summary of Lifecycle management of AI/ML model in SA2 and RAN
Vivo view: Alignment/convergence btw SA2 and RAN as AI/ML framework and terminology has been defined in since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
SA2 R18 eNA_ph3 KI#1
RAN1 FS_NR_AIML_Air
Since R16, Data storage architecture via Message Framework defined in TS 23.288
Data collection is one of the key aspects in lifecycle management of AI/ML in RAN study

## Slide 11
Summary of Model performance monitoring in SA2 and RAN
Vivo view: Alignment/convergence between SA2 regarding ML performance monitoring in R18 eNA-Ph3 KI#1 and potential R19 enhancement
SA2 R18 eNA_ph3 KI#1
RAN1 FS_NR_AIML_Air
In R18, define Model/Analytics Accuracy for classification in TS23.288, which is the number of correct predictions out of all predictions.
In R19, may further discuss how to measure Model performance for regression
Model monitoring is used to against generalization problem, and then is the key point in R18 RAN1
Model monitoring methods and monitoring KPIs have been deeply discussed

## Slide 12
Summary of Model/Functionality/Analytics ID in SA2 and RAN
Vivo view: Alignment/convergence between SA2 and RAN or enhancement in SA2 regarding ML Model ID definition/analytics ID since R16 eNA/R17 eNA_ph2/R18 eNA_ph3
SA2 R18 eNA_ph3 KI#1
RAN1 FS_NR_AIML_Air
Since R16, NWDAF service consumer subscribes to a (set of) ML Model associated with a Analytics ID(s)
The NWDAF containing MTLF notifies the NWDAF service consumer with a set of pair(s) of ML Model ID
NOTE: the structure and format of the ML Model ID and its uniqueness are up to stage 3 in R18.
Model ID is important in model identification to distinguish different models with same functionality

## Slide 13
RAN2 progress：
  CP solution：Logged/Immediate MDT, L3 measurements, L1 measurement (CSI reporting), UAI, Early measurements, LPP (for positioning only, related to AI based positioning discussion in SA2)
  UP solution: EVEX framework(highly related to SA2 DCAF/NWDAF)
Note: Please see joint discussion paper S2-2306506 from QUALCOMM/vivo for the details.
    vivo view: UP solution is complementary to CP solution and SA2 should be tasked to study whether and how to enhance UE data collection framework to meet RAN requirement (coordinated with RAN).
Summary of UE data collection

## Slide 14
R17 SA2 eNA_ph2 progress
R18 SA2 eNA_ph3 progress
Summary of Model transfer/delivery in SA2
In R17, only Model delivery within 5GC between same vendor is supported
Model delivery to UE is not supported
In R18, introduce ML model Interoperability information to somehow support Model delivery within 5GC NWDAFs among multi-vendors;
ML Model Interoperability Information, this is vendor-specific information that conveys, e.g., requested model file format, model execution environment, etc.
Still Model delivery to UE is not supported

## Slide 15
Training
NW side
Neutral site
UE side
Compiling
Storage
Inference (inside UE)
Model delivery
Case y
Training
NW side
Neutral site
UE side
Compiling
Storage
(inside NW)
Inference (inside UE)
Model transfer in proprietary format
Case z1
Training
NW side
Neutral site
UE side
Compiling
Storage
(inside NW)
Inference (inside UE)
Model transfer in proprietary format
Case z2
Training
NW side
Neutral site
UE side
Compiling
(inside UE)
Storage
(inside NW)
Inference (inside UE)
Model transfer in open format
Case z3
Training
NW side
Neutral site
UE side
Compiling
(inside UE)
Storage
(inside NW)
Inference (inside UE)
Model transfer in open format of a known or unknown model structure at UE
Case z4 and z5
Summary of Model transfer/delivery discussion in RAN1

## Slide 16
How to support Model delivery to UE - RAN2 progress
Based on RAN1 draft conclusion of model transfer/delivery，RAN2 listed all potential solutions 。
  Option 1: Model transfer/delivery between UE and gNB via CP and UP solutions
    Applicable use cases: CSI feedback enhancement, Beam management
  Option 2: Model transfer/delivery between UE and CN (except LMF) via CP and UP solutions
    Applicable use cases: CSI feedback enhancement, Beam management
  Option 3: Model transfer/delivery between UE and LMF via CP and UP solutions
    Applicable use cases: Positioning accuracy enhancement
  Option 4: Model transfer/delivery between UE and server
    Applicable use cases: CSI feedback enhancement, Beam management, Positioning accuracy enhancement
    vivo view: SA2 should be involved and tasked to study whether and how to support Model delivery to UE (coordinated with RAN).
Summary of Model transfer/delivery discussion in RAN2

## Slide 17
For characterization and performance evaluations of AI/ML based positioning accuracy enhancement, the following two AI/ML based positioning methods are selected.
  Direct AI/ML positioning
  AI/ML assisted positioning
AI based Positioning - RAN1 progress
Summary of AI based Positioning discussion in RAN

## Slide 18
Uses cases listed by RAN
Uses cases listed by RAN

## Slide 19
Coordination between LMF and NWDAF
  How CN help train AI LCS Model(s), including A-AIML/D-AIML
  Model delivery enhancement
    Regarding UE based A-AIML/D-AIML, how CN delivery Model(s) to UE
    Regarding RAN based A-AIML, if CN involved, whether and how CN delivery Model(s) to RAN
    etc.
Data collection enhancement for AI based Positioning
AI model performance monitoring for positioning related to how to measure ML Model performance for regression
5GC architecture enhancement to support AI based Position
5GC architecture enhancement to support AI based Positioning
Notes: 基于AI的定位增强—SA2网络架构增强Objective(s)

## Slide 20
Objectives for new study on AIML for 5GS (draft)
Part B: AI/ML alignment and convergence for Air interface and Core network
  Terminology alignment btw RAN and SA2 (e.g. AI/ML Mode in RAN vs ML Mode defined in SA2)
  UE data collection framework enhancement to support AI/ML use cases (coordinated with RAN, UP solution related to DCAF/EVEX UE data collection defined in R17 eNA_ph2 in SA2)
  ML Model delivery to UE(Model delivery within core network supported in R17/18 eNA without involving UE)
  Lifecycle management of AI/ML model btw RAN and SA2 (especially data collection, model training, model inference, model monitoring )
  SA2 and RAN Convergence for Model ID/Analytics ID defined in SA2 since R16 eNA and Model ID/feature ID studied/concluded in RAN R18
    Model ID concept coordination btw RAN and SA2
    Analytics ID vs feature ID
  Architecture enhancement to support AI based Positioning
Part A: Architecture enhancement to support 5G Core Intelligence (see joint paper S2-2306503 from China Mobile/vivo for details)
Please see joint SID S2-2306462 from China Mobile/vivo for new study on AIML for 5GS Service to enable 5GC and Air interface Intelligence

## Slide 21
Thanks!

## Slide 22
Two side CSI and some other RAN background….
Training Type 1 for two-sided model：Joint training of the two-sided model at a single side/entity, e.g., UE-sided or Network-sided.
Model delivery of UE-sided or network-sided model is needed.
Train the two-sided model
NW side
UE side
Storage
Joint Inference
Model delivery of UE sided model
Network first
Train the two-sided model
NW side
UE side
Storage
Joint Inference
Model delivery of network sided model
UE first

## Slide 23
Two side CSI and some other RAN background….
Training Type 2 for two-sided model：Joint training of the two-sided model at network side and UE side, respectively.
The FP (front-propagating) results and BP(back-propagating) information need to be exchanged between network side and UE side.
Generates the FP results of Encoder (PMI)
NW side
UE side
Generates the FP results of Decoder (reconstructed CSI)
The FP results (PMI)
One FP/BP Loop
Trains the Decoder and generates the BP information (e.g., gradients)
Trains the Encoder
The BP information (e.g., gradients)

## Slide 24
Two side CSI and some other RAN background….
Training Type for two-sided model：Separate training at network side and UE side, where the UE-side CSI generation part and the network-side CSI reconstruction part are trained by UE side and network side, respectively.
In step 3, transmitting exchange dataset with large number of samples will be needed.
Take UE first as example

## Slide 25
How to support UE data collection in case of NAT
    vivo’s view: Study whether and how to support UE data collection in case NAT is deployed.
UE 1 private IP address:
192.168.1.1
UE 2 private IP address:
192.168.1.2
RAN
UPF
NAT deployed
AF
SMF
UE 1 (ID) | 192.168.1.1
UE 2 (ID) | 192.168.1.2
NWDAF
NATed address: 110.124.8.1
UE ID to UE IP mapping from 5GC
UE IP address seen from Application layer
UE 1 | 110.124.8.1 port: 874
UE 2 | 110.124.8.1 port: 875
① NWDAF subscribes AF to data collection with UE ID
② AF obtains the UE private IP address associated with the UE ID from SMF
AF still can’t identify which UE to collect data by private UE IP address
×
    Issues clarification: The AF can only obtain the private UE IP address from SMF and establish the mapping table between UE ID and the private UE IP address. But the AF can’t use the private address to identify the target UE to data collection.