## Slide 1: Proposed enhancements in handling of radio capabilities
Qualcomm Incorporated
S2-2307190

## Slide 2: Issues to be addressed
Issue #1: Disabling RATs the UE radio capability does not need to support due to Ues subscription
  It is possible that certain UEs due to their subscription are only allowed in 5GS and not in LTE/EPS e.g. "CAG only" UEs, UEs with no NTN subscription etc.
  Nevertheless since the UE (modem) has radio capability to access LTE/EPS in certain cases it will attempt to do idle mode reselection to LTE and as a result be rejected.
  This procedure wastes battery power for the UE and network resources for the network. It is therefore proposed that the network indicates to the UE that due to its subscription it needs to disable its radio capabilities for specific RATs and as a result the UE does not need to perform inter-RAT measurements and mobility.

## Slide 3: Issues to be addressed
Issue #2: Exposure of support/no support of specific UE radio capability by NEF
  In certain deployments the viability of a particular application and the actions that an Application Function (AF) will take depend on the “alignment” of radio features deployed in network and UE.
  Network (PLMN and SNPN) may deploy a sub-set of the available radio features. UE operating in such network may or may not support the radio capabilities to operate such features.
  How an AF (internal or external to the network) know in advance before initiating a session for a particular application that there is “alignment” of radio features that would be required in order to support this application or the specific function is required.
  Examples use cases: Timing resiliency service (delay compensation), XR (RedCap vs full scope NR), QoS sustainability

## Slide 4: Issues to be addressed
Issue #3: Transfer of radio capability container from AMF to MME (and vice versa)
  When UE moves frequently between EPS and 5GS (in idle mode) a new retrieval of radio capability is needed from target system when the UE moves to connected mode.
  This procedure would be optimised if like inside 5GS there is transfer of the radio capability container from AMF to MME and vice versa in similar fashion that is transferred between AMFs inside 5GS.

## Slide 5: Objectives
WT#1: Identify how to prevent a UE to access a specific RAT/system in which it does not have subscription and therefore will be rejected. How to indicate to UE to disable certain radio capabilities in order to avoid attempting to register to this RAT/system and be rejected. How to define exceptions for emergency services.
WT#2: How an AF (internal or external to the network) know in advance before initiating a session for a particular application that there is “alignment” of radio features that would be required in order to support this application or the specific function is required.
WT#3: How to transfer the radio capability container or UE Radio Capability ID between AMF and MME (and vice versa) in order to avoid retrieval of radio capabilities from the UE (if possible) from the target system.
The work will be based on following deployment options: 1) RACS support in UE and NW, 2) No RACS in UE, but support of RACS in NW, 3) No RACS support.