## Slide 1: Discussion on LCS user plane connection binding to UE
Qualcomm Incorporated
S2-2404874

## Slide 2: Background information
What CT1 has defined for location service over user plane
  UPP-CM: Control plane procedure between UE and LMF for user plane connection mgmt.
  LCS-UPP: User plane procedure between UE and LMF for LPP/LCS-SS message exchange
Providing user plane information (to establish user plane connection) via control plane
= UPP-CM(connection mgmt.) procedure defined in TS 24.572
Establishment of user plane connection using TLS
LPP message/LCS-SS message exchange over the user plane connection
= LCS-UPP procedures defined in TS 24.572
to
TS 23.273 Section 6.18

## Slide 3: Issue described in CT1 LS (S2-2403871/C1-241722)
Issue 1) After the TLS connection is established, the UE and the LMF initiate LPP or LCS-SS procedure. For the LMF-initiated case, given that multiple UEs are served by the LMF and multiple TLS connections are active, the LMF needs to determine a TLS connection for the target UE. However, it has not been specified how to link the association between the TLS connection and the UE, e.g., how the LMF knows which TLS connection is for the UE who has received the UPP-CM command message. If the TLS connection can be linked to the ‘wrong UE’ then there could be a risk of location related data from one UE which is sent to another UE.
 How to link the user plane connection with the control plane signaling is needed.
Issue 2) Once the binding of the TLS connection to the UE is done, if there is a new LCS service request (e.g., MT-LR) for the same UE, the AMF invokes Nlmf_location_determinelocation service operation to the LMF. However, it has not been specified how the LMF associates the LCS service request to the TLS connection of the UE. In this case, the LMF cannot determine which TLS connection can be used for the LCS service request. Therefore, the LMF cannot reuse the TLS connection of this UE for subsequent LCS service request(s).
 As AMF does not include any UE ID in Nlmf_location_determinelocation API, the LMF cannot know whether the target UE is the one having TLS connection.

## Slide 4: Proposal for issue 1)
Allocating a connection ID (like a token) during UPP-CM and use the connection ID for LCS-UP binding
UE
LMF
User plane connection establishment command message
(User plane information, LCS-UP Connection ID)
TLS session establishment procedure
LCS-UP connection binding request
LCS-UP session binding response
(LCS-UP connection ID)
User plane connection complete message
(LCS-UP connection ID)
LCS-UP connection ID is valid until LCS-UP connection release procedure is performed
- During lifetime of LCS-UP connection, TLS session may be released/re-established. At every TLS session est., the UE performs binding procedure.
1. When LMF performs user plane connection est. procedure, LMF allocates LCS-UP connection ID to the UE, and stores the association between the LCS-UP connection ID and UE IE (SUPI or GPSI)
2. UE stores the received LCS-UP connection ID and uses the ID for binding procedure over user plane after TLS session establishment.
4. UE sends the complete message to the LMF over the control plane, and LMF finalizes the binding of user plane connection.
3. LMF acknowledges the binding request. If the ID is not available in the LMF, it responds an error and the user plane connection establishment procedure is aborted.

## Slide 5: Alternative solutions for issue 1)
Alt. 1) Indicating TLS session ID in the UPP-CM complete message
  The UE sends the TLS session ID to the LMF (over the control plane)
  Evaluation: Using TLS session ID does not guarantee the identification of the UE for the TLS connection, as it can be re-issued at any time and another TLS client can use the same value accidentally
Alt. 2) Indicating IP address of the UE in the UPP-CM complete message
  The UE sends the IP address of the UE for the TLS connection to the LMF (over the control plane), then the LMF associates the received IP address to the UE
  Evaluation: If NAT is deployed, it does not work. IP address verification can be an issue.
Alt. 3) allocating a TCP port number to the UE and identifying the UE over the TLS connection using the port
  Given well-known port values registered in IANA, the remainder of the ports from 49152 to 65535 can be used dynamically by applications. LMF assigns one of port value to the UE during UPP-CM, and the UE uses the port when establishing TLS connection
  Evaluation: The number of available port number is limited. The UE shall use the port number for a lifetime of LCS user plane for subsequent LCS services. (TLS can be released/re-established during the lifetime). Critical security issue: Someone easily picks any port value and pretending it is the UE.
 None of above alternative works securely

## Slide 6: Proposal for issue 2)
For LMF-initiated User Plane Connection establishment, in Nlmf_Location_UPNotify, the LMF indicates the connection ID to the AMF. The AMF stores the connection ID and includes the ID for further LCS service until the UP connection is released.
For UE-initiated User Plane connection establishment, in Nlmf_Location_UPConfig Response, the LMF indicates the connection ID to the AMF. The AMF stores the connection ID and includes the ID for further LCS service until the UP connection is released.

## Slide 7: Conclusion
For issue 1)
  LMF assigns a connection ID to UE and provide to the UE (along with the user plane information)
  UE sends binding request (including the connection ID) to LMF over the TLS connection
  LMF responds to UE the completion of user plane connection binding over the control plane
For issue 2)
  LMF provides the connection ID to the AMF in Nlmf_location_UPNotify or Nlmf_location_UPConfig response
  AMF includes the connection ID received from the LMF for further LCS request (Nlmf service operation, Namf_Communication_N1MessageNotify) until the user plane connection is released
>> S2-2404857 for TS 23.273 and S2-2404865 for TS 23.502 were submitted.

## Slide 8: Further security consideration
The LCS-UP connection ID is allocated by the LMF, which should prevent any overlap of LCS-UP connection IDs across different UEs. However, a rogue UE could potentially generate a random value that coincidentally matches the LCS-UP connection ID of another UE, so that the rogue UE uses the matched value to associate its TLS connection with the LMF. There is also a possibility that attackers could intercept the contents of a UPP-CM message and extract the value of the LCS-UP connection ID, in particular if the NAS connection is not confidentiality protected.
The situations mentioned above can be mitigated but not fully prevented with a few procedural measures. For instance, if the LMF detects a potential overlap of LCS-UP connection IDs (such as when a TLS connection for a particular LCS-UP connection ID is active and another message arrives from a different UE using the same LCS-UP connection ID), the LMF can reject the latter one. For the suspected risk of LCS-UP connection ID collision, the LMF can reassign the LCS-UP connection ID at any time. For the UE side, the UE sends the allocated LCS-UP connection ID over LCS-UPP right after the TLS connection establishment, so the time of possible snooping will be limited.
 It is proposed to specify such detailed management in stage-3.