## Slide 1: Results of drafting session on Contribution summary and way forward proposal for LCS user plane connection binding to the UE
CATT
SA WG2 Meeting #162 S2-2405261
April 15 – 19, 2024

## Slide 2: Contents
Background
Contribution Summary
Way forward proposal

## Slide 3: Background
LS on LCS user plane connection binding to the UE(S2-2403871/C1-241722) is received in SA2#162 meeting, the questions include；
  Q1: After the TLS connection is established, the UE and the LMF initiate LPP or LCS-SS procedure. For the LMF-initiated case, given that multiple UEs are served by the LMF and multiple TLS connections are active, the LMF needs to determine a TLS connection for the target UE. However, it has not been specified how to link the association between the TLS connection and the UE, e.g., how the LMF knows which TLS connection is for the UE who has received the UPP-CM command message. If the TLS connection can be linked to the ‘wrong UE’ then there could be a risk of location related data from one UE which is sent to another UE.
  Q2: Once the binding of the TLS connection to the UE is done, if there is a new LCS service request (e.g., MT-LR) for the same UE, the AMF invokes Nlmf_location_determinelocation service operation to the LMF. However, it has not been specified how the LMF associates the LCS service request to the TLS connection of the UE. In this case, the LMF cannot determine which TLS connection can be used for the LCS service request. Therefore, the LMF cannot reuse the TLS connection of this UE for subsequent LCS service request(s).
Contributions on the issue in SA2#162 meeting: 7 draft LS replies, 8 CRs and 4 DPs are contributed

## Slide 4: Contribution Summary
Tdoc number | Company | Summary | 
 |  | Mechanism to solve Q1 | Mechanism to solve Q2
S2-2404044(LS OUT) S2-2404045(CR) | vivo | The LMF allocates a LCS-UP connection ID for the user plane connection in order to associate one user plane connection with one UE. | The LCS-UP connection ID is stored in the AMF as part of LCS-UP connection context. When receiving the subsequent location request for the UE, the AMF may send the LCS-UP connection ID to the LMF.
S2-2404131(LS OUT) S2-2404132(CR) | Xiaomi EV Technology | Option 1: LMF reuses the existing AF specific UE ID retrieval procedure to retrieve the UE ID (i.e., SUPI or GPSI) from NEF. Option 2: UE includes the IP address in the user plane positioning ACK message. Option 3: LMF allocates a connection ID and sends the ID to UE. UE adds connection ID in the control plane. | Not described
S2-2404166(LS OUT) S2-2404167(CR) | Huawei, HiSilicon | A temporary LCS UP UE ID is assigned by LMF to associate the user plane connection with the GPSI/SUPI provided by AMF | If UE supports user plane positioning, the AMF should include the GPSI/SUPI in the location request to LMF
S2-2404664(LS OUT) S2-2404665(CR) | OPPO | UE includes UE ID and UE IP address in the User Plane Positioning Acknowledge. Based on UE provided information, LMF can associate the user plane connection with UE. | The AMF will include the UE ID in the subsequent positioning request to LMF
S2-2404713(LS OUT) S2-2404712(CR) | CATT | A binding ID is assigned by LMF to associate the user plane connection with the GPSI/SUPI provided by AMF | If UE supports user plane positioning, the AMF should include the GPSI/SUPI in the location request to LMF
S2-2404773(LS OUT) S2-2404774(CR) | ZTE | The LMF always assigns a LCS-UP session id and sends it to UE. After UE the user plane connection is established, the UE sends the LCS-UP session id to the LMF via the user plane so that the LMF can bind the UP and the UE | Based on the answer#2 in the draft LS, the AMF should include the GPSI/SUPI in the location request to LMF
S2-2404868(LS OUT) S2-2404857(CR) S2-2404865(CR) | Qualcomm Incorporated | The LMF allocates a LCS-UP connection ID for the user plane connection in order to associate one user plane connection with one UE. | The LCS-UP connection ID is stored in the AMF as part of LCS-UP connection context. When receiving the subsequent location request for the UE, the AMF may send the LCS-UP connection ID to the LMF.

## Slide 5: Way forward proposal (For Question 1)
Summary and supporting company of mechanism to solve Q1
  Alternative#1 : LMF allocates a new ID and includes the new ID in the User Plane Information to UE. After the user plane connection is established, the UE sends the new ID via the user plane connection. Based on the received ID, the LMF can associate a user plane connection with the new ID
    Supporting company: 6 (vivo, Xiaomi-option3, Huawei, CATT, ZTE, Qualcomm)
  Alternative#2: UE includes UE ID and UE IP address in the User Plane Positioning Acknowledge. Based on UE provided information, LMF can associate the user plane connection with UE
    Supporting company: 1 (OPPO)
  Alternative#3: LMF reuses the existing AF specific UE ID retrieval procedure to retrieve the UE ID (i.e., SUPI or GPSI) from NEF
    Supporting company: 1 (Xiaomi-option1)
  Alternative#4: UE includes the IP address in the user plane positioning ACK message
    Supporting company: 1 (Xiaomi-option2)
  Alternative#5: no further enhancements needed for SA2, as LMF can derive LCS UPP connection corresponding to UE ID based on LCS session ID and correlation ID association.
    Supporting company: 1 (Xiaomi-option4)
Way forward proposal: Alternative#1 : LMF allocates an ID (e.g. LCS UP connection ID), to be used to associate with the LCS UP connection ( and configuration for the connection to be established ) for the UE .

## Slide 6: Way forward proposal (For Question Q2)
Summary and supporting company of mechanism to solve Q2
  Alternative#1 : LMF stores the mapping of <new ID, user plane connection information> and provides the new ID to AMF. AMF stores the new ID and includes the new ID in the subsequent Nlmf_Location_DetermineLocation request. Based on the new ID, the LMF knows the related user plane connection.
    Supporting company: 2 (vivo, Qualcomm)
  Alternative#2: if UE supports user plane positioning capability, the AMF shall include SUPI/GPSI in the subsequent Nlmf_Location_DetermineLocation request. LMF stores the mapping of <SUPI/GPSI, user plane connection>. Based on the SUPI/GPSI, the LMF knows the related user plane connection.
    Supporting company: 4 (CATT, Huawei, ZTE, OPPO)
  Alternative#3: no further enhancements needed for SA2, as LMF can derive LCS UPP connection corresponding to UE ID based on LCS session ID and correlation ID association.
    Supporting company: 1 (Xiaomi-option4)
Way forward proposal: Alternative#2: e.g. if UE supports user plane positioning capability, the AMF shall includes the same UE ID (i.e. SUPI or GPSI, existing parameters) in the subsequent Nlmf_Location_DetermineLocation request, LMF does the correlations of <SUPI or GPSI, LCS UP connection ID >.

## Slide 7: Way forward proposal (Baseline CR and LS reply)
Proposal of baseline for further discussion
  Draft LS reply: S2-2404713
  CR: S2-2404712