## Slide 1: Centralized and Distributed SON for multi-vendor RAN
S5-131066
Supporting presentation for s5-130938
Source: Cisco

## Slide 2: 3GPP Management Architecture Centralized SON and Distributed SON
RAN vendors normally supply NEs (RNCs, NodeBs, eNodeBs etc.) together with the Element Manager (EM)
The only really standardized interface is the EM north bound (Type 2) interface; typically conformant with 32 an 28 series of 3GPP standard
Supplied by RAN vendor B
Supplied by RAN vendor A
Centralized NM-Based SON (“cSON”)
LTE Distributed SON (“dSON”) functions running on eNBs; using X2 interface when needed
Network element: NB, RNC,
eNB, MME, …
Element Manager
Itf-N, Type 2 Interface
Northbound interface of the EM
Network Manager

## Slide 3: cSON & dSON cooperation
cSON is a NM-based entity that collects information (e.g. RAN measurements) and controls the Radio parameters over Itf-N interface
The proposed approach includes a centralized entity with combined functionality of NM-based SON (Radio control) and SON Monitoring and Management Function (32.500, 32.521)
The concept: dSON instances are supervised and complemented by centralized entity which includes also some SON capabilities
  It’s called in this presentation just “cSON”

## Slide 4: Problems of dSON that can be alleviated by supervision of cSON
Limited network visibility: a single eNodeB, possibly with close neighborhood. Then:
  “Chain reaction” can happen: change in eNB #1 triggers change in eNB#2 which triggers change in eNB#3 etc.
  Not necessarily the changes applied by local dSON entities result in convergence of the whole network domain
  If converging, it is not necessarily to the optimal state of the whole network domain
Typically dSON functions are using only a subset of possible measurements and controlled parameters therefore not necessarily reach optimum
  For example, ICIC does not necessarily change total transmit power, power allocation parameters in the DL, tilt angle
Lack of interoperability over X2 interface between dSON functions from different vendors
  Basic reason: 3GPP specified only inter-eNB signaling, but did not specify algorithms

## Slide 5: MV MLB case study (1)

## Slide 6: MV MLB case study (2)

## Slide 7: MV MLB case study (3)

## Slide 8: Solution: dSON supervised by cSON
dSON functions should have sufficient set of OAM parameters  “Mode B” in the contribution
  To configure dSON
  To monitor dSON operations
  To intervene in case when a problem (e.g. oscillations) is identified: reconfigure dSON or even take over some dSON operations until the problem is resolved
    The latter may require extension of the set of OAM parameters set used by cSON  “Mode A” in the contribution
This approach allows alleviation of dSON problems by using capabilities of cSON:
  Visibility of wide network domain
  Ability of simultaneous operations with eNodeBs (dSON functions included) that are supplied by different vendors