## Slide 1: 3GPP SA5 status update on NFV
Christian Toche, 3GPP SA5 chairman
November 2014

## Slide 2: Introduction
This presentation provides the current status of 3GPP SA5 work on NFV.
The main objective is to indicate the areas where 3GPP SA5 could contribute to the standardization of NFV management and operations aspects.
This presentation describes:
  Objectives of 3GPP SA5 study
  Current status of the SA5 study
  Mixed network management architecture
  Areas for involvement of SA5 for 3GPP-defined networks

## Slide 3: Objectives of 3GPP SA5 study
The objectives of this study are:
  Study the use cases and concepts for the network management of virtualized networks, taking into account the relevant use cases from ETSI NFV ISG.
  Analyse and classify the scenarios when all or some instances of 3GPP-defined network elements in a subsystem/domain are virtualized (i.e. respectively fully virtualized networks and mixed networks)
  Identify the requirements for potential solutions to the scenarios above. Study whether or not a single management system for mixed networks is required.
  Identify the potential impacts on the existing 3GPP Management reference model.
  Analyse the existing 3GPP Management reference model, interfaces, protocols and procedures to determine what can be re-used, adapted or extended, and whether new IRPs are needed.
  Propose enhancements or extensions to the 3GPP Management reference model, if an impact is foreseen. If needed, solution(s) for a single management system for mixed networks should be studied.
  Provide recommendations for the normative work, based on the result of the analyses and the potentially identified impacts, enhancements or extensions.
  SA5 will take in account the work done by ETSI NFV ISG and cooperate with ETSI NFV ISG as necessary.
  Study Item Description: http://www.3gpp.org/ftp/TSG_SA/TSG_SA/TSGS_64/Docs/SP-140398.zip

## Slide 4: Current status of the SA5 study
The following content is already included in the draft TR 32.842
  Management use cases
    Instantiation of Core Network Service
    VNF expansion
    Termination of Core VNF instance
    Fault management
  Potential solutions
    Management architecture
    Management architecture diagram (work in progress)
Target for delivery of the TR 32.842 is June 2015
  Latest version of the draft TR (October 2014, v0.2.0): http://www.3gpp.org/ftp/TSG_SA/WG5_TM/TSGS5_97/Docs/S5-145358.zip

## Slide 5
Mixed network management architecture
Figure 7.1-1 from draft TR 32.842 (work in progress)

## Slide 6: Areas for involvement of SA5 for 3GPP-defined networks
Interfaces |  | Os-Ma-nfvo (OSS/BSS/NM - NFVO) | Ve-Vnfm-em (EM-VNFM) | Ve-Vnfm-vnf (VNF-VNFM) | Or-Vnfm (NFVO-VNFM) | Vi-Vnfm (VIM-VNFM) | Or-Vi (NFVO-VIM) | Itf-N (OSS/BSS/NM - EM)
Functions |  |  |  |  |  |  |  | 
Lifecycle management | Network service1 | 3GPP SA5 |  |  |  |  |  | 3GPP SA5
 | VNF2 | 3GPP SA5 | 3GPP SA5 | 3GPP SA5 | 3GPP SA5 |  |  | 3GPP SA5
FCAPS | Network services3 | 3GPP SA5 |  |  |  |  |  | 3GPP SA5
 | VNF4 | 3GPP SA5 | 3GPP SA5 | 3GPP SA5 | 3GPP SA5 |  |  | 3GPP SA5
NFVI management5 |  | 3GPP SA5 |  |  |  |  |  | 3GPP SA5
Policy administration6 |  | 3GPP SA5 |  |  | 3GPP SA5 |  | 3GPP SA5 | 3GPP SA5
Architecture7 |  | 3GPP SA5 |  |  |  |  |  | 
E2E management procedures (mobile network) 8 |  | 3GPP SA5 |  |  |  |  |  | 
(work in progress)

## Slide 7: Notes
References are corresponding to ETSI NFV MANO GS:
1: "Life cycle management — Network Service": 7.1.1, 7.1.2, 7.1.3.
2: "Life cycle management — VNF" : 7.2.1 to 7.2.5.
3: "FCAPS — Network Service": 7.1.4, 7.1.5, 7.5.
4: "FCAPS — VNF": 7.2.6 to 7.2.8.
5: "NFVI management": 7.3, 7.6 to 7.8.
6: "Policy administration": 7.4.
7: "Architecture": 5.
8: "E2E management procedures (mobile network)" means the end-to-end procedures for NFV management (of mobile networks), including the interactions among all the relevant management entities (OSS/BSS/NM, EM, NFVO, VNFM, VIM) and VNF/PNF, and if needed it will include the interactions between VNFs/PNFs too.

## Slide 8: Thank you !