## Slide 1: Constrained Devices
Peter Sanders
one2many

## Slide 2: Proposal
The way the MSGin5G service supports constrained devices is unnecessarily complicated.
  It is complicated because
    We combined different UE types into a single box in the diagram
    We gave 3 names to the single UE-in-the-middle depending on which capabilities it exposes at any moment
The proposal is
  To separate the constrained device into individual UEs in the diagram
  To allocate a UE-in-the-middle for the constrained devices, give it one name and all capabilities it exposes to constrained UEs are optional, but we define only a single device for it.

## Slide 3: Modified architecture diagram
MUE-2a
Application Client
MUE-2b
Application Client
MSGin5G Client
MUE-1b
Application Client
MSGin5G Client
MUE-1a
Application Client
MSGin5G Client
3GPP network
MSGin5G Server
MSGin5G-6
MSGin5G-5
MSGin5G-1
MSGin5G-5
MSGin5G-5
UE-2a is an AC, like the AC in UE-1a and both ACs are served by the MSGin5G Client in UE-1a
  UE-1a is our regular MSGin5G UE
  No need to define an AC as constrained
UE-2b is a constrained device (which cannot connect directly via the 3GPP network)
UE-1b is a Proxy UE
  Supports bulk stuff
No need for a GW UE or Relay UE

## Slide 4: UE roles
UE-1a is a regular MSGin5G UE with ACs on UE-1a itself and on UE-2a
  It is a deployment option to locate an AC on the same UE as the UE that has the MSGin5G Client or on a different UE. In both cases the reference point between MSGin5G Client and ACs is MSGin5G-5.
UE-2b is a constrained UE
  Definition: A Constrained UE cannot communicate via the 3GPP network with the MSGin5G Server
    An AC cannot communicate with the MSGin5G Server at all, so no need to distinguish between ACs that are constrained devices and ACs that are not constrained devices (i.e. UE-2a is not a constrained device under the definition)
UE-1b supports relaying messages between all UE-2b UEs and the MSGin5G Server and UE-1b optionally supports bulk-configuration and bulk-registration on behalf of all UE-2b UEs
  Since UE-2b does more than relaying, we could call UE2b a Proxy UE