## Slide 1: Clarification on ACR scenarios
Yajie
Huawei, Hisilicon

## Slide 2
EES#1
EES#2
EAS#1
There would be two issues using current ACR scenario definition
Reason 1:
    There would be a mismatch when OAM determine the which EES need to be associated with the certain EAS only considering the service continuity support (i.e. ACR scenario) of the EAS/EES
Assumption:
  The EES#1, EES#2, EAS#1 all support “S-EAS decided ACR scenario”
  Case#1: EAS#1 without the ACR Detection capability; EES#1 with the ACR Detection capability
  Case#2: EAS#1 without the ACR Detection capability; EES#2 without the ACR Detection capability
  Issue:
  For Case#2: the ACR will never be triggered when only support “S-EAS decided ACR scenario” is used
With ACR Detection capability
Without ACR Detection capability
Without ACR Detection capability
EAS#1
Without ACR Detection capability
Case #1
Case #2
Case#1: the ACR can be triggered when only support “S-EAS decided ACR scenario” is used
Case#2: the ACR can not be triggered when only support “S-EAS decided ACR scenario” is used

## Slide 3
The EEC, EES or EAS detect ACR are OPTIONAL
There is no clear description which entity shall detect the ACR event in TS, take S-EAS decided ACR as an example
  There are four cases of detection entity combination in the following table, there is case that both EAS and EES don’t detect the ACR event
Issue: no entity will really perform the ACR detection
  If the EAS only support S-EAS decided ACR but rely on EES to detect, but EAS can still announce the EAS support the S-EAS decided ACR
  Similarly, the EES only support S-EAS decided ACR but rely on EAS to detect, but EES can still announce the EAS support the S-EAS decided ACR
  Then S-EAS decided ACR is selected as the only one ACR scenario the error will happens: no entity will really perform the ACR detection
 | EAS detect | EAS not detect
EES detect | ACR can be triggered | ACR can be triggered
EES not detect | ACR can be triggered | ACR can NOT be triggered
Table: detection entity combination of S-EAS decided ACR

## Slide 4
There would be two issues using current ACR scenario definition
Reason 2:
  For the “S-EES executed ACR”, there is no negotiation between EEC and EES about the ACR Detection capability of EEC and EES
  Thus, the EEC and S-EES may not detect the ACR event
Assumption:
  The EES#1, EEC all support “S-EES executed ACR”
  EEC and EES are without the ACR Detection capability;
  However, the EEC and EES are not be aware of the ACR Detection capability of each other, thus this error will not be discovered
  Issue:
    None of EEC and S-EES will detect the ACR event;
    And this error will not be discovered
    Then the ACR will never be triggered in above case.
Figure 8.8.2.5-1: S-EES executed ACR

## Slide 5
How to solve the issue?
Enhance the ACR scenario name with the ACR detection entity (Take the “S-EAS decided ACR scenario” as an example)
  Then the ACR scenario should be defined in a way that both reflect the detection and decide capability
S-EAS decided ACR
S-EAS decided ACR
with S-EAS detection
S-EAS decided ACR
with S-EES detection

## Slide 6
Way Forward (Huawei)
Split current ACR scenario into smaller granularity
Detection capability and Determination capability need to be reflected in ACR scenario.

## Slide 7
Thanks