## Slide 1: Discussion Paper on Policies in Application Layer AI/ML Services
Igor Pastushok
Ericsson

## Slide 2: Agenda
Background
  TR for FS_AIMLAPP
  Policy in SEALDD and NSCALE
Discovery/Selection/Re-selection in AIMLApp
AIML member selection policies
Proposed solution
Summary

## Slide 3: Background – FS_AIMLAPP
FS_AIMLAPP - TR 23.700-82 v0.2.0
  5.7 - Key issue 7: Discovery or Support of Member Selection and Maintenance for Application Layer AIML Service
    Mentions the AI/ML Services need have information about conditions when AI/ML entities (e.g., VAL server, AI/ML Enablement Client, AI/ML Enablement Server) are available or not available to participate in the AI/ML operations (e.g., ML model training).
    Indicate the need to study the solutions on how to select and maintain the member for AI/ML Application layer Services.

## Slide 4: Background – FS_AIMLAPP
FS_AIMLAPP - TR 23.700-82 v0.2.0
  8.6 - Solution #6 on AIML enablement client selection
  8.7 - Solution #7 on AIML enablement client discovery
  8.8 - Solution #8 on AIML enablement client registration
    Mentions the procedure and IEs for AIML client registration, discovery, and selection, and member selection policy.
Open issues:
  - It is FFS how the request parameters are used in relationship to other member selection policy provisioned to the AIML enabler layer.
  - Whether the IEs are included in the AIML member selection policy is FFS.

## Slide 5: Background –Policy in SEALDD
Figure 1: SEALDD policy configuration
Figure 2: SEALDD policy configuration update
SEALDD - TS 23.433
  Clause 9.9.2.1: A SEALDD service policy (i.e., the necessary SEALDD layer actions for meeting the service policy requirements) has been configured in SEALDD server and shared with the SEALDD client.
  Clause 9.10: Mentions procedures and information flows of SEALDD policy configuration, update, and delete.
Figure 3: SEALDD policy configuration delete

## Slide 6: Background –Policy in SEALDD
SEALDD - TS 23.433
  Clause 9.10.3.1: SEALDD policy configuration request
Information element | Status | Description
Application traffic identifiers | M | Identify of the application traffic (e.g. VAL server ID, VAL service ID)
VAL UE identity | O | Identifier of the VAL UE for which SEALDD policy applies
SEALDD policy | M | The SEALDD policy associated with application traffic identifiers, VAL UE identify
> Quality guarantee policy | O (See NOTE 1) | Indicates the action to be performed when the measurement event (e.g. measurement threshold) occurs, in order to meet the quality guarantee.
> Bandwidth control policy | O (See NOTE 2) | The bandwidth control policy from VAL server, e.g. re-allocating the bandwidth limit between different VAL users, including UL/DL
NOTE 1: This IE is used for the SEALDD enabled transmission quality guarantee, as specified in clause 9.9. NOTE 2: This IE is used for the SEALDD enabled bandwidth control, as specified in clause 9.8. |  | 
Table 1: SEALDD policy configuration request

## Slide 7: Background –Application Layer Policy
Application layer Policy has the best practice definition in SA6 and implemented in multiple TSs.
The policy consists of identifier, action, and the action related condition.

## Slide 8: Discovery/Selection/Re-selection in AIMLApp
During the discussion, the following terms appear:
  Discovery - the VAL server requests a list of AIML Enablement Clients that complies with the provided filtering criteria from AIML Enablement Server;
  Selection – the VAL server provides the request to the AIML Enablement Server to select the list of AIML clients or ask the AIML Enablement Server select X AIML Enablement Clients for the operation based on provisioned policies. The selection procedure implies that AIML Enablement Server starts monitoring the condition of the selected AIML Enablement Clients and invokes the re-selection procedure if AIML Enablement Client does not comply with the provisioned policies.
  Re-selection – a process of including/excluding/replacing of the selected AIML Enablement Clients based on monitoring output and provisioned selection policies.

## Slide 9: Discovery/Selection/Re-selection in AIMLApp and Policies
During the discussion, the following terms appear:
  Discovery – discovery procedure can utilize the policies conditions to filter the AIML Enablement Clients.
  Selection – selection procedure can utilize the AIML policies to select X AIML Enablement Clients for the VAL server.
  Re-selection – re-selection procedure require AIML policies in order to including/excluding/replacing of the selected AIML Enablement Clients.
Main goal of the AIML member selection policies: support and enable continuous and secured AIML process.

## Slide 10: AIMLAPP Member Selection Policies
AI/ML member selection policies cover selection and re-selection procedures.
Use-cases:
  Given: The critical vulnerability is found in OS X version of AIML Enablement Clients. Action: The VAL server can add or update the selection policies to exclude all AIML members with the given OS X version. Result: the AIML Enablement Server initiates re-selection procedure and excluding/replacing all AIML members with the given OS X version.
  Given: The AIML Enablement Client was selected as a member for participate in the AIML operation(s) and experiences congestion in the network. Action: The AIML Enablement Server observes the congestion state of the AIML Enablement Client. The AIML Enablement Server configures the network QoS for the AIML Enablement Client (based on provided member selection policies by the VAL server) in order to keep the AIML Enablement Client as selected member for the AI/ML operation(s). If failed, the AIML Enablement Server initiates the re-selection procedure. Result: AIML Enablement Server maintains the continuity of the AIML process via generating or updating 5G network policies based on the provided AIML member selection policies.
Table 4: AI/ML member selection policies and format
Information element | Status | Description
Requester Identity | M (NOTE 1) | The identity of the VAL server performing the request.
VAL service ID | M | Identify the VAL service ID.
List of AI/ML traffic QoS policies | O | Provides the list of AI/ML traffic QoS policies, e.g., AI/ML traffic QoS parameter(s) (e.g., bitrate, jitter, latency, PLR, connection sustainability) with the corresponding threshold(s) and threshold matching direction(s) (e.g., above, below or crossed). (NOTE 3)
List of AI/ML compute capability policies | O | Provides the list of the AI/ML compute capability policies, e.g., the OS, OS version, hardware capabilities, software capabilities. (NOTE 3)
List of AI/ML member mobility policies | O | Provides the list of mobility policies for the AI/ML member, e.g., low mobility, high mobility, stationary. (NOTE 3)
List of AI/ML member participation configurations | O | Provides the list of the AI/ML member participation configurations as defined in table 8.10.3.1-1. (NOTE 2) (NOTE 3)
NOTE 1: This information element shall not be updated in the AI/ML member participation configurations management request. NOTE 2: The member participation configurations represent the requestor conditions for the member selection based on the configurations provided in table 8.10.3.1-1 to be selected to participate into the AI/ML operations. NOTE 3 The policy format is provided in table 8.A.3.1-2. |  | 
Information element | Status | Description
Policy ID | M | The identity of the policy.
Action | M | Represents the policy action, e.g., include member, exclude member.
List of the conditions | M | Provides the list of conditions, e.g., the threshold(s) with the associated threshold matching direction(s) or the set of value(s).

## Slide 11: Proposed Solution
Following changes to clause 5.7 in FS_AIMLAPP TR 23.700-82
  Add the following study aspects on AI/ML policies and configurations provisioning, management, and enforcement:
    How to support the AI/ML member selection policies.
    How to support the AI/ML member participation configurations.
    How to support the AI/ML policies for maintaining the AI/ML process.
    How to utilize the AI/ML policies and configurations in the AI/ML Application layer Services.
The proposed changes complete the key issue mentioned in the clause 5.7 and are in line with the solutions mentioned in the clauses 8.6, 8.7, and 8.8 TR 23.700-82.

## Slide 12: Summary
This discussion paper proposes a solution to
  Complete the Key Issue in clause 5.7 of TR 23.700-82 v0.2.0
  Align with the solutions in clauses 8.6, 8.7, and 8.8 of TR 23.700-82 v0.2.0
  It is proposed to discuss and agree on pCR S6-240196 that provides implementation of the solution described in the discussion paper.

## Slide 13: BACKSLIDES

## Slide 14: Background –Policy in NSCALE
NSCALE – TS 23.435
  Clause 3.1: VAL server policy: Network slice management Policy which can be seen as application function policy from VAL Provider/ slice customer/ASP, abstracted based on the slice usage pattern of application, consisting of trigger event and expected action.
  Clause 9.5.2: Mentions the procedures and information flows of VAL server policy provisioning, Update, and Delete.
Figure 4: VAL server policy provisioning
Figure 5: VAL server policy update
Figure 6: VAL server policy delete

## Slide 15: Background –Policy in NSCALE
NSCALE – TS 23.435
  Clause 9.5.3.2: VAL server policy provisioning request, and policy profile
Information element | Status | Description
Requestor Identifier | M | Unique identifier of the requestor (i.e. VAL server ID).
Security credentials | M | Security credentials resulting from a successful authorization.
Network slice related Identifier(s) | O | Identifier of the network slice.
Requested DNN | O | Indication of the DNN which is requested.
Indicator of policy harmonization | O | Indicating whether the policy harmonization is requested.
Policy | O | The policy profile is defined in Table 9.5.3.2-2. The supported VAL server policies are listed in Table 9.5.3.2-3 to Table 9.5.3.2-5.
Default policy indication | O | Indicates the policy in the request to mark as a default policy for slices provisioned without any policy.
Information element | Status | Description
Policy | O | The name of VAL server policy.
>Area of interest | M | The geographical or service area for which the policy profile applies.
>Trigger event | M | Indicating the event that should be monitored, associated with the threshold of the monitored parameter.
>Expected action | M | Indicating the excepted actions associated with the updated parameter.
Lifetime or number of events | M | Time duration or number of times the policy can take action.
Priority | O | Indicates the priority of the policy.
Scheduling period | O | Indicates the scheduling of policy in terms of time.
>Start time | M | Indicates the scheduled start time.
>End time | M | Indicates the scheduled end time.
Preemption | O | Indicates the pre-empt capability of the policy.
Table 2: VAL server policy provisioning Request
Table 3: Policy profile