## Slide 1: Discussion Paper: Multiple UEs in use by one MC service user. Relevance and possible addressing.
Andreas Platzer
BDBOS

## Slide 2: Status
An MC service user may be concurrently logged into multiple UEs.
Based on current Stage 2 MCX standards it is not possible
  to distinguish or
  to address a specific MC service UE

## Slide 3: Where is it relevant to distinguish? 1/4
Ambient Listening: A listening user needs to listen to a specific MC service UE.
Temporarily / permanent disabling of UEs: A dispatcher needs to disable a specific MC service UE.
In all cases distinguishing and addressing of a specific UE is required.

## Slide 4: Where is it relevant to distinguish? 2/4
Location services: For example, a dispatcher needs to distinguish Location information from multiple UEs of one user.
Using the optional “MC service UE label” location reports/notifications from different UEs can be distinguished.
Note: The “MC service UE label” is not routable and not globally unique, but human readable.

## Slide 5: Where is it relevant to distinguish? 3/4
Logging and recording: A dispatcher wants to activate Logging & Recording from activities on any UE of a user.
Question : Is it needed to limit this use cases to a specific UE? Proposal : Logging & Recording shall be activated per User and not on UE level. Distinguishing of logging records can be done on existing Stage 3 MC client IDs.

## Slide 6: Where is it relevant to distinguish? 4/4
Discreet Listening / Lawful Interception:
  What is the Use Case? An authorized User wants to listen/view any activities of a specific User?
  Or An authorized User wants to listen/view activities on a specific UE?
Question: Shall DL/LI be activated per User or per UE?

## Slide 7: Possible addressing of a specific UE, based on “MC service UE label”
Authorized MC service user
(e.g., dispatcher) wants to address a specific UE (e.g., UE 2)
Preconditions: labels set at UEs
„MC User X”, logged into multiple UEs, (with the same MC service ID).
Label = „A“
Label = „B“
Label = „C“
MC service server sends a message to all UEs of this User including label „B“ .
label „B“ does not match “A” NO Change
label „B“ does match “B” this UE is addressed
label „B“ does match “C” NO Change
UE 1
UE 2
UE 3
„B“
„B“
„B“
Client sends message to User „X“, including label „B“.