## Slide 1: Disabling MC service UE remotely
Arunprasath R
Samsung

## Slide 2: Call flow proposal
Authorized user(MC service client 1) issuing remote disable request for an MC UE
MC Service server checks whether MC service client 1 is authorized to disable the MC UE
MC Service server sends the remote disable request to the target MC Service client 2.
MC service client 2 acknowledges the receipt of the disable request
MC service client 2 handles the disable request (Log off from the MC service client)
If no acknowledgement received from the target client, MC service server caches the information – Which MC UE is disabled and so on
MC service server sends the response to the Originating client

## Slide 3: Points to consider (1/2)
Can have an indicator in the request to specify whether the request is to temporarily disable(logoff) or permanently disable
Permanent disable : Leave it outside the scope of standards or consider it in the scope need to be discussed. How to handle the devices which do not have support for MDM ??
MC service server need to cache the disable information to handle the target UE in a not reachable state (Step 6 in the prev slide)
Handling of MC Service user logged in from more than one MC service Ues:
  Dispatcher or authorized MC service user specifying the device identifier in the disable request to uniquely identify a particular device
  Stage 3 specified MC client ID which is a unique identifier – Consider using this ??
    MCPTT client ID: is a globally unique identification of a specific MCPTT client instance. MCPTT client ID is a UUID URN as specified in IETF RFC 4122 [67]. [TS 23.479]

## Slide 4: Points to consider (2/2)
6. Handling of MC UE disable request not delivered to the target MC service client
  MC service server to maintain the information that a particular MC UE is disabled and request not delivered to the UE.
  When the UE come back online re-send the disable request
  When the UE attempts to login or utilize MC services , reject all the requests and resend the disable request.

## Slide 5: Handling of MC Service user logged in multiple devices
The MCX user can login from multiple devices. What do we have so far for handling the multiple device scenario are as below :
  MC service UE label – An optional entry that can be configured as part of Initial MC service UE configuration data. Excerpts from 23.280 Clause 8.1.6 :
    The optional MC service UE label allows to distinguish between different MC service UEs in use by the same MC service ID. The MC service UE label may be added to location information reports.
    The non-routable MC service UE label may include human readable information, such as an incident or MC service user specific ID, manufacturer name, brand, model, serial number, etc.
  (Stage 2) Mapping information maintained at MC Service server (Clause 8.3.1 of TS 23.280)
    The MC service server manages the mapping between MC service IDs and public user identities.
    The MC service server manages the mapping between MC service IDs and public GRUUs.

## Slide 6: Handling of MC Service user logged in multiple devices
  [Stage 3] MC service Client ID (MCPTT Client ID) – Clause 4.10 of TS 24.379
    The MCPTT client ID is a globally unique identification of a specific MCPTT client instance.
    The MCPTT client generates the MCPTT client ID as specified in clause 4.2 of IETF RFC 4122 [67].
    The MCPTT client preserves the MCPTT client ID across power cycles and it remains same across sessions till it’s factory reset.
    The MCPTT client ID is shared with MCPTT server as part of SIP REGISTER/SIP PUBLISH during service authorization.
  [Stage 3] Mapping information maintained at MC Service server (Clause 7.3.2 of TS 24.379)
    The MC service server maintains the binding between the MCPTT ID, MCPTT client ID to the IMS public user identity.
    The no of binding information depends on the no of devices the user is simultaneously logged in.
    The MCPTT server will store the binding of the MCPTT ID, MCPTT client ID, IMS public user identity and an identifier addressing the MCPTT server in an external database.

## Slide 7: Handling of MC service ID mapping at MC service server
As-is
To-be

## Slide 8: To discuss
The MCX client to share the MC service UE label or any unique human readable identifier to MCX server during the MC service authorization – This UE label to be configured in the Initial MC UE configuration data
MC service server to maintain this unique device identifier as part MC service ID binding information
This binding information to be made available to the MCX dispatcher/MCX Admin/MCX Authorized user [Procedure b/w MC service client and MC Service server to be there to fetch this information]
MCX dispatcher/MCX Admin/MCX Authorized user when performing any operation targeted to particular device of the MC Service user shall include the unique identifier as part of the request (e.g. Remote disable)
MC service server to identify the public GRUU of the target MC UE and route the request to the MC service client on that UE

## Slide 9
Thank you !!!