## Slide 1: ProSeP V2XP provisioning during registration

## Slide 2: Comparison of proposed solutions
Conditions | Alt1(C1-223416 / 3417) | Alt2(C1-223476) | Alt3(C1-223477) | Alt4(C1-223938 / 3744)
If A and NOT B | using the UE state indication procedure. | Same as C1-223416 | using the UE state indication procedure. | using the existing UE state indication procedure.
If NOT A，and B | the UE shall set the Payload container type IE to "UE policy container" and include the UE POLICY PROVISIONING REQUEST message (see 3GPP TS 24.587 [19B]) in the Payload container IE of the REGISTRATION REQUEST message. The UE POLICY PROVISIONING REQUEST message is extended to include UE policy classmark IE and UE OS Id IE. (C1-223417). | Using the existing UE POLICY PROVISIONING REQUEST message for ProSeP as for V2XP. In addition: the AMF shall set V2X (V2XP?) or ProSe (ProSeP?) bit in the 5GS network feature support IE to the value "1“ if V2X/ProSe is supported by the network. | Not described. -- Only include UE POLICY PROVISIONING REQUEST message in UE policy payload container? | Not described. -- Only include UE POLICY PROVISIONING REQUEST message in UE policy payload container? The UE POLICY PROVISIONING REQUEST message is extended to include UE policy classmark IE and UE OS Id IE. (C1-223744, same as C1-223417)
If A and B | The UE STATE INDICATION message is extended to contain an Requested UE policies IE which is included when the UE needs to request V2XP, ProSeP or both. | Same as C1-223416. In addition: the AMF shall set V2X (V2XP?) or ProSe (ProSeP?) bit in the 5GS network feature support IE to the value "1". | Include both the UE STATE INDICATION message and UE POLICY PROVISIONING REQUEST message in UE policy payload containers. No change/extension to the UE STATE INDICATION message. | Same as C1-223477.
Condition A: The UE has one or more stored UE policy sections identified by a UPSI; Condition B: The UE needs to request V2XP, ProSeP or both.

## Slide 3: Main divergence
When both condition A and B are met, whether the request of V2XP/ ProSeP is indicated via:
Alt-1: New IE (Requested UE policies IE) in the UE STATE INDICATION message (C1-223416/3476); or
Alt-2: UE POLICY PROVISIONING REQUEST message (C1-223477/3938)
Proposal: Discuss the pros and cons of the above two alternatives and choose one. SoH if needed.

## Slide 4: Comparison of Alt-1 and Alt-2
 | Pros | Cons
Alt-1 | 1) backward compatible 2) UE initiates one UPDS transaction during registration. This resulting into simple PCF handling needed to create one MANAGE UE POLICY COMMAND providing all needed UE policy sections (URSP, ANDSP, V2XP, ProSeP, ...) to the UE, as requested in SA2 LS S2-220129 stating “Therefore, there is no expectation that the PCF will generate two separate MANAGE UE POLICY COMMAND messages to the UE.” 3) Aligned with SA2 LS S2-2201294 which states “the PCF will determine the policies to be provisioned taking into consideration of the indications received within the same UE Policy Container.” 4) No AMF impact. | 1) Change of the concept of the UE state indication procedure which is mainly for notifying the network for the UPSI supported list, ANDSP support and OS ID support.
Alt-2 | 1) No AMF impact since the AMF procedure has been defined in subclause 5.4.5.2.3 since rel-15, 2) I (Roozbeh) do not agree with bullet 2 of Ivo as the con (see yellow highlight) with the following reasoning: The AMF should know how to treat multi payloads which is to treat the request from the UE as 1) current identified UE state indication procedure and 2) current identified UE policy request procedure. Therefore the PCF receives two different request from the same UE, which it shall treat. Note that multi requests to the PCF should not be an issue, since it receives many requests which it should treat. | Need to fix the back-compatibility issue, i.e. how the legacy network decode the multiple payload containers. –The UE STATE INDICATION message can be defined as the first payload? [RA] Backward compatibility issue due to use of other type than “UE policy container type” or new structure for Payload container IE UE initiates one or two UPDS transactions during registration. This resulting into more complex PCF handling needed to create one MANAGE UE POLICY COMMAND providing all needed UE policy sections (URSP, ANDSP, V2XP, ProSeP, ...) to the UE, as requested in SA2 LS S2-220129 stating “Therefore, there is no expectation that the PCF will generate two separate MANAGE UE POLICY COMMAND messages to the UE.” Not aligned with SA2 LS S2-2201294 which states “the PCF will determine the policies to be provisioned taking into consideration of the indications received within the same UE Policy Container.” If Additional payload container IE is introduced in REGISTRATION REQUEST as in draft-revision-of-C1-223938-v1, this creates a new AMF impact, new impact on AMF-PCF signalling.

## Slide 5: Other proposals
Agree the following as it seems a consensus:
When the UE only needs to request V2XP, ProSeP or both, the UE POLICY PROVISIONING REQUEST message is used with the extension of including UE policy classmark IE and UE OS Id IE. (C1-223417, C1-223744).
Not include the following in R17 since many companies raised concerns in the email discussion:
the AMF shall set V2X (/V2XP) or ProSe (/ProSeP) bit in the 5GS network feature support IE to the value "1" if V2X/ProSe is supported by the network.

## Slide 6: Thank You!