## Slide 1: 3GPP TSG GERAN #64 GP-140985 17-21 November, 2014 Agenda item 7.1.5.3.5 Proposal for CIoT Complexity Comparison Source: u-blox

## Slide 2: Standalone analysis
No sub-functional level comparison between candidates
Functional blocks listed to the level that reviewers can understand the content and analysis
  Details of functional blocks left open since they will be dependent on solution
  Describe what is on chip, and what external components are used

## Slide 3: Complexity metrics
Silicon area estimate, including on-chip memory
  Process node, and some indication of required gate density
  Indication of RF and BB area ratio for the solution
List of external components
  Main technical characteristics indicated enabling comparison between solution, e.g.:
    Memory size
    PA power / linearity
    Filters
    Crystals
    …

## Slide 4: Exclude
Power management, LDO’s, charging, etc.
Interfaces ( related to application functionality)
Application HW and memory
IC package
PCB / screens
Connectors and other mechanics
Antennas

## Slide 5: Compare…
Silicon area
  Gives indication about complexity, but not direct cost difference
External components
  Number of components
  Any special requirements that affect relative cost?

## Slide 6: GPRS reference
Desirable to have “worked example” for the legacy GSM reference
Legacy GPRS reference
  Quadband modem area 20 mm2 in 65 nm
    What is included?
  Also derive area for single band