## Slide 1: NR NTN Ka band on-going trials
Inmarsat, Viasat, Fraunhofer, ESA
3GPP TSG RAN#100 RP-231304
Taipei, Taiwan, 12th – 18th June 2023 Agenda Item 9.3.2.7
(For Information)

## Slide 2: First GEO Ka-band trial of 3GPP New Radio for Non-Terrestrial networks (NR NTN)
GOAL: prove functionality and evaluate performance of 5G NR OFDM/SC-FDMA waveform over Inmarsat Ka-band GEO Very High-Throughput Satellite (VHTS)
Project sponsored by: under the aegis of:
5G NR gNB and UE (OpenAirInterface) development:
Ka band GEO satellite, VSAT and ground station:

## Slide 3: Trial Setup
  Inmarsat GX5 Ka band VHTS (11E) – 72 Ka band transponders
  Inmarsat GX Ka band ground station
  (Nemea, Greece)
  Cobham Explorer 3075 Ka band VSAT
  (Germany, UK)
  NI Ettus N310 SDR
  +
  x86_64 Linux PC with OpenAirInterface 5G
  (UE, gNB )

## Slide 4: Trial setup (continued)
Standard VSAT RF Frontend:
  75 cm aperture
  Low-Noise Block Down-converter (LNB) – NJRC, NJR2825*
  Block Up-Converter (BUC) – NJRC NJT5830*
Frequency: 20 GHz (DL), 29 GHz (UL)
2x40 MHz carrier bandwidth (initial test)
30 kHz Subcarrier Spacing (SCS)
QPSK, 16QAM
No PTRS enabled
No PAPR compensation
Timing pre-compensation based on known UE and Satellite location
No Doppler pre-compensation
  VSAT UE Architecture
  *NOTE: Datasheets are publicly available

## Slide 5: Early results
The UE with VSAT frontend can successfully decode DL SSB and synchronize with the NR carrier
Successful PDSCH and PUSCH decoding
The carrier was backed-off (not driven to satellite HPA saturation point)
With power back-off, the carrier is very sharp, extremely low spectral regrowth – guard band could be minimized to improve spectral utilization
Even without PTRS, the phase noise at 30 kHz SCS is acceptable at least for GEO
30 kHz SCS is very feasible at least for GEO
40 MHz Carrier BW is very feasible at least for GEO, smaller CHBW (e.g. 20, 30 MHz, irregular CHBWs) are expected to be feasible as well
TA control loop works and is able to maintain timing.

## Slide 6: Conclusion
The trial has already demonstrated that 5G NR NTN in Ka band is possible with existing satellite and VSAT UE architectures
Re-using of current VSAT UE architecture with Intermediate Frequency (IF) would enable fast market adoption of NR NTN, without precluding other implementations
GEO can already be supported
30 kHz SCS can be supported at least for GEO with slow-moving UE
Sub-50 MHz channel BWs can be supported and are important for NTN Above 10 GHz
FR1 UE parameters could be reused for quicker time to market
PAR/PAPR reduction techniques are expected to be required – Further studies are on-going
Guard band could be reduced compared to terrestrial operation, to improve spectral utilization
Cyclic prefix reduction could be further studied, if UE GNSS and Ephemeris are accurate enough
Further consider autonomous TA for higher numerologies
Trials are still on-going, more results are expected