## Slide 1: Way forward for the Rel-18 WID NR_NTN_enh
Sources: Moderator (Thales)
3GPP TSG RAN #99
June 12 - 14, 2023
Agenda: 9.3.27
TDOC: RP-231451
For: discussion

## Slide 2: From RP-230878
Proposal 1:
  “TSG RAN tasks RAN4 to scope the work needed to define the RRM requirements (i.e. beam steering related) necessary for NR-NTN UEs operating in the NTN example band (i.e. Ka band) based on associated assumptions of the UE architecture (including beam steering capabilities) .”

## Slide 3: From RP-231432
Proposal 2:
  TSG-RAN tasks RAN1 to focus its network verified UE location work on Alt1 for the combination of “UE and gNB receive-transmit time difference measurements”:
    Alt-1: UE Rx-Tx time difference based on Option 3 and gNB Rx-Tx time difference as defined in TS 38.215.
      Note 1: The signaling method of UE Rx-Tx time difference definition option 1 is not precluded if Alt1 is adopted
  If the work at RAN1 is not completed at RAN#101, the nwk verified UE location will be dropped from RAN1

## Slide 4: From RP-231298
Proposal 3: in clause 4.1.4 “mobility enhancement” of the NR-NTN-enh WID
  Add “Identify and if needed, define RRM enhancement in idle/inactive mode for autonomous SMTC shifting to address the effect of opposite satellite motion across adjacent orbital planes (RAN4)”

## Slide 5: From RP-231214
Proposal 4:
  TSG-RAN tasks RAN4 to define the release independent requirements for NR-NTN (FR1 & above 10 GHz) as part of Rel-X and reflect them in the corresponding release independent specification
    FFS whether these requirements shall be captured in TS 38.307 or in a separate TS
    Rel-X refer to Rel-17 or beyond

## Slide 6: From RP-231173
Proposal 5: Select one among the 2 options here after
  Opt1: The discussion on the followings is postponed to RAN#101 however without further discussion in RAN1#114
    whether to support repetitions for PUCCH transmission when dedicated PUCCH resource configuration is not provided
    Regarding the PUCCH transmission behavior after the transmission of HARQ ACK of PDSCH with UE contention resolution identity until the decoding of RRC message containing dedicated PUCCH resource configuration, whether to support SIB indication for the choice between "no PUCCH repetition" or "same as the PUCCH transmission of HARQ ACK of PDSCH with UE contention resolution identity"

## Slide 7: From RP-231173 (cont’d)
Proposal 5: Select one among the 2 options here after
  Opt2: RAN tasks RAN1 to discuss followings in RAN1#114
    whether to support repetitions for PUCCH transmission when dedicated PUCCH resource configuration is not provided
    Regarding the PUCCH transmission behavior after the transmission of HARQ ACK of PDSCH with UE contention resolution identity until the decoding of RRC message containing dedicated PUCCH resource configuration, whether to support SIB indication for the choice between "no PUCCH repetition" or "same as the PUCCH transmission of HARQ ACK of PDSCH with UE contention resolution identity"