## Slide 1: Summary for discussion [RAN1-UL-Coverage]
Moderator (NTT DOCOMO, INC.)
3GPP TSG-RAN Meeting #100
Taipei, June 12-14, 2023
Agenda Item: 9.3.1.3
RP-231493
Revision of RP-231473

## Slide 2: Issue #1: Enhancements to reduce MPR/PAR
Proposals in contributions
  RP-230864: RAN#100 should confirm that at least FDSS with spectrum extension (FDSS-SE) shall be specified as a solution for MPR/PAR reduction in Rel-18.
  RP-231254: Only transparent MPR reduction schemes are specified in Rel-18. Schemes should provide gains for inner RB allocations.
  RP-231406: Due to limited TU left, RAN4 focuses on transparent scheme for MPR/PAR reduction.
    No RAN1 specification impact is expected.
Proposal #1 (Offline consensus)
  No RAN1 specification impact is expected for MPR/PAR reduction in Rel-18 UL Coverage WI
    RAN4 will define new optional requirements in the form of at least MPR reduction suitable for a transparent scheme (such as FDSS) that have no RAN1 specification impact

## Slide 3: Issue #2: PHR enhancement for DWS
Proposals/Observations in contribution (RP-231254)
  UE assistance information such as PHR of the target waveform can improve the scheduler’s ability to know when to switch waveforms
  RAN1 agreements on dynamic waveform switching assume that PHR enhancements are in scope
  Determining whether RAN2 work is needed is part of the work on the dynamic waveform switching objective.
  Proposal: Inform RAN1 and RAN2 that PHR enhancements are in scope of the Rel-18 coverage enhancements work item
Proposal #2 (whether or not to remove yellow part needs to be discussed/decided in online session)
  RAN provide guidance to RAN1/2 on dynamic waveform switching objective as below
    [RAN1 will decide whether to define any PHR enhancement for dynamic waveform switching by August meeting
    If RAN1 agreed to define PHR enhancement,] RAN1 will provide details on the PHR enhancement for dynamic waveform switching to RAN2 by August meeting
    RAN2 will not work on any new PHR triggering procedure for dynamic waveform switching in Rel-18 UL Coverage enh WI

## Slide 4: Updated proposals for making decision at RAN#100
Alt.1 (option 1 in RAN1 agreement):
  RAN provide guidance to RAN1/2 on dynamic waveform switching objective as below
    RAN1 will provide details on the PHR enhancement for dynamic waveform switching to RAN2 by August meeting
    RAN2 will not work on any new PHR triggering procedure for dynamic waveform switching in Rel-18 UL Coverage enh WI
Alt.2 (updated version of one with yellow part):
  RAN provide guidance to RAN1/2 on dynamic waveform switching objective as below
    RAN1 will discuss whether to define any PHR enhancement for dynamic waveform switching and to provide the details to RAN2 by August meeting
    RAN2 will not work on any new PHR triggering procedure for dynamic waveform switching in Rel-18 UL Coverage enh WI
Alt.3 (option 4 in RAN1 agreement):
  RAN provide guidance to RAN1 on dynamic waveform switching objective as below
    No PHR enhancement for dynamic waveform switching is introduced in Rel-18 UL Coverage enh WI