## Slide 1: Views on Rel-19 NR positioning
3GPP TSG RAN Meeting #101
Bangalore, India, September 11-15, 2023
Source： ZTE, Sanechips
Agenda: 8A.2.12.4
RP-232151

## Slide 2: Motivation
Commercial interest
Higher accuracy
Further Power saving
Reasonable workload
UWB positioning
  UWB positioning (>= 500MHz) provides confident sub-meter accuracy of positioning which attracts a lot of attention from product and market. However, currently UWB technology is not included in either LPP or NRPPa spec.
eLPHAP
  Rel-18 LPHAP evaluates performance and specifies solutions for use case 6 (6 months - 1 year battery life), only a part of contributions show that battery life requirement can be achieved with potential enhancement for LPHAP device A.
  Longer battery life requirements (e.g. use case 5 with 18 month battery life) with limited capacity is desirable.
SL positioning (if TU budget is allowed)
  During Rel-18 SI phase, most contributions show that target requirement Set B (sub-meter accuracy) can NOT be achieved.
  Partial sensing, IUC is not supported in Rel-18
  Only ITS band and licensed spectrum in FR1 are supported in Re-18 SL positioning

## Slide 3: Proposals for Rel-19 positioning
UWB based positioning [RAN2, RAN3]
  Both LPP and NRPPa enhancement
LPHAP enhancement [RAN2]
    Relaxed positioning, e.g. for UEs in the cell center/with low mobility
SL positioning enhancement [RAN1, RAN2]
  SL positioning in Unlicensed bands
  Rel-18 leftovers:
    IUC
    Partial sensing
High priority

## Slide 4: UWB Positioning

## Slide 5: Background - Current LPP in NR (1)
    UWB based positioning is NOT supported in current NR specifications
    While Bluetooth-based positioning and WLAN-based positioning are supported
      In the Bluetooth positioning method, the UE position is estimated with the knowledge of geographical coordinate of reference Bluetooth beacons. This is accomplished by collecting a certain amount of measurements from UE's Bluetooth receiver, and applying a location determination algorithm using databases of the estimated position's references points
Information may be from the UE to the LMF
Information | UEAssisted | Standalone
Bluetooth Location Information |  | 
MAC Address | Yes | No
Received Signal Strength (RSSI) | Yes | No
Time Stamp | Yes | No
Measurement characteristics | Yes | No
UE Location Information |  | 
UE position estimate with uncertainty shape | No | Yes
Position Time Stamp | No | Yes
Location Source (method(s) used to compute location) | No | Yes

## Slide 6: Background - Current LPP in NR (2)
    Bluetooth based positioning was introduced in Rel-13 inheritted from LTE.
TS 37.355

## Slide 7: Background - Current NRPPa
    UWB based positioning and Bluetooth-based positioning is NOT supported in current NRPPa procedure
    While WLAN-based positioning is included in ECID method
Direction: NG-RAN node ® LMF.
IE/Group Name | Presence | Range | IE type and reference
Message Type | M |  | 9.2.3
NRPPa Transaction ID | M |  | 9.2.4
LMF UE Measurement ID | M |  | INTEGER (1..15,…, 16..256)
RAN UE Measurement ID | M |  | INTEGER (1..15,…, 16..256)
E-CID Measurement Result | O |  | 9.2.5
Criticality Diagnostics | O |  | 9.2.2
Cell Portion ID | O |  | 9.2.12
Other-RAT Measurement Result | O |  | 9.2.13
WLAN Measurement Result | O |  | 9.2.14
>WLAN Measurement Result Item | 
>>WLAN RSSI | M
>>SSID | O
>>BSSID | M
>>HESSID | O
>>Operating Class | O
>>Country Code | O
>>WLAN Channel List | 
>>>WLAN Channel List Item | 
>>>>WLAN Channel | M
>>WLAN Band | O

## Slide 8: Background - UWB based positioning
    IEEE802.15.4/4z protocals defines UWB technics, where IEEE802.15.4z was distributed in 2020.
    Integraton of 5G gNB and UWB anchor have been specified in CCSA
.
>= 500MHz bandwidth
Very Large bandwidth
Support TDOA, RTT, AOA methods
Nowadays, UWB is more and more deployed in the market

## Slide 9: ZTE product
pRRU
BBU
UWB AP Module
5GC
5G+UWB measurement
UWB
UE/tag
5G UE
provide power

## Slide 10: Proposal 1 for UWB positioning
    Introduce UWB-based positioning in LPP and NRPPa in Rel-19
UWB anchor
LMF
NG-RAN node
UWB measurement report
UWB measurement request
LMF
UE
UWB measurement report
Asstance data / UWB measurement request
UE
UWB measurement
Transparent to NR
Fusion positioning between 5G and UWB

## Slide 11: LPHAP enhancement

## Slide 12
LPHAP Enhancement - background
    Related background:
    Relaxed RRM measurement: UE can receive and measure SSB from the serving cell and neighbor cell in RRC_INACTIVE or RRC_IDLE state for RRM (radio resource management) measurement. If some conditions are satisfied, UE can perform relaxed RRM measurement via reducing SSB measurement.
TS 38.304 Relaxed RRM measurement 5.2.4.9 Relaxed measurement 5.2.4.9.0 Relaxed measurement rules 5.2.4.9.1 Relaxed measurement criterion for UE with low mobility 5.2.4.9.2 Relaxed measurement criterion for UE not at cell edge 5.2.4.9.3 Relaxed measurement criterion for a stationary RedCap UE 5.2.4.9.4 Relaxed measurement criterion for a stationary RedCap UE not at cell edge

## Slide 13
LPHAP Enhancement - relaxed positioning
    Use case:
    Current positioning behavior: Currently UE has to wake up to receive every PRS indicated by LMF in RRC_INACTIVE or RRC_IDLE state (and/or sends SRS as configured by gNB) to remain high positioning accuracy, which will cause large ramp-up/ramp-down power consumption.
    For LPHAP UE: It is likely that the LPHAP UE has low mobility state, or the LPHAP UE is always within the cell center (e.g., in a factory area with small movement). Since the UE can be assumed as rarely changing its location, the UE does not need to measure the DL-PRS(or transmit SRS) frequently under such conditions in order to achieve power saving.
    Benefit:
    Reduce power consumption while maintaining high accuracy positioning, especially in RRC_INACTIVE and RRC_IDLE state. i.e., adaptive power saving for LPHAP UE.

## Slide 14
Proposal 2 for LPHAP Enhancement
    Support LPHAP UE to perform relaxed positioning under certain conditions
      DL: Relaxed DL-PRS measurement
      UL: Relaxed positioning SRS transmission
        Conditions: Reusing criterions configured for RRM relax measurement in SIB2 including low mobility criterion, not at cell edge criterion, stationary UE, etc.
Example procedure of relaxed DL-PRS measurement

## Slide 15: SL positioning enhancement

## Slide 16
SL Positioning enhancement
Rel-18 SL positioning
Methods: RTT, SL-AoA, SL-TDOA Support for SL PRS in FR1 spectrum Licensed band Resource allocation Scheme 1 Scheme 2: Only full sensing and random resource selection Others: Inter-UE coordination (IUC)
Rel-19 SL positioning
Resource allocation scheme 2: partial sensing Potentially: IUC Unlicensed band
*All the above bullets were discussed in Rel-18, but not finally specified because of limited time budget

## Slide 17
    If TU budget is allowed, the following scope can be considered:
    Support IUC for SL positioning
    Support partial sensing for SL positioning scheme 2
    SL-U positioning
      Specify channel access mechanism for SL positioning, use the mechanism defined in Rel-18 SL communication (e.g. LBT, COT sharing) as a starting point.
Proposal 3 for SL positioning

## Slide 18: Thank you