## Slide 1: Rel-19 Study on ISAC
Sourced By: Lekha Wireless
Agenda Item: 9.1.1.7
3GPP TSG RAN Meeting #102 RP-232756
Edinburgh, GB, December 11-15, 2023

## Slide 2: Prioritising Use Cases
Importance to limited set of use cases in TR22.837 [1].
UAV detection/tracking use cases in TR22.837 must be prioritized for RAN study [2]:
  Unmanned aerial vehicles (UAVs) have enormous potential in the public and civil domains.
  High flexibility, unmanned aerial vehicles (UAVs) can be very useful in the current and future wireless communication systems.
  UAV flight trajectory tracing
  sensing for UAV intrusion detection
Other use case can be addressed with less priority.
Proposal 1: UAV detection/tracking use case in 3GPP TR22.837 must be prioritized for Rel-19 RAN study.

## Slide 3: Frequency Ranges for Sensing
FR1 ( < 7.125 GHz): can support the use cases requiring a low level of details from the sensing channel, specifically, the ones concerning object detection, location and/or tracking, etc.
FR2(> 24.25 GHz): characterized by properties such as large bandwidth and large no. of antenna elements compared to FR1 and FR3.
  a large sensing resolution in terms of range, angle (e.g., for AoD, AoA measurements), phase, etc.
  Enables receiver to measure the signal with finer resolution and hence in higher detail compared to FR1 and FR3.
FR3 (7.125-24.25 GHz): the mid-way point between the two frequency bands that allow for more higher sensing resolution compared to FR1 band.
  It has the advantage of higher reliability and coverage area compared to FR2 band.
Observation 1: Existing frequency bands (FR1, FR2, FR3) are enough to support sensing application and new frequency bands would add complexity to the system in terms of modelling efforts.
Proposal 2: For UAV detection, use 7-15 GHz to achieve propagation characteristics like below 7 GHz with moderate sensing resolution.

## Slide 4: Prioritising Sensing Modes
Types of Sensing:
  gNB based sensing: collision avoidance, pedestrian/animal intrusion on a highway, rainfall monitoring, flooding in smart cities, and railway intrusion detection.
  UE based sensing: integrated sensing and positioning in factory hall, blind spot detection, Vehicles Sensing for ADAS, and immersive experience based on sensing.
  UE assisted sensing: at crossroads with/without obstacle, accurate sensing for automotive maneuvering and navigation service, gesture recognition.
For UAV tracking/detection, enable gNB based Bi-static sensing.
Observation 2: gNB-gNB and UE-gNB (UL) based Bistatic sensing are more appropriate for UAV detection and tracking.
Proposal 3: UE-gNB (UL) Bistatic sensing should be prioritised for UAV detection and tracking as the current channel models are based on DL and UL.
Proposal 4: Enable sensing at gNB.

## Slide 5: Conclusion
Observations 1 : Existing frequency bands (FR1, FR2, FR3) are enough to support sensing application and new frequency bands would add complexity to the system in terms of modelling efforts.
Observation 2: gNB-gNB and UE-gNB (UL) based Bistatic sensing are more appropriate for UAV detection and tracking.
Proposal 1: UAV detection/tracking use case in 3GPP TR22.837 must be prioritized for Rel-19 RAN study.
Proposal 2: For UAV detection, use 7-15 GHz to achieve propagation characteristics like below 7 GHz with moderate sensing resolution.
Proposal 3: UE-gNB (UL) Bistatic sensing should be prioritised for UAV detection and tracking as the current channel models are based on DL and UL.
Proposal 4: Enable sensing at gNB.

## Slide 6: References
[1] 3GPP TR 22.837 Study on Integrated Sensing and Communication.
[2] RP 232617 Moderator's summary for REL-19 RAN1 topic ISAC & Exploring Study in New Spectrum (7-24GHz) Nokia, Nokia Shanghai Bell.
[3] RP 231737 Study on Channel Model for ISAC Techniques, Lekha Wireless Solutions.
[4] RP 231990 Views on Rel-19 Channel Modelling, InterDigital, Inc.

## Slide 7
Thank You!