## Slide 1: Study on AI/ML based Mobility Enhancement in Release 19
Sourced By: Lekha Wireless
Agenda Item: 9.1.2.4
3GPP TSG RAN Meeting #102
Edinburgh, Scotland, December 11-15, 2023
RP-232758

## Slide 2: Motivation
Mobility leads to handover mechanism. The existing handover mechanisms (including Rel-18 features) can be considered as a starting point:
    Rel-15: Basic HO
    Rel-16: CHO
    Rel-18: LTM (L1/L2-Triggered Mobility)
Limitations: They can perform well in normal mobility scenarios, however, the performance is constrained in some scenarios, e.g. FR2, high mobility etc.
      The existing handover mechanisms are reactive by design
      The existing decisions are made based on historical measurements and sometimes inaccurate RRM measurements and/or UE location that can impair good handover decisions
      The complexity, measurement effort, and signalling overhead may be high
      Due to mobility, there may be RLF, beam failure and HOF happened, and current failure handling methods focus on fast recovery, and they are reactive and cannot eliminate the interruption or bad services caused by a failure event.
  All these limitations related to mobility have led to the researchers working on AI/ML based Mobility Enhancements.

## Slide 3: Objective: Handover Enhancement
  HO decision optimization, including
      Candidate/target cell prediction in L3-based mobility, or, candidate/target beam(s) and cell(s) prediction in LTM
      HO parameter adjustment/tuning
      Unintended events prediction, e.g., HO failure/RLF prediction, ping-pong and short-stay HO prediction
  RRM measurement prediction, including
      Beam-level measurement prediction
      Cell-level measurement prediction, e.g., using intra-frequency measurement results to forecast the RRM measurement of inter-frequency/inter-RAT cells
  Taking above into account, the study item can aim to investigate potential enhancements on AI/ML-based mobility and corresponding feasibility
Frequency Bands : FR3 and its feasibility study of handover mechanisms

## Slide 4: Use Cases and Performance Evaluation
Group handover (for UEs with the same mobility properties) For example: Group of passengers in a train who move from same source to destination.
AI/ML can be used in the following aspects
  AI/ML based Target/Candidate cell/beam prediction
  AI/ML based Load balancing in Target cell to achieve better QoE
  AI/ML based Interference aware RRM (e.g., RSRP, SINR) and Synchronization procedures in teh target cell
  AI/ML based HO parameter tuning such as triggering time, decision metrics etc.
  Reliability/robustness
  Reduction in interruption time
  Reduction in procedure latency (eg: Same set of RRM resources, Beams used in all target BS’s)
  Reduction in signalling overhead
  Minimising data rate impact during mobility procedures
KPIs for performance comparison:
Predictive mobility:
Intelligent transportation networks
  For example: Railways, Fixed source to destination routes like home, office etc.

## Slide 5
Conclusion
Following are the observations:
Observation 1: Existing handover mechanisms (Basic HO, CHO and LTM-L1/L2-Triggered Mobility) can perform well in normal mobility scenarios, however, the performance is constrained in some scenarios, e.g. FR2, high mobility etc.
Observation 2: Existing handover decisions are made based on historical measurements and inaccurate RRM measurements and/or UE location that can impair good handover decisions.
Observation 3: Catering to mobility there may be RLF, beam failure and HOF happened, and current failure handling methods focus on fast recovery, and they are reactive and cannot eliminate the interruption or bad services demanding mobility enhancements.

## Slide 6
Conclusion
It is proposed to consider the following for further discussion:
Proposal 1: Study and investigate the potential enhancements of AI/ML based mobility involving HO decision optimization and RRM measurement prediction with respect to FR3 bands.
Proposal 2: Study and evaluate performance of predictive mobility in intelligent transportation networks.
Proposal 3: Study and investigate the AI ML models in establishing Group HO.
Proposal 4: Evaluate the KPIs performance of the AI ML based mobility enhancements and compare with the existing methods.

## Slide 7
References :
RP-231590- Mobility Enhancements objectives, 3GPP #RAN 101, Deutsche Telekom
RP-232623- Moderator's summary for Rel-19 RAN3 topic AI/ML for NG-RAN, 3GPP #RAN 101
RP-232622- Moderator's summary for Rel-19 topic AI/ML for Air Interface SI (mobility), 3GPP #RAN101

## Slide 8
Thank You