## Slide 1: Release-19 NR Sidelink Relay Enhancements for Public Safety
RAN#102, Edinburgh, UK, December 11-15, 2023
RP-232896
Source:
FirstNet, AT&T, Ericsson, NOKIA, MediaTek Inc., OPPO, KT Corp., Kyocera International, LG Electronics, InterDigital, Motorola Solutions, ASUSTek, Sharp, Philips, Fraunhofer IIS, Fraunhofer HHI, UK Home Office, SOFTIL, SYNC TECHNO, ERILLISVERKOT, BDBOS, Norwegian Communication Authority, Netherlands Police , Ministere de l'Interieur France, European Utilities Telecom Council (EUTC), National Institute of Standards and Technology (NIST), National Security Agency (NSA), National Telecommunications and Information Administration (NTIA), EDF (Électricité de France), Kyoto University

## Slide 2: Background: multi-hop SL Relay Enhancement for Public Safety
We consider public safety use cases and their requirements to facilitate mission critical Prose/D2D communications among public safety personnel in all coverage scenarios including off-network in Release-19 (R19)
Release-18 (R18) NR SL U2U and U2N single-hop relaying solutions are expected to be stable by the end of R18. However, R18 NR SL Relay is not sufficient to provide much-needed coverage extension for out-of-coverage public safety personnel for mission critical public safety use cases due to terrain limited coverage.
Public safety community has been requesting the support for multi-hop relaying since Release-17. As captured in 'RP-213496 Moderator's summary of discussion [94e-16-R18-SLRelayEnh]', RAN Chair's suggestion was "focus on single hop (REL-18 should be forward compatible to include multiple hops); multi-hop is then rather for future REL".
SA2 removed support for U2U and U2N multi-hop in release 18 (see SP-191317). It was generally understood the work would be re-addressed as a part of R19.
In public safety community’s opinion, R19 is the right time to incorporate multi-hop SL Relay enhancement to ensure communication to public safety personnel who are otherwise not reachable by R18 single-hop SL U2U/U2N Relaying. Any delay will deprive public safety personnel an important tool. Public safety has a concern that if this feature is not included in R19, it may be difficult to include in near future releases due to focus on new areas for 6G

## Slide 3: U2U multi-hop NR SL Relay Enhancement for Public Safety – No Coverage
This scenario presents a public safety use case requiring multi-hop U2U relaying to facilitate mission critical Prose/D2D communications among public safety personnel in an off-network areas.
In this scenario, there is a group of fire fighters that parachute into a remote mountainous wilderness to fight a forest fire. The fire fighters spread out across the fire line that spreads over several mountains. Due to the location, there is no network coverage but the need to communicate is high so they can keep each other informed of the conditions. The ability to support both private 1-to-1 calling, and group calling is mission critical to the fire fighter’s safety and enable them to do their job.
Release-18 SL U2U single-hop relay is not sufficient to reach each other by 1-hop SL coverage range. Multi-hop SL U2U relaying is necessary to ensure communication among fire fighters.
U2U Relay UE
U2U Relay UE
Source Remote UE
Target Remote UE
Fig. 1. Public safety use case requiring multi-hop U2U relaying (two U2U Relays)

## Slide 4: U2N multi-hop SL Relay Enhancement: In-building no Basement Coverage
This scenario presents another public safety use case requiring multi-hop U2U and/or multi-hop U2N relaying to facilitate mission critical Prose/D2D communications among public safety personnel.
Consider a situation where a fireman is in the back corner of a basement and has no connection to the network and needs to communicate with an on-scene commander on the street.
There could be a second fireman at the base of the steps and a third fireman at the top of the steps by the exterior door.
Multi-hop relay could allow the fireman in the back of the basement to have a mission critical communications with the onsite commander using multi-hop relay, even without network access.
Basement Area 1
Basement Area 2
U2N Relay UE
U2N Relay UE
U2N Relay UE
U2N Relay UE
Remote UE
Fig. 2. Public safety use case requiring multi-hop U2N relaying (and/or multi-hop U2U relaying).

## Slide 5: Objectives and Proposal for SL Relay Enhancement for Public Safety
We consider public safety use cases and their requirements to facilitate mission critical Prose/D2D communications among public safety personnel in all coverage scenarios including off-network in R19.
Our Objective is to enhance R18 NR SL U2U and U2N Relaying feature to multi-hop SL U2U and multi-hop SL U2N for L2/L3-based relaying respectively in R19.
Currently the SA2 SID is worded such that work on the sidelink multi-hop is dependent on RAN inclusion in R19. As such, it is mission critical to include the RAN work for multi-hop in the initial package decision during this meeting (#102). Otherwise, SA will not approve their work in the December meeting.
Proposal: RAN Plenary agree to include enhancements for NR Sidelink multi-hop relay as a part of the Rel-19 package.

## Slide 6
Thank you!