## Slide 1: Discussion on sidelink further evolution project scope for Rel-19
OPPO, LG Electronics, Apple, NEC, Toyota ITC, Mitsubishi Electric, Fraunhofer HHI, Fraunhofer IIS, WILUS, Hyundai Motor Company, Sharp, CATT, CICTCI, Continental, Transsion
3GPP TSG RAN Meeting #102
Edinburgh, GB, December 11 – 15, 2023
Agenda: 9.1.1.9
For: Discussion and decision
RP-232907

## Slide 2: Background for R19 sidelink
During Rel-19 RAN workshop, considerable interests are shown by 14 contributions proposed continuing the evolution of NR sidelink technology to support wider range of applications and use cases for V2X, public safety and commercial deployments
  SL evolution is listed as an additional RAN1-led candidate topic in both R19 workshop summary (RWS-230488), and endorsed RAN chair guidance for R19 (RP-231540)
  Remaining 2-3 TUs in RAN1 can accommodate up to 2 RAN1-led small projects
  Remaining 3 TUs in RAN2 can accommodate up to 3 RAN2-led small projects
RAN#101 discussion outcome / summary (RP-232626)
  Substantial support for NR sidelink evolution in Rel-19 especially in the area of sidelink beamforming / beam management in FR2

## Slide 3: Background on SL FR2 beam management
SL beam management in FR2 was studied during Rel-18 “NR sidelink evolution” WI in RAN1 and RAN2
  Evaluation methodology study and definition are completed in RAN1
  Technical solution options and feasibility are studied in RAN1 and RAN2 for SL unicast communication in the following aspects
    Reference signals for beam management
    Initial beam-paring
    Beam maintenance
    Beam failure detection and recovery
    Beam-based resource allocation
  A summary of RAN1 and RAN2 study outcomes is collected in RP-232787
RAN WGs are ready to covert the Rel-18 study to a Rel-19 WI
  A small RAN1-led project that requires
    1 TU in RAN1
    0.5 TU in RAN2
    0.2~0.5 TU in RAN4

## Slide 4: Justification for further evolution of SL in R19
Enhancements for NR sidelink operation in FR2-1 licensed spectrum has gained a strong interest from both operators and vendors since Rel-18 to improve sidelink communication performance and link coverage. The network operators could manage and utilize their FR2 spectrum for direct sidelink communication between two or more devices to offload their FR1 network traffic when the devices are in close proximity. Combining with NR sidelink relay, the network would be able to reach more devices that are out-of-coverage and in coverage-holes (weak coverage in black spots).
Besides the cellular network deployment, the use of SL beam management feature has been also proposed and needed for V2X communication and industrial applications.
The study on sidelink beam management (including initial beam-pairing, beam maintenance, and beam failure detection & recovery) by reusing existing sidelink CSI framework and Uu beam management concepts for SL unicast communication has been carried out by RAN WGs in Rel-18. During the Rel-19 RAN workshop in June 2023 and the discussion on Rel-19 SL topics in RAN#101 (RP-232626), the sidelink beam management feature received the most support. A normative work that based on Rel-18 SL beam management study outcomes is expected to introduce this feature for NR sidelink communication in Rel-19.

## Slide 5: Objectives for R19 NR sidelink further evolution WI
Specify mechanism to support beam management in NR sidelink operation [RAN1, RAN2, RAN4]
  SL beam management features including beam-panel selection should focus on FR2-1 licensed spectrum with an applicability of beam-panel selection in FR1 (ITS band).
  The support of SL beam management should target unicast communication based on Rel-18 study outcomes.
    To review the progress in RAN#105, if time allows, simple SL beam management scheme (e.g., beam sweeping with no feedback) can be considered and supported for broadcast and groupcast communications.
  Study and specify, if necessary, the support of beam-based resource allocation to enable spatial reuse of SL resources.
UE Tx and Rx RF requirement for supporting new features introduced in this WI, sidelink frequency bands for single-carrier operation [RAN4]
  The supported frequency band(s) for NR sidelink operation in FR2-1 licensed spectrum are to be determined based on company input during the WI.
  Support of new sidelink frequency bands should ensure coexistence between sidelink and Uu interface in the same and adjacent channels in licensed spectrum.
UE RRM core requirement for the new features introduced in this WI [RAN4]
Rel-19 sidelink should be able to coexist with Rel-16/17/18 sidelink in the same resource pool. This does not preclude the possibility of operating Rel-19 sidelink in a dedicated resource pool.