## Slide 1: Views on Rel-19 AI/ML for NG-RAN
Qualcomm
Dec 11th to 15th, 2023
Edinburgh, Scotland
3GPP TSG RAN Meeting #102
RP-233022
Agenda Item: 9.1.3.1

## Slide 2: Overview
RAN Chair’s summary for RAN Rel-19 Package (RP-232745)
Proposals for Rel-19
  AI/ML based mobility optimization
  Continuous MDT
  AI/ML based coverage adaptation
Potential SI/WI objectives for Rel-19 AI/ML for NG-RAN

## Slide 3: RAN Chair’s summary for RAN Rel-19 Package (RP-232745)
AI/ML for NG-RAN SI  WI
References: RWS-230488, RP-231540, RP-232623
Potential objectives:
  6 months SI + 12 months WI
  Rel-18 leftovers (depends on Rel-18 outcome), e.g.:
    Mobility optimization
      NR-DC
      UE Trajectory prediction
    Energy saving
      Prediction for energy cost
    Continuous MDT
  At least 1 At most 2 potential new use case/scenario which benefits from inference-based techniques
    Coverage and Capacity Optimization
    Potential Rel-18 use case enhancements (e.g. new scenarios for ES)
    QoE
    Slicing
    Note: Model training/inference at the DU and/or F1 enhancements must be justified by the use case
  Study: Consider available functionality specified in 5GC (NWDAF, MDAS) in order to align AI/ML framework between RAN and CN
In this contribution, we express our views to further clarify the potential objectives for Rel-19

## Slide 4: AI/ML based Mobility Optimization (1/2)
AI/ML based mobility optimization specified in Rel-18 included the following objectives:
  Predicting UE Trajectory for PCell mobility
  Collecting UE trajectory feedback from first-hop target node
Since we already have an AI/ML framework for PCell Mobility Optimization in Rel-18, the same can be reused and enhanced if needed to benefit other mobility use cases like PSCell mobility, CHO, LTM for Rel-19. We therefore propose the following:
Proposal 1a: RAN3 should study and specify signaling enhancements for R18 AI/ML based mobility optimization use case for the following scenarios, for both split and non-split gNB architectures :
  AI/ML based PSCell mobility (e.g. predicting PSCells)
  AI/ML based CHO (e.g., predicting CHO candidate/target cells)
  AI/ML based LTM (e.g., predicting LTM candidate/target cell(s) and beam(s))
RAN3 collaborates with RAN2 if assistance information is required to augment the above new scenarios and we therefore propose the following:
Proposal 1b: RAN3 collaborates with RAN2 to specify assistance information, if needed for the above mobility scenarios, both from UE to NW and NW to UE.
Extension of R18 use case

## Slide 5: AI/ML based Mobility Optimization (2/2)
The following leftovers from Rel-18 AI/ML based Mobility Optimization use case should be considered for Rel-19.
  UE Trajectory Feedback from multi-hop target nodes – though the source node predicts UE trajectory for multi-hop targets, due to time restriction and complexity involved, the feedback was restricted to single (first) hop target node in Rel-18. Hence, we propose to further work on solution to receive feedback from multi-hop targets for prediction validation at the source node.
  UE Trajectory Prediction continuity across UE RRC State Transition – UE stays in RRC Connected mode for a very short period and to collect metrics and perform AI/ML training and predictions in this short duration will not be beneficial for AI/ML based MO. Hence, we propose to specify solutions to provide predictions and collect feedback for UE trajectory across RRC states of the UE.
Proposal 2: RAN3 should study and specify signaling enhancements, if needed, to enhance R18 AI/ML based mobility optimization for both split and non-split gNB architectures for the following:
  UE Trajectory Feedback collection across multi-hop Target nodes
  UE Trajectory Prediction and Feedback across UE RRC state Transition
Leftover from R18

## Slide 6: Continuous MDT (1/2)
In Rel-18 we had the following common understanding captured in RAN3 Chair’s Notes RAN3#120
  Continuous collection of MDT traces is beneficial only for AI/ML training in OAM.
  Continuous MDT collection is to enable the continuous collection of MDT data from the same UE across RRC state changes (RRC_Connected, RRC_Idle, RRC_Inactive).
  Signaling-based MDT could provide continuous Data Collection from a certain UE; however, it has scalability issues when selecting large number of UEs and lacks cell-level granularity.
  Management-based MDT provides the advantage of being scalable when selecting large number of UEs. However, current management-based MDT mechanism cannot identify and group together MDT reports collected from the same UE across RRC states. UE selection is left to RAN implementation and it is not controllable by OAM.
Due to time constraint and the complexity involved, solutions to address Continuous MDT could not be achieved in Rel-18. However, there was common understanding that continuous MDT can be useful e.g., for AI/ML training.
Left over from R18
Notes: In Rel-18, RAN3 further discussed how to enable a more granular selection of UEs (e.g., certain UE types, UEs with certain capability) during management-based MDT but was not pursued. We think this can be one potential objective for Rel-19 and we therefore propose the following:

## Slide 7: Continuous MDT (2/2)
During R18 RAN3 discussions, there were many different solutions proposed by various companies to achieve Continuous MDT in Rel-18. It is preferable to achieve Continuous MDT via Network based solutions without any UE impact.
  Any UE enhancement for enabling continuous MDT would mean continuous data collection can only be done from Rel-19 UEs (and not from legacy UEs) and this will not be very useful for AI/ML training across a diverse set of UEs (including legacy UEs).
Observation: Continuous MDT collection is to enable identification of the UE across RRC state changes by leveraging legacy Logged and Immediate MDT procedures.
Therefore, we propose,
  Proposal 3: RAN3 should study and specify Network-based solution (without UE impacts) to enable Continuous MDT i.e., continuous collection of MDT data from the same UE across RRC state changes for NG-RAN AI/ML use cases.
Leftover from R18

## Slide 8: AI/ML based Coverage and Capacity Adaptation
AI/ML based coverage adaptation can be a good practical use case to study in Rel-19 because:
  Operators perform CCO as a regular operational task in their network and any intelligence to enhance this operation will be very useful in Operator Network.
  Coverage and capacity adaptation can be performed via existing SON procedures but is done reactively. Proactive coverage adaptation (via AI/ML techniques) can help in performing better CCO and NES e.g., by proactively deciding how to change cell/beam patterns and cell/beam activation states, predicting coverage, capacity and NES etc.
  Proposal 4: RAN3 should study and specify signaling enhancement to support AI/ML based Coverage and Capacity Adaption (including CCO and cell/beam (de)activation) for both split and non-split gNB architecture
New Use Case

## Slide 9: Potential SI/WI objectives for Rel-19 AI/ML for NG-RAN
R18 leftovers
Study and specify signaling enhancements, if needed, to enhance R18 AI/ML based mobility optimization for both split and non-split gNB architectures for the following [RAN3]:
  UE Trajectory Feedback collection across multi-hop Target nodes
  UE Trajectory Prediction and Feedback across UE RRC state Transition
Study and specify Network-based solution (without UE impacts) to enable Continuous MDT i.e., continuous collection of MDT data from the same UE across RRC state changes for NG-RAN AI/ML use cases. [RAN3]
R19 New use cases
Study and specify signaling enhancements for R18 AI/ML based mobility optimization use case for the following scenarios, for both split and non-split gNB architectures : [RAN3]
  AI/ML based PSCell mobility (e.g. predicting PSCells)
  AI/ML based CHO (e.g., predicting CHO candidate/target cells)
  AI/ML based LTM (e.g., predicting LTM candidate/target cell(s) and beam(s))
Collaborate with RAN2 if assistance information is required for the above new mobility use cases:
  UE to NW assistance information, and
  NW to UE assistance information.
Study and specify signaling enhancement to support AI/ML based Coverage and Capacity Adaption (including CCO and cell/beam (de)activation) for both split and non-split gNB architecture [RAN3]
NOTE: Model training and/or inference in gNB-DU and F1AP enhancements are needed to support R19 new use cases