## Slide 1: Proposals on Ambient IoT in Rel-19

## Slide 2: Background (1)
Generic requirements of ambient IoT devices
  Ultra-low complexity, ultra-low power, and compact form factor
  Device types/categories/set of devices
  Device A: No energy storage, backscattering transmission
  Device B: Has limited energy storage (e.g., capacitor), backscattering transmission
  Device C: Has energy storage, independent signal generation
  Target use cases
  Inventory, sensors, positioning, and command
  Indoor and outdoor
  Competing non-3GPP IoT technologies
  RFID and barcode
  Compared to existing 3GPP IoT technologies
  (NB-IoT/LTE MTC/RedCap)
  Power and complexity orders of magnitude lower
  Device (connection) density orders of magnitude higher
  Coverage much smaller, especially for Devices A and B

## Slide 3: Background (2)
As an outcome of RAN Rel-19 workshop in June, a summary document RWS-230488 was endorsed
  The summary was intended to be used as a starting point for follow-on discussions on Rel-19 topics
In RAN#101, RP-231540 (RAN Chair’s Guidance for RAN Release 19) was endorsed
Meanwhile, in RAN#101, Rel-18 Study on Ambient IoT in RAN was completed with a few recommendations for the initial WG-level study of Ambient IoT (TR 38.848 V1.0.0)
  In this contribution, we share our views on the support, focus areas and high-level objectives for ambient IoT in Rel-19

## Slide 4: Support for Ambient IoT in Rel-19
Supporting ambient IoT in 3GPP is beneficial
  To accelerate automation and digitization of various industries
  To expand the 3GPP echo system and create a new market opportunity
RAN concluded that, in preliminary feasibility analysis at TSG-RAN level, Ambient IoT is feasible and beneficial, and recommended a further WG-level study prior to normative work (TR 38.848 V1.0.0)
We support to introduce a follow-on RAN WG-level SI for ambient IoT in Rel-19
  To gain a deeper insight into feasibility and potential specification effort needed to support the ambient IoT in 3GPP
  To continue feasibility study in WG level on power, complexity, coverage, and so on (mainly by RAN1)
  Timely completion of Rel-19 SI/WI within the 18-month time frame is important
  * We are open to discuss whether to proceed with a normative work on ambient IoT in December 2024, but, for now, we think it is more realistic to pursue the study phase only in Rel-19
Proposal: Introduce RAN WG-level SI for the feasibility study of ambient IoT in Rel-19
  The study to be led by RAN1

## Slide 5: Focus Area – Topology & Device Types
Connectivity topologies (Rel-18 RAN study)
WG-level study to focus on topology 1 in Rel-19
  Feasibility study on topology 1 can be the basis for studying other topologies. Therefore, studying topology 1 should be considered to be most important as well as urgent in Rel-19
  To extend the deployment scenarios (and hence use cases), study on topologies 2 and 3 can start in a later phase in Rel-19 or in a later release
WG-level study to consider all Devices A, B and C in Rel-19
  According to TR 38.848, with topology 1 which is the most basic and important topology, deployment scenario 1 (Device indoors, basestation indoors) is applicable for all Devices A, B and C
Proposal: SI focuses on (or prioritize) connectivity topology 1 (BS  Ambient IoT device):
  Further consideration : whether to additionally study connectivity topologies 2 and 3 in Rel-19
  Proposal: SI considers all ambient IoT devices (Device A, B and C)
Topology 1:
BS  Ambient IoT device
Topology 2:
BS ↔ intermediate node ↔ Ambient IoT device
Topology 3:
BS ↔ assisting node ↔ Ambient IoT device ↔ BS
Topology 4:
UE ↔ Ambient IoT device
Topology 3 with DL assistance
Topology 3 with UL assistance

## Slide 6: Focus Area – Spectrum
Spectrum in deployment scenarios
  Focus on the licensed spectrum in FR1 (as recommended in Rel-18 RAN study)
    After feasibility study on the licensed spectrum, study on the unlicensed spectrum can start in a later release
    For FR2, further discussions on the justification in terms of applications and use cases, and the feasibility in terms of power, complexity, coverage, etc., are needed before starting the study/work in RAN WG
  Focus on the spectrum in-band to NR in Rel-19
    We are open for further discussion on whether to further consider the spectrum in guard-band NR/LTE and in standalone band(s) in Rel-19
  Selection or prioritization between FDD and FDD/TDD
  Study both FDD and TDD in licensed spectrum in FR1
  For FDD, whether there is any (regional) spectrum regulation issues, especially for the devices based on backscattering communications, needs to be carefully checked
    Note: Currently, non-3GPP competing technology (e.g., RFID) is mainly operating in ISM bands
  For TDD, feasibility study on whether Ambient IoT devices can support TDD can start in Rel-19
Proposal: SI focuses on (or prioritize) the licensed spectrum in FR1:
  Study both FDD and TDD in licensed spectrum in FR1
  Proposal: SI focuses on the spectrum in-band to NR in Rel-19
  Further consideration : whether to add the spectrum guard-band to NR/LTE and in standalone band(s) in Rel-19

## Slide 7: High-level Obejctives for Ambient IoT in Rel-19
High-level objectives to be included in the WG-level study
  Evaluations and WG-level feasibility assessments
    Study and evaluation on device architectures and characteristics
    Including coexistence evaluations
  PHY layer DL/UL signal/channel design & L1 procedures to support ambient IoT
    Study on PHY layer signal/channel design & L1 procedures to support the ambient IoT devices in NR network
  Collision/interference/load handling
    Study on collision/interference/load handling techniques to support larger coverage and denser deployment of devices compared to existing non-3GPP IoT technologies
  Coexistence/harmonization with existing NR signals/channels
    Study on coexistence/harmonization techniques with existing NR signals/channels for NR in-band deployment scenario
Proposal: SI includes study on
  Evaluations and WG-level feasibility assessments
  PHY layer DL/UL signal/channel design & L1 procedures to support ambient IoT
  Collision/interference/load handling
  Coexistence/harmonization techniques with existing NR signals/channels

## Slide 8: Proposals on Ambient IoT in Rel-19
Introduce RAN WG-level SI for the feasibility study of ambient IoT in Rel-19
  The study to be led by RAN1
SI focuses on (or prioritize) on the following:
  Connectivity topology 1 (BS  Ambient IoT device):
    Further consideration : whether to additionally study connectivity topologies 2 and 3 in Rel-19
  Both FDD and TDD in the licensed spectrum in FR1:
  The spectrum in-band to NR in Rel-19
    Further consideration : whether to add the spectrum guard-band to NR/LTE and in standalone band(s) in Rel-19
  SI considers all ambient IoT devices (Device A, B and C)
SI includes study on
  Evaluations and WG-level feasibility assessments
  PHY layer DL/UL signal/channel design & L1 procedures to support ambient IoT
  Collision/interference/load handling
  Coexistence/harmonization techniques with existing NR signals/channels