## Slide 1: Proposal on LP-WUS WI in Rel-19
RP-233156

## Slide 2: Introduction
During Rel-18 Study on low-power Wake-up Signal and Receiver for NR [1][2], followings have been discussed/analyzed,
  By RAN1:
    System impacts for introducing LP-WUS/WUR
      Coverage, network power consumption, system overhead
    Candidate waveforms for LP-WUS
      OOK, FSK, OFDMA-based waveforms
    Potential UE power saving gains compared to the existing Rel-15/16/17 UE power saving mechanisms
      LP-WUS/WUR for Idle/Inactive mode (paging, RRM measurement)
      LP-WUS/WUR for Connected mode (connected mode DRX)
    Low-power WUR architectures
      RF envelope detector, heterodyne/IF envelope detector, homodyne/zero IF with BB envelope detector
      OFDM-based receiver with or without FFT
  By RAN2:
    LP-WUS based wake up procedure
    Entry/exit condition for using LP-WUS
    System information update and PWS during ultra-deep-sleep
    RRM measurement offloading using Low-power receiver
    UE subgrouping using LP-WUS
In this contribution, we propose our preferred work scopes for Rel-19 LP-WUS WI
[1] RP-222644 Revised SID on low-power WUS WUR for NR
[2] TR38.869 Study on low-power wake up signal and receiver for NR
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Waveform for LP-WUS
Motivation
  In RAN#101, waveform down-selection for potential WID objectives was discussed and the following two directions were proposed for further discussion
    Direction#1: Waveform-option-1 + Waveform-option-3
    Direction#2: Waveform-option-3 only
  During SI phase, Waveform-option-1 (i.e., OOK-1 and/or OOK-4) was extensively discussed in terms of power consumption, spectral efficiency, resource overhead, complexity, impact to the existing NR transmitter, etc., and concluded this waveform option as one of potential waveforms for LP-WUS.
  Waveform-option-3 (i.e., Overlayed OFDM sequences over OOK waveform) was also discussed but not much due to the limited input and time, therefore it is difficult to say that this option was intensively investigated, sufficiently to be selected as the potential waveform at this stage. Moreover, although it is observed in TR conclusion that the knowledge of sequence(s) used in LP-WUS waveform may improve performance, but it may be only for the receiver with I/Q branches, not for all types of receivers.
  In this perspective, between two directions, Direction#1 is preferred although we think further investigation seems to be necessary before selecting Waveform-option-3 as the potential waveform for LP-WUS.
Proposal
  Adopt both Waveform-option-1 (i.e., OOK-1 and/or OOK-4) and Waveform-option-3 (i.e., Overlayed OFDM sequences over OOK waveform) as the potential waveforms for LP-WUS

## Slide 4: LP-SS for LP-WUS
Motivation
  During SI phase, RAN1 studied on synchronization signal for LP-WUR. At least for LP-WUR that cannot receive existing PSS/SSS, periodic LP-SS signal is beneficial at least for the following functionalities:
    RRM measurements by LP-WUR
    Coarse time synchronization of LP-WUR
    Coarse frequency synchronization of LP-WUR
  In RAN#101, the majority companies considered that the dedicated LP-SS could be helpful to LP-WUR, which could ensure the main radio is in sleep state and consequently reduce the power consumption as much as possible.
  Moreover, the following consensus was reached regarding the necessity of LP-SS
    For RRC IDLE/INACTIVE, in addition to existing PSS/SSS, LP-SS (i.e., OOK-1 and/or OOK-4 waveform with/without overlayed OFDM sequences with potential further down selection in WI phase) for LP-WUR that cannot receive existing PSS/SSS, is supported for synchronization and/or RRM measurement for serving cell.
Proposal
  Specify LP-SS and necessary procedures for synchronization and RRM measurement

## Slide 5: Procedures for LP-WUS
Motivation
  In SI phase, LP-WUS based operations in both RRC Idle/Inactive and Connected mode have been investigated
  For Idle/Inactive mode
    Significant power saving gains have been observed by adopting LP-WUS for Idle/Inactive mode compared to existing I-DRX operation with or without Rel-17 PEI
    When LP-WUS is monitored by UE while the MR is in ultra-deep sleep state, it has been observed the paging latency increases compared to the legacy I-DRX operation with same I-DRX cycle
    For paging, as RAN2 concluded during SI, paging subgrouping via LP-WUS can significantly increase power saving gain
  For Connected mode
    Significant power saving gains have been observed by adopting LP-WUS for Connected mode compared to Rel-15 long/short C-DRX operation, Rel-16 DCP or Rel-17 PDCCH monitoring adaptation
  Regarding the potential coverage imbalance between LP-WUS and NR
    LP-WUS may have a smaller coverage than PDCCH/PDSCH. When the channel condition of LP-WUS is not good enough, the UE needs to fallback to legacy operation based on the MR. Accordingly, UE needs to start/stop using LP-WUS based on the condition configured by network
    Considering potential coverage imbalance between LP-WUS and NR transmissions, RAN1 agreed to further study on activation/deactivation procedures of LP-WUS monitoring for Idle/Inactive mode
Proposal
  For IDLE/INACTIVE mode, to specify procedures to allow UE MR paging monitoring triggered by LP-WUS
    Including entry/exit condition of LP-WUS, paging subgrouping via LP-WUS and paging latency reduction for LP-WUS
  For CONNECTED mode, to specify procedures to allow UE MR PDCCH monitoring triggered by LP-WUS

## Slide 6: RRM supported by LP-WUR
Motivation
  Even though LP-WUS is adopted for Idle/Inactive mode, UE power saving gain cannot be guaranteed with existing RRM measurement by the main radio
    For example, if serving cell measurement by the main radio is not offloaded to LP-WUR, a UE with LP-WUR should wake up to perform serving cell measurement every I-DRX, thus the power saving benefit of ultra-deep sleep state cannot be fully utilized.
  During SI, significant power saving gains have been observed by adopting serving cell measurement offloading to LP-WUR compared to I-DRX and eDRX.
  For MR serving cell measurement with further time domain relaxation, at least serving cell RRM offloading from MR to LR is beneficial
Proposal
  Specify RRM offloading from MR to LR for RRM measurement relaxation in MR

## Slide 7: Cell reselection for LP-WUS
Motivation
  It is expected that some cells are capable of LP-WUS and others are incapable of LP-WUS.
  For UE power saving in RRC IDLE/INACTIVE mode, it is desirable for UE to camp on a cell capable of LP-WUS rather than a cell incapable of LP-WUS.
  Even if LP-WUS capable cells are deployed on a certain frequency layer, it is not always desirable to configure LP-WUS capable UEs with highest priority for the frequency, because all those UEs will be concentrated on that frequency as camping frequency.
Proposal
  To allow UE to prioritize LP-WUS capable cell for cell reselection

## Slide 8: Proposed WI scope for Rel-19 LP-WUS
LP-WUS and LP-SS physical design
  Specify OOK-based waveform with or without overlayed OFDM sequences
  Specify LP-SS for synchronization and RRM measurement by LP-WUR
The necessary L1/L2 procedures for LP-WUS
  Specify procedures to allow UE MR paging monitoring triggered by LP-WUS in Idle/Inactive mode
    Including entry/exit condition of LP-WUS, paging subgrouping via LP-WUS and paging latency reduction for LP-WUS
  Specify procedures to allow UE MR PDCCH monitoring triggered by LP-WUS in Connected mode
RRM measurement by LP-WUR
  Specify RRM offloading from MR to LR for RRM measurement relaxation in MR
  Mobility enhancement for LP-WUS
  Specify UE’s prioritization of LP-WUS capable cell for cell reselection