## Slide 1: UIC enhancements for FRMCS
3GPP TSG RAN#102 - RP-233211
December 11-15, 2023
Agenda item 9.1.4.5
RP-233211

## Slide 2: Achievements for FRMCS
UIC highly appreciates the work already done in 3GPP RAN for the
Future Railway Mobile Communication System (FRMCS):
Definition of frequency bands n100 (FDD 900MHz) and n101 (TDD 1900MHz)
Definition of PC1 for n100 and n101
Definition of NR support for dedicated spectrum less than 5MHz for FR1

## Slide 3: FRMCS enhancements: CA/DC
Use case: further enhance the capabilities of 5G for FRMCS and hence its attractiveness:
  Improve handover between cells
  Improve the network coverage
  Improve the peak data rate
UIC would like to request in Release 19 support of CA and DC for band n100 with band n101
Description:
  Inter-band CA/DC for 5G NR SA for n100 FDD and n101 TDD with simultaneous Tx/Rx
    Downlink:
      CA/DC for n100 CBW 5MHz with n101 CBW 10MHz;
      CA/DC for n100 CBW <5MHz 20RB, 12 and 15RB with n101 CBW 10MHz;
      CA/DC for n100 CBW 5MHz with n101 CBW 5MHz;
      CA/DC for n100 CBW <5MHz 20RB, 12 and 15RB with n101 CBW 5MHz;
    Uplink:
      For PC1 UEs only;
      The same CA/DC band combinations as mentioned for Downlink.
  Intra-band DC for 5G NR SA for n101 TDD with simultaneous Tx/Rx
    Downlink:
      DC for n101 CBW 5MHz with n101 CBW 5MHz
    Uplink:
      For PC1 UEs only;
      For n101 CBW 5MHz with n101 CBW 5MHz
  For both collocated and no-collocated Basestations

## Slide 4: FRMCS enhancements: MIMO
Use case: Increase throughput in uplink
UIC would like to request in Release 19 support of Uplink MIMO and Tx diversity
Description:
  Support of Uplink 2x2 MIMO
  Support of Uplink Tx diversity for 2Tx
  In bands n100 and n101
  For PC1 and PC3 UEs
  For open loop configuration to support high speeds (350 – 500km/hr)

## Slide 5: FRMCS enhancements: HST
Use case: Downlink and uplink connectivity on high-speed trains (350 – 500km/hr)
UIC would like to request in Release 19 enhanced support of HST
Description:
  In R15 HST in FR1 has been addressed for best effort (MFCN) services
  Railways/ FRMCS need support of specific QoS profiles for critical services:
  Unclear if current HST capabilities sufficiently support the railway required QoS profiles
  RAN is requested to study High Speed Mobility in FR1 for critical services and specify enhancements where necessary.