## Slide 1: Low-power Wake-Up Signal / Wake-Up Receiver
RP-233290
3GPP TSG-RAN Meeting #102
Edinburgh, Scotland, Dec. 11 – 15, 2023
Agenda Item: 9.1.1.6
Source: Ericsson
For: Discussion & Decision
Ericsson
3GPP TSG RAN#102
11-15 Dec, 2023

## Slide 2: LP-WUS waveform
Regarding the waveform for LP-WUS, OOK and OFDM are the main candidates from the Rel-18 SI.
If the decoding time to achieve the same coverage is taken on to account OFDM-based LP-WUS looks very promising and should be included in Rel-19 scope, i.e. as the unified LP-WUS.

## Slide 3: WI scope
According to Rel-18 SI TR, the largest WUR gains are found for Idle/Inactive (>90%). Idle/Inactive should be the priority for Rel-19 WI, and progress should not be jeopardized by Connected workload*, which can instead be considered in Rel-20.
WUR UE power saving gains are largest for shorter duty-cycles compared to baseline. For WUR the UE power is mainly determined by the MR start-up which is dictated by the paging rate. Therefore, WUR duty-cycles longer than 10.24s would have little gain compared to shorter duty-cycles and could be omitted (to avoid eDRX-like open issues*).
* See comment field below.
Chart: WUS duty cycle length
| 1.28s | 2.56s | 5.12s | 10.24s | 20.48s | 40.96s
Power gain, PWUR=0.5 (OOK) | 0.97078 | 0.96079 | 0.95064 | 0.94258 | 0.91809 | 0.84431
Power gain, PWUR=4 (OFDM) | 0.96677 | 0.95774 | 0.94858 | 0.94133 | 0.91717 | 0.8434
Avg.delay, PWUR=0.5 (OOK) | 1.091 | 1.731 | 3.011 | 5.571 | 10.691 | 20.931
Avg.delay, PWUR=4 (OFDM) | 1.103 | 1.743 | 3.023 | 5.583 | 10.703 | 20.943
Notes: [*]
Even if the same LP-WUS design is reused for RRC Connected, there are several additional open issues for Connected which would take a lot of time in Rel-19:
Relation to legacy power saving features, i.e., DCP, C-DRX, SPS, CG, etc. (See RAN2 input to Rel-18 SI TR).
WUS-PDCCH time offset, also WUR PDCCH monitoring window and inactivityTimer may be different from legacy C-DRX parameters (i.e., different from drx-onDurationTimer).
Continuous WUR operation
Difference in the WUS payload, UE subgrouping info, etc.
Connected mode measurements, procedures, RLM, etc. using WUR.
Using MR for measurements also while MR is running.
eDRX complexity:
CN impact
  CN awareness
  DL data buffering
Paging Time Window (PTW)

## Slide 4: WI Objectives
4.1 Objective of Core part WI
The objective is to specify support for the following functionality:
Wake-up receiver procedure
  Specify LP-WUS procedure and the associated UE behaviour in RRC IDLE/INACTIVE state. [RAN1, RAN2]
  LP-WUS detection triggers UE legacy paging monitoring by MR.
  Duty cycled WUR operation with WUS monitoring occasion(s) associated to PO occasion(s).
  For UE subgrouping, PEI mechanism is assumed as baseline.
WUR UE capability signalling and configuration. [RAN2]
Wake-up signal
Specify low power wake-up signal (LP-WUS). [RAN1, RAN2, RAN4]
  LP-WUS with harmonized waveform that accommodates OOK-1/OOK-4 and OFDM waveform. [RAN1]
    Target full cell coverage without reduction of the paging success rate.
    Same SCS used for LP-WUS and other NR transmissions in the same CP-OFDM symbol.
    Existing signal structures/sequences should be reused when possible.
  Specify WUR receiver RF minimum performance requirements, e.g., if new performance metric is needed. [RAN4]
  WUS BW, payload size, and content, e.g., UE subgrouping information [RAN1, RAN2]
Low-power synchronization signal
Specify Low power synchronization signal (LP-SS). [RAN1]
  OOK-1 and/or OOK-4 waveform with/without overlayed OFDM sequences with potential further down-selection in WI phase.
    LP-SS used at least to support synchronization for envelope detection-based LP-WUR.
      Note: For OFDM-based LP-WUR, existing PSS/SSS can be used for synchronization instead of LP-SS.
    System impact due to LP-SS (i.e., overhead and NW energy efficiency) should be minimized.
RRM measurements
Specify serving cell RRM measurement support in IDLE/INACTIVE for LP-WUR. [RAN2, RAN4, RAN1]
  Study and if found beneficial, specify RRM measurements by envelope detection-based LP-WUR using LP-SS in RRC IDLE/INACTIVE. [RAN1, RAN2, RAN4]
    Evaluate the feasibility of LP-SS based RRM measurements considering the LP-SS periodicity. [RAN4, RAN2]
  Specify offloading of RRM measurements from MR to LP-WUR. [RAN2, RAN4]
    RRM measurements using existing PSS/SSS for OFDM based LP-WUR.
    RRM measurements using LP-SS for envelope detection-based LP-WUR (if found beneficial as of above).
  Study and if found feasible, specify relaxation of MR RRM measurement periodicity for LP-WUR. [RAN2, RAN4]
  Specify RAN4 core requirements for the above.
  Notes:
LP-WUS transmission should not require new gNB hardware nor trigger new emissions/compliance requirements.
LP-WUR supports band and carrier tuning and flexible frequency location within a carrier.
Dynamic reuse of unused LP-WUS radio resources for legacy NR transmissions should be supported.
We therefore propose the following Rel-19 objectives: