## Slide 1: Views on R19 SON/MDT scope
RP-233292
Agenda Item: 9.1.3.2
Source: Xiaomi
Document for: Discussion
3GPP TSG RAN#102
Edinburgh, Scotland, December 11-15, 2023

## Slide 2: Introduction
  The baseline objectives of R19 SON/MDT from RAN Chair are as follows in RP-232745.
  We support the objectives above and have some considerations on the details of the yellow highlighted part.
  MRO enhancement for R18 mobility mechanisms, Lower layer triggered mobility (LTM), CHO with candidate SCGs, subsequent CPAC [RAN3, RAN2]:
    Specification of the inter-node information exchange, including possible enhancements to interfaces[RAN3];
    Identify and specify necessary UE reporting to enhance the mobility parameter tuning [RAN2]
  Only SON/MDT enhancements for intra NTN mobility, Network slicing and NW energy saving are for further consideration.
    etails of these aspects (e.g., spec changes, assessment of workload).
    No other new features are to be added
  For NW energy saving, Note: avoid duplication with AI for NG-RAN.
  R18 leftovers, FFS details, which can be decided based on further progress in RAN2/3 [RAN3, RAN2]

## Slide 3: SON/MDT enhancements for NTN
Motivation:
  The NTN feature was introduced in R17 with basic functionalities, e.g. TA pre-compensation, and further enhanced in R18 for coverage enhancement and mobility enhancement. R19 SON/MDT should be able to support the data collection for NTN.
Potential enhancements:
  Support the data collection for SON features for NTN, including RACH optimization and intra-NTN & TN-NTN mobility enhancement optimization. [RAN3, RAN2]
    Specification of the UE reporting necessary to enhance the network configuration. [RAN2]
    Specification of the inter-node information exchange, including possible enhancements to S1/NG, X2/Xn, and F1/E1 interfaces. [RAN3]
  Support the data collection for MDT features for NTN. [RAN2, RAN3]
    Enhancement of logged and immediate MDT. [RAN2, RAN3]
    Enhancement of reporting e.g. RLF and accessibility measurements, Successful Handover reporting. [RAN2, RAN3]

## Slide 4: SON/MDT enhancements for Slicing
Motivation:
  In R18, slice information (i.e. NSAG) has already been included in RA-InformationCommon and is also included for RLF report and CEF.
  To optimize slice access and ensure service continuity, it is beneficial for operators to know the slice coverage situation, such as the areas where the slice is unavailable or where interruptions may occur.
Potential enhancements:
  Support the logged MDT enhancements for network slicing. [RAN2, RAN3]

## Slide 5: Potential objective of Rel-19 SON/MDT
MRO enhancement for R18 mobility mechanisms, Lower layer triggered mobility (LTM), CHO with candidate SCGs, subsequent CPAC.
  Specification of the inter-node information exchange, including possible enhancements to interfaces[RAN3];
  Identify and specify necessary UE reporting to enhance the mobility parameter tuning [RAN2]
Specify the SON/MDT enhancements for NPN
  Support the data collection for SON features for NTN, including RACH optimization and intra-NTN & TN-NTN mobility enhancement optimization. [RAN3, RAN2]
    Specification of the UE reporting necessary to enhance the network configuration. [RAN2]
    Specification of the inter-node information exchange, including possible enhancements to S1/NG, X2/Xn, and F1/E1 interfaces. [RAN3]
  Support the data collection for MDT features for NTN. [RAN2, RAN3]
    Enhancement of logged and immediate MDT. [RAN2, RAN3]
    Enhancement of reporting e.g. RLF and accessibility measurements, Successful Handover reporting. [RAN2, RAN3]
Specify the MDT enhancements for network slicing.
  Support the logged MDT enhancements for network slicing. [RAN2. RAN3].

## Slide 6: Thanks
Xiaomi