## Slide 1
0
2023-12
Views on Rel-19 ATG
CMCC
3GPP TSG RAN Meeting #102 RP-233433 Edinburgh, GB, December 11-15, 2023

## Slide 2
As promising solution for aviation internet, ATG network attracts operators and aircraft industry’s interest to provide services for all passengers during the whole journey. In May 2023, Chinese Ministry of Industry and Information Technology release 4.9 GHz trial spectrum to CMCC for ATG technical testing.
In R18, RAN4 start the standardization that only focus on FR1 single carrier scenario. The details are summarized as below:
Define RF requirements for ATG BS and UE
Evaluate co-existence issue for both ATG synchronized and non-synchronized operation with TN scenarios.
  for the synchronized scenario, ACLR and ACS are derived
  for the non-synchronized scenario, isolation distance is derived
Define enhanced RRM requirements, at least including NR-NR cell reselection requirements, timing requirements, measurement requirements in RRC_CONNECTED to support ATG scenario.
Define new PDSCH/PUSCH requirements for ATG propagation condition (AWGN with doppler) are introduced
Background

## Slide 3
During the standardization discussion, following issues are found which needs further enhancement in R19.
Mitigate severe ATG gNB-to-TN gNB interference
Enhance throughput to meet ATG capacity demand
Motivation for Rel-19 enhancement

## Slide 4
Motivation to mitigate severe ATG gNB-to-TN gNB interference
To avoid severe ATG BS to TN BS interference, tens of kilometers or even hundreds of kilometers isolation distance is required which will introduce huge burden for ATG and TN cooperation deployment, especially for FR1 because FR1 TN network usually have contiguous coverage and hard to find isolation distance to avoid gNB-to-gNB interference
As discussed in [1], ATG network require more guard period compared with TN network due to larger propagation delay from air ATG UE to ground BS. To enhance spectrum utilization and reduce waste of guard period (GP), normally ATG network is configured with larger TDD periodicity which will lead to non-synchronization operation with TN network. Severe gNB-to-gNB interference occurs.
  According to simulation results[2], tens of kilometers or even hundreds of kilometers isolation distance between ATG BS and nearest TN sector is required to enable ATG and TN network adjacent-channel co-existence when the networks are non-synchronized.
[1] R4-2218642, ATG co-existence simulation assumption, CMCC
[2] TR 38.876, Study on Air-to-ground network for NR

## Slide 5
Motivation to meet large ATG network capacity demand
100MHz is not enough for ATG network especially for very-busy route
According to the analysis in [3], we assume 144 seats per airplane with 80% passengers, of whom 50% use ATG services.
  when assuming ATG network always use 64 QAM modulation scheme, for hexagon area,
    180km cell radius require 30M CBW for non-busy route;
    90km cell radius require 60M CBW for busy-route;
    90km cell radius require 100M CBW for very-busy routes
  however, when assuming ATG nework use 16 QAM or QPSK due to large propagation loss, larger than 100MHz CBW is required especially for very busy-route.
 | Radius of one hexagon area/km |  |  |  | 
 | 60km | 90km | 120km | 150km | 180km
Non-busy routes | 20.2 | 45.4 | 80.8 | 126.2 | 181.7
Busy routes | 93.2 | 209.8 | 373.0 | 582.8 | 839.2
Very busy routes | 149.4 | 336.2 | 597.7 | 933.8 | 1344.7
Capacity demand for each hexagon with different radius/Mbps [3]
[3] R4-2215482, ATG co-existence simulation assumption, CMCC

## Slide 6
Objective-FR2-1
The objective of NR ATG enhancement are as following:
FR2-1 to enhance capacity and reduce ATG gNB-to-TN gNB CLI interference
  Define ATG BS and ATG UE requirements
  Example operation bands include n258, ...etc
  ATG and TN co-existence issue analysis, including synchronized and non-synchronized scenario
  Define ATG UE EMC requirements
  Define RRM Core requirements
  Define Performance requirements

## Slide 7
Objective- FR2-1 operation band
Compared with FR1, FR2 is more feasible to reduce ATG BS-to-TN BS interference
  FR2 ATG BS to TN BS interference would be reduced to some extent due to larger propagation loss
  Usually FR2 is not contiguous coverage, making isolation distance solution more feasible
Tens of km cell coverage is achievable for FR2, and at least QPSK, 16QAM could be supported based on simulation results
  At 100km cell edge, SNR is -4.3 dB for 16*4*2 antenna configuration
  At 80km cell edge, SNR is -2.4dB for 16*4*2 antenna configuration
  At 60km cell edge, SNR is 0.19dB for 16*4*2 antenna configuration
Chart: UL SNR CDF(dB)
Chart: DL SNR CDF(dB)

## Slide 8
Objective – CA and leftover issues
CA to enhance capacity
  Define ATG BS and ATG UE requirements
  Define RRM Core requirements:
  Define Performance requirements
  Including
    FR1 intra-band CA
    FR2 intra-band CA
    FR1+FR1 inter-band CA
    FR1+FR2 inter-band CA
R18 leftover issues
  DL 1024 QAM: In Rel-18, 1024QAM is supported by BS declaration, but there are no UE RF and UE demodulation requirements specified so far.
  FR1 MIMO: In R18, two kinds of ATG UE types have been defined, one with omni-directional antenna and the other with antenna array. For the UE with antenna array, if dual-polarization antenna is used, UL MIMO can be supported. However, corresponding requirements are not specified in Rel-18.
  FR1 ATG EMC requirement: ATG UE is the UE mounted on an aircraft and the deployment enviroment is much different from TN UE. it seems it’s hard to reuse TN UE spec and now there is no EMC requirements specified in Rel-18.

## Slide 9
Annex- Partial FR2 UE simulation assumption
Parameters | ATG
Carrierfrequency | 30GHz
Channel bandwidth | 200MHz
UL power control | YES
UE Peak EIRP in dBm | 40 dBm
UE min TX power in dBm | -40dBm
BS Noise figure in dB | 11
UE Noise figure in dB | 9
Handover margin in dB | 3dB
BS antenna height | 25 m
UE mechanical downtilt in degrees | 0（Horizontal orientation）
Antenna element vertical radiation pattern (dB) | θ3dB=90°，SLAV=25dB
Antenna element horizontal radiation pattern (dB) | φ3dB=90°，Am=25dB
Maximum directional gain of an antenna elementGE,max | 5dBi
UE antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 16, 4, 2)
(dv, dh) | (0.5λ, 0.5λ)

## Slide 10
Annex- Partial FR2 BS simulation assumption
Parameters | ATG
BS TRP TX power | 43dBm/200MHz
BS mechanical uptilt in degrees | 14
BS antenna height | 30 m
Antenna element vertical radiation pattern (dB) | θ3dB=65°，SLAV=30dB
Antenna element horizontal radiation pattern (dB) | φ3dB=65°，Am=30dB
Maximum directional gain of an antenna elementGE,max | 8 dBi
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 16, 2)
(dv, dh) | (0.5λ, 0.5λ)