## Slide 1: Discussion on scope of Rel-19 XR enhancement
Edinburgh, Scotland, December 11-15, 2023
3GPP TSG RAN Meeting #102
RP-233482
Agenda Item: 9.1.2.2
Source: Xiaomi
Document for : Discussion and decision

## Slide 2: Discussing on scope of Rel-19 XR enhancement(1)
  New use cases/scenarios (e.g., multi-modality interactions, XR, Metaverse, etc) addressing coordinated parallel transmission impose new requirements for 5G system.
RAN#101 summary (RP-232619)
  Most companies expect:
      A study or study phase is needed, and the following is included:
      Study of traffic case(s), with SA-groups, to establish better understanding for justifications.
      Both Intra-UE and inter-UE scenarios.
      Enhancements (e.g. scheduling, LCP) for Coordinated / Synchronized transmissions for multi-modal flows.
      Enhancements for RAN/AS awareness of inter-dependencies in multi-modal flows.
      Enhancements for multiple DRX for multiple flows (Moderator comment: may be applicable to general mixed traffic case)
  Conclusion: No Consensus, but still majority support to do something. If a study on Multi-modality is to be done in RAN WGs, SA2/SA4 support is required, at least for synchronization / coordination aspects. A number of companies think RAN should not do any work unless SA2 first identifies requirements.
RAN Chair’s summary (RP-232745)
  Study and if justified, specify aspects related to multi-modality(intra-UE)/multi-QoS flow (intra-UE) (with coordination with SA2/SA4), and other aspects requiring coordination w/ SA initiated work as necessary (e.g., SA2/SA4 task list which may potential have RAN impact)
    Check in RAN#105

## Slide 3: Discussing on scope of Rel-19 XR enhancement(1)
  SA1 requirements on multi-modality (TS 22.261)
      Synchronization threshold: For immersive multi-modal VR applications, synchronization between different media components is critical in order to avoid having a negative impact on the user experiences.
  SA2 work in Rel-18:
      Multi-modality related key issues in SA2 Rel-18 TR 23.700-60:
      Key issue #1 Policy control enhancements to support multi-modality flows coordinated transmission for single UE.
      Key issue #2 Support the Application Synchronization and QoS Policy Coordination for Multi-modal Traffic among Multiple UEs.
      SA2 introduces multi-modality support in Rel-18, e.g. in TS 23.501 clause 5.37.2 and 23.503 clause 6.1.3.27.3. RAN related specification change is mainly the introduction of Multi-model service ID (“an identifier that refers to the multi-modal communication service. Multi-modal flows belonging to the same multi-modal service share the same Multi-modal Service ID”, as defined in TS 23.503).

## Slide 4: Discussing on scope of Rel-19 XR enhancement(1)
RAN work to support multi-modality
  RAN awareness of multi-modal service
    Similar to Rel-18 XR awareness, RAN awareness of multi-modal service is needed to facilitate related enhancements.
  To meet synchronization threshold of different flows of a multi-modal service, scheduling enhancements (e.g. LCP enhancements, dynamic grant enhancements, CG enhancements) are needed.
  Discard enhancements:
    PDU set based discard is specified in Rel-18. Discard can be further enhanced to consider inter-PDU set dependency.
  QoS flow / DRB / LCH mapping enhancements
    In the study phase of Rel-18 XR, various mapping options are discussed. Considering that a multi-modal service consists of different flows with different QoS requirements, it is necessary to revisit the mapping options to support multi-modality.
  Multiple active DRX configurations can be considered to support different traffic pattern characteristics of flows within a multi-modal service.
  Management of multi-modal service during admission control and mobility
    Different flows of a multi-modality service should be handled in an integrated way.
      =>Xiaomi’s view:
      To support Multi-modality and Metaverse, RAN is kindly requested to study and specify following aspects related to multi-modality(intra-UE)/multi-QoS flow (intra-UE)

## Slide 5: Discussing on scope of Rel-19 XR enhancement(2)
  In Rel-18, RAN2 introduced DSR reporting while the delay information is additionally reported to the network in order to request the uplink scheduling in time. However, with current LCP procedure, the LCG that triggered DSR can still not be prioritized and lead to long queueing delay and packet discarding;
  For PDCP, the transmitting PDCP entity performing PDCP duplication for PDUs of certain type(s) of PDU Set (e.g., inferred from the PDU Set Importance) while not performing PDCP duplication for PDUs of other types will ensure reliable transmission of the PDU set with high importance and save the radio resource when in presence of congestion;
  UTO-UCI can be extended to multiple CG configurations in Rel-19 XR WI for the following reasons:
      XR traffic can be configured to map to Multiple CG configurations
      Possibility for earlier indication of the unused CG PUSCH occasions
      Possibility to indicate unused TO for the first CG PUSCH occasion of a CG configuration.
      =>Xiaomi’s view:
      To further study the enhancements related to capacity, RAN is kindly requested to consider LCP enhancement for UL delay-aware scheduling and PDCP enhancement;
      For the enhancements related to capacity, RAN is kindly requested to consider UTO-UCI for multiple CG configurations.

## Slide 6: Summary
  Proposal 1: RAN is suggested to consider the following objectives for Rel-19 XR enhancement:
Study and specify following aspects related to multi-modality(intra-UE)/multi-QoS flow (intra-UE) (RAN2, RAN3, RAN1): RAN awareness of multi-modal service; Scheduling enhancements (e.g. LCP enhancements, dynamic grant enhancements, CG enhancements) to guarantee synchronous transmission of different flows of a multi-modal service; Discard enhancements considering inter-PDU set dependency; QoS flow / DRB / LCH mapping enhancements; Multiple active DRX configurations; Management of multi-modality service during admission control and mobility; Further enhancements related to capacity (RAN2, RAN1): LCP enhancement for UL delay-aware scheduling; Selective PDCP duplication; UTO-UCI for multiple CG configurations.

## Slide 7
THANKS!