## Slide 1: Rel19 Priorities on MIMO Enhancements
3GPP TSG RAN Meeting #102 December 11-15, 2023
Agenda Item: 9.1.1.2
RP-233502
Sourced by: CEWiT, IIT-K, Tejas Networks

## Slide 2
  Enhancements to CSI framework to support > 32 (64/128) CSI-RS ports
  Objective 1: Type I codebook enhancements to support > 32 CSI-RS ports
  Objective 2: Type II codebook enhancements to support > 32 CSI-RS ports
  Objective 3: Hybrid beamforming enhancements (CRI based reporting enhancements)
  Note 1: Extension of legacy codebooks and legacy CSI-RS resources
  Note 2: Objective 3 may require further study or clarification.
  Enhancement for asymmetric downlink S-TRP/UL M-TRP scenario assuming intra-band intra-cell non-co-located M-TRP scenarios without changing existing cell definition or defining a new cell
  Objective 1: Extension of Rel-18 2TA mDCI to sDCI assuming legacy PRACH resources
  Objective 2: Separate UL power control for SRS only to downlink S-TRP from SRS to UL M-TRP and introduce path loss measurement to uplink M-TRP
  CJT/DL multi-TRP enhancements
  Objective 1: UE-assisted calibration reporting of delay and frequency/phase offsets for CJT with non-ideal synchronization and backhaul
  Note: Assume legacy CSI-RS design and standalone aperiodic reporting on PUSCH.
  Beam management enhancements to reduce overhead/latency through UE-initiated/event-driven beam management
  Objective 1. Signalling/mechanism to facilitate UE-initiated beam management procedure including UE-initiated beam reporting/[switch]
References: RP-232745
Summary

## Slide 3
Extension of CSI-RS Ports
Enabling the support of CSI-RS transmission with increased number of ports and without increasing the CSI-RS overhead per port (1RE/RB per port according to the current specification)
  Support of CSI-RS transmission up to 128 ports
Providing the required codebook support for the enhanced CSI-RS ports by reusing/refining the existing codebook structures
  Study and specify at least one of
    Type-1 based CSI-RS reporting for the increased number of ports
    e-Type-2 based CSI-RS reporting for the increased number of ports
    CJT Type-2 based CSI-RS reporting for the increased number of ports
  No need for introducing a new codebook structure

## Slide 4
Extension of CSI-RS Ports
Type-1 (Rel15) Extension
Advantages:
Low Overhead
Low Spec impact
Lower computational complexity
Disadvantages
Performance compared to Type-2
eType-2 (Rel16) Extension
Advantages:
Moderate Overhead
Exploits spatial correlation
Better performance compared to Type-1
Disadvantages
Higher computational complexity compared to Type-1
CJT Type-2 (Rel18) Extension
Advantages:
Higher performance compared to Type-1 and eType-2
Disadvantages
High overhead and computational complexity compared to Type-1 and eType-2
Doesn’t exploit spatial correlation

## Slide 5
S-TRP DL/M-TRP UL
Introducing the TRPs that can perform only UL related operations and can be deployed in UL-coverage limited areas
  Enhancements related to TA w.r.t multiple UL TRPs
    TA calculation for the UL-only TRP.
    Impact on STxMP
  Enhancements related to power control w.r.t multiple UL TRPs

## Slide 6
Beam Management Enhancements
Motivation:
The beam management procedures as per the current specification are controlled by the BS.
The current beam management procedures i.e., P1, P2 & P3 are relatively slow. To make these procedures faster using the current specification, the RS and reporting overhead will increase significantly since the entire beam management procedure has to be performed with a smaller periodicity.
Hence, there is a need to reduce beam management latency without increasing the overhead
Enhancements
Introducing a UE initiated beam management to facilitate faster beam management procedures.
  UE initiated beam management should include UE-initiated beam reporting and UE-initiated beam switching

## Slide 7
CJT Enhancements
Motivation:
  The current CJT framework and S-DCI based NCJT framework assumes an ideal backhaul among the coordinating TRPs and also assumes that the coordinating TRPs are perfectly synchronized
  However, in some of the deployment scenarios, ideal backhaul or perfect synchronization among the TRPs cannot be realized
  Non-ideal backhaul or non-ideal synchronization among the coordinating TRPs results in different time and frequency offsets among the TRPs
  Hence, in these cases, UE assistance is required to assist the BS to mitigate the performance loss that could be created by non-ideal backhaul and non-ideal synchronization
Enhancements
  Specify UE assisted CJT/S-DCI based NCJT transmission wherein UE reports to the BS the synchronization errors among the TRPs in the case of non-ideal backhaul and non-ideal synchronization