## Slide 1: NR Duplex Evolution
RP-233503
3GPP TSG RAN Meeting #102 Edinburg, Scotland, December 11-15, 2023
Agenda item: 9.1.1.3
Sourced by: CEWiT, IIT-K, Tejas Networks

## Slide 2
© CEWiT 2022
2
gNB simultaneously transmits and receives in frequency sub-bands within a TDD carrier
Rel. 18 SI on duplexing enhancements for RAN1 got completed in August 2023
  Evaluation on NR Duplex operation
  Sub-band non-overlapping full duplexing (SBFD)
  Potential enhancements on dynamic/flexible TDD
    gNB-gNB cross link interference
    UE-UE cross link interference
Background
Fig. 1 SBFD at gNB

## Slide 3
© CEWiT 2022
3
SBFD at the gNB side
Half duplex operation at the UE side
FR1 and FR2-1
SBFD operation for single NR TDD carrier within a single DL/UL BWP pair with aligned center frequencies
SBFD operation for UEs in RRC_CONNECTED mode
SBFD scheme with one UL subband within a TDD carrier located at one side or the middle part of the carrier in DL or flexible symbols
SBFD operation option 4, where both time and frequency locations of subbands for SBFD operation are known to SBFD aware UEs
Non-SBFD aware UEs, including legacy UEs, and SBFD aware UEs can coexist in cells with SBFD operation at gNB side
Assumptions for the WI

## Slide 4
© CEWiT 2022
4
Specify semi-static signaling support to configure the time and frequency locations of SBFD subbands and/or guard band
Specify transmission, reception and measurement behaviour and procedure for SBFD-aware UEs
  Transmission and reception behaviours on SBFD subbands configured at DL and/or flexible symbol in TDD-UL-DL-ConfigCommon
    UL transmissions within UL subband only and DL receptions within DL subband(s) only
Enhancement on resource allocation in frequency domain in SBFD symbol, including
  resource allocation in frequency domain for PDSCH/CSI-RS across two DL subbands in SBFD symbol
  unaligned boundaries between resource block group(s)/ CSI reporting subband(s) and SBFD subbands in SBFD symbol
Proposed baseline objectives for WI

## Slide 5
© CEWiT 2022
5
  Enhancements on physical channels/signals and procedure across SBFD symbols and non-SBFD symbols in different slots, where each transmission/reception within a slot has either all SBFD or all non-SBFD symbols, including
    resource allocation in frequency domain for transmission or reception in SBFD symbols and non-SBFD symbols with different available frequency resource in different slots
    CSI report of which associated CSI-RS instances occur in both SBFD symbols and non-SBFD symbols in different slots
  Separate configurations for SRS, PUCCH and PUSCH on SBFD symbols and non-SBFD symbols, e.g., resources, frequency hopping parameters, UL power control parameters and/or beam/spatial relation
  Collision handling between DL reception in DL subband(s) and UL transmission in UL subband in a SBFD symbol
Specify UE-UE CLI measurement and reporting enhancements and gNB-gNB CLI handling for SBFD operation
Contd…

## Slide 6
© CEWiT 2022
6
Dynamic SBFD better adapts to the UL/DL resource requirements based on UL/DL traffic loads.
The gNB can flexibly schedule DL in the UL subband when no UL is scheduled within the UL subband
Dynamic SBFD
Fig. 2 Dynamic SBFD

## Slide 7
© CEWiT 2022
7
The following is captured in the TR 38.858 [1]
In addition, whether DL receptions outside semi-statically configured DL subband(s) are allowed or not in a symbol configured as DL in TDD-UL-DL-ConfigCommon for SBFD aware UEs are studied based on the following options:
  - Option 1 (semi-static SBFD): DL receptions outside semi-statically configured DL subband(s) are not allowed
  - Option 2: (dynamic SBFD): DL receptions outside semi-statically configured DL subband(s) are allowed
Contd…

## Slide 8
© CEWiT 2022
8
In addition, whether DL receptions outside semi-statically configured DL subband(s) and UL transmissions outside semi-statically configured UL subband are allowed or not in a symbol configured as flexible in TDD-UL-DL-ConfigCommon for SBFD aware UEs are studied based on the following options:
- Option 1 (semi-static): DL receptions outside semi-statically configured DL subband(s) are not allowed and UL transmissions outside semi-statically configured UL subband are not allowed
- Option 2 (dynamic SBFD): DL receptions outside semi-statically configured DL subband(s) are allowed
- UL transmissions outside the semi-statically configured UL subbands are not allowed
- Option 3 (dynamic SBFD): DL receptions outside semi-statically configured DL subband(s) are allowed
- UL transmissions outside the semi-statically configured UL subbands are allowed
Contd…

## Slide 9
© CEWiT 2022
9
Based on the previous discussion, the following additional objectives are proposed:
Specify transmission, reception and measurement behaviour and procedure for SBFD-aware UEs
  Transmission and reception behaviours on SBFD subbands configured at DL and/or flexible symbol in TDD-UL-DL-ConfigCommon
    UL transmissions within UL subband only and DL receptions within DL subband(s) only
  Dynamic conversion of semi-statically configured SBFD symbols to non-SBFD symbols
    Conversion of SBFD symbol semi-statically configured as DL by TDD-UL-DL-ConfigCommon into full DL symbol
    Conversion of SBFD symbol semi-statically configured as flexible by TDD-UL-DL-ConfigCommon into full DL/UL symbol
Proposed additional objectives for WI

## Slide 10
© CEWiT 2022
10
UE-UE CLI measurement and reporting
  L1/L2 based UE-UE CLI measurement and reporting
    Rel. 16 CLI management supports only L3 measurement and reporting
      Provides an average CLI measurement value
      Higher latency of reporting
    L1/L2 based measurement captures instantaneous CLI measurements
    L1/L2 based reporting reduces latency of reporting
  Spatial domain enhancements for UE-UE CLI measurement and reporting
    Rel. 16 CLI management does not consider CLI on different Tx/Rx beams
    CLI varies across different Tx/Rx beams
    CLI measurement and reporting per Tx/Rx beams needs to be supported
Enhancements related to dynamic/flexible TDD
Fig. 3 UE-UE and gNB-gNB CLI

## Slide 11
© CEWiT 2022
11
  Enhancements related to UE and gNB transmission and reception timing
    In Rel. 16 CLI management, timing adjustment is left to Rx UE implementation
      Leads to timing misalignment
      CLI measurement accuracy gets affected due to timing misalignment
    Support enhancements to manage timing misalignment to improve CLI measurement accuracy
Contd…
Fig. 4 Timing misalignment

## Slide 12
© CEWiT 2022
12
  Relevant information exchange between gNBs for UE-UE CLI management
    Rel. 16 supports limited information exchange for CLI management, [e.g., TDD Configuration]
    Additional information exchange helps in better inter-cell UE-UE CLI management, e.g., SRS configuration information exchange
      Better coordination across gNBs
      Better measurement accuracy
      Reduce CLI
Contd…

## Slide 13
© CEWiT 2022
13
gNB-gNB CLI measurement and reporting
  Left to implementation in Rel. 16
  gNB-gNB CLI affects UL performance
  Following enhancements are supported from Rel. 18 SI [1]
    UL Resource Muting-based scheme for measuring the gNB-gNB CLI interference covariance matrix
      Muting helps in more accurate measurement of interference covariance matrix
      UL muting can be transparent/non-transparent to the UE
      Transparent muting has no spec impact but can lead to wastage of UL resources
      Non-transparent muting decreases UL resource wastage but has spec impact
    Spatial domain enhancements for gNB-gNB CLI measurement and reporting
      CLI varies across different Tx/Rx beams of gNBs
      Measurement and reporting of CLI wrt beams is required
Contd…

## Slide 14
© CEWiT 2022
14
Proposed additional objectives for WI
Based on the previous discussion, the following additional objectives are proposed:
Specify UE-UE CLI measurement and reporting enhancements and gNB-gNB CLI handling for SBFD operation
  L1/L2 based UE-UE CLI measurement and reporting
  Spatial domain enhancements for UE-UE CLI measurement and reporting
  Enhancements related to UE and gNB transmission and reception timing for UE-UE CLI
  Relevant information exchange between gNBs for UE-UE CLI
  UL Resource Muting-based scheme for measuring the gNB-gNB CLI interference covariance matrix
  Spatial domain enhancements for gNB-gNB CLI measurement and reporting

## Slide 15
© CEWiT 2022
15
Specify semi-static signaling support to configure the time and frequency locations of SBFD subbands and/or guard band
Specify transmission, reception and measurement behaviour and procedure for SBFD-aware UEs
  Transmission and reception behaviours on SBFD subbands configured at DL and/or flexible symbol in TDD-UL-DL-ConfigCommon
    UL transmissions within UL subband only and DL receptions within DL subband(s) only
  Enhancement on resource allocation in frequency domain in SBFD symbol, including
    resource allocation in frequency domain for PDSCH/CSI-RS across two DL subbands in SBFD symbol
    unaligned boundaries between resource block group(s)/ CSI reporting subband(s) and SBFD subbands in SBFD symbol
  Dynamic conversion of semi-statically configured SBFD symbols to non-SBFD symbols
    Conversion of SBFD symbol semi-statically configured as DL by TDD-UL-DL-ConfigCommon into full DL symbol
    Conversion of SBFD symbol semi-statically configured as flexible by TDD-UL-DL-ConfigCommon into full DL/UL symbol
Summary of objectives for the WI

## Slide 16
© CEWiT 2022
16
  Enhancements on physical channels/signals and procedure across SBFD symbols and non-SBFD symbols in different slots, where each transmission/reception within a slot has either all SBFD or all non-SBFD symbols, including
    resource allocation in frequency domain for transmission or reception in SBFD symbols and non-SBFD symbols with different available frequency resource in different slots
    CSI report of which associated CSI-RS instances occur in both SBFD symbols and non-SBFD symbols in different slots
  Separate configurations for SRS, PUCCH and PUSCH on SBFD symbols and non-SBFD symbols, e.g., resources, frequency hopping parameters, UL power control parameters and/or beam/spatial relation
  Collision handling between DL reception in DL subband(s) and UL transmission in UL subband in a SBFD symbol
Contd…

## Slide 17
© CEWiT 2022
17
Specify UE-UE CLI measurement and reporting enhancements and gNB-gNB CLI handling for SBFD operation
  L1/L2 based UE-UE CLI measurement and reporting
  Spatial domain enhancements for UE-UE CLI measurement and reporting
  Enhancements related to UE and gNB transmission and reception timing for UE-UE CLI
  Relevant information exchange between gNBs for UE-UE CLI
  UL Resource Muting-based scheme for measuring the gNB-gNB CLI interference covariance matrix
  Spatial domain enhancements for gNB-gNB CLI measurement and reporting
Contd…

## Slide 18
© CEWiT 2022
18
  [1] 3GPP TR 38.858, "Study on Evolution of NR Duplex Operation", V1.0.0 (2023-09)
References

## Slide 19
Thank you