## Slide 1: NTN Enhancement topic prioritization for Rel 19
RP-233509
Sourced by: CEWiT, IIT-K, Tejas Networks
3GPPTSG RAN Meeting #102 Edinburgh, Scotland, Dec 11-15, 2023
Agenda Item: 9.1.2.3

## Slide 2: Background
As the outcome of the Rel 19 workshop, NTN evolution was agreed as one of the possible topics.
In RAN#101 (Bangalore) further discussion took place with the following way forward,
Based on the offline discussion the following potential focus objectives have been identified: Coverage enhancements for Downlink Coverage enhancements for Uplink Regenerative payload Mobility enhancements Enhanced GNSS Operation Uplink capacity/throughput enhancement Robust Notification/Alert MBS via NTN (->) Broadcast only for NGSO REDCAP Further discussion on detailed objectives/tasks shall be performed for the final approval of a WI at RAN#102 in December 2023. Until then – also depending on the progress of the Rel-18 NTN NR work – further re-/ down-/up-scoping is possible as the required work clearly depends on the detailed aspects of each individual objective. Guidance from the RAN chair is appreciated on the practical way forward to detail the 9 listed objectives for a potential WI approval in RAN#102.
Based on the offline discussion and initial agreement, the following objectives have been taken: Store & Forward (requiring regenerative payload) Capacity enhancements for Uplink Mobility enhancements “Coarse Location Reporting” (similar as the NTN NR Rel-17 solution) Further discussion on detailed objectives/tasks shall be performed for the final approval of a WI at RAN#102 in December 2023. Until then – also depending on the progress of the Rel-18 IoT NTN work – further re-/ down-/up-scoping is possible as the required work clearly depends on the detailed aspects of each individual objective. It was commented by one company and the session chair that the [1] TU is potentially already well filled up with the necessary work for the 4 objectives. Guidance from the RAN chair is appreciated on the practical way forward to detail the 4 listed objectives for a potential WI approval in RAN#102.
NR NTN
IoT NTN

## Slide 3: Prioritization of the topics For NTN evolution
NR-NTN Topics
Coverage enhancements for downlinks (RAN 1)
Robust Notification/Alert (RAN 1)
Enhanced GNSS Operation (RAN 2)
Regenerative payload (RAN 3)
IoT-NTN Topics
Mobility enhancements (RAN 2)
Support of S&F Satellite operation (RAN 3)
Multiple topics are presented in the last plenary but considering the possible TUs and guidelines set to make Rel 19 reasonable and smaller compared to Rel 18, down scoping is necessary.
Following are the topics of priority from our end on top of co-sourced contributions RP-232860 and RP-232861

## Slide 4: NR-NTN Enhancement
Detailed Objectives

## Slide 5: 1) Coverage enhancements for downlinks
Satellite deployments are expected to be power optimized from CAPEX and OPEX point of view.
A satellite has constraints on both transmission power and feeder link bandwidth
It may not be possible to activate all the beams with nominal EIRP density [38.821].
Hence DL coverage enhancements are needed to enhance the number of active beams considering the maximization of overall satellite throughput and not affecting UE traffic.
Study followed by work item should be carried out in Rel 19.

## Slide 6: … contd
DL coverage enhancements objectives:
  Study phase:
    Link Level:
      Identify/prioritize which physical channels need to be enhanced and corresponding link margin improvement.
      Identify/prioritize the enhancements needed to the physical channels.
    System level:
      Define reference Satellite payload parameters (e.g. beam illumination plan constraints, total EIRP) and energy consumption model along with necessary evaluation methodology and relevant KPIs.
      Identify potential solutions to support an efficient dynamic and flexible power sharing between beams or different beam patterns/sizes (i.e., wide or narrow) across the satellite footprint considering priority existing 3GPP techniques.
  Normative phase:
    Define link-level enhancements to downlink physical data and control channels as appropriate
    Define system-level enhancements to support an efficient dynamic and flexible power sharing between beams or different beam patterns/sizes (i.e., wide or narrow) across the satellite footprint as appropriate.

## Slide 7
Paging message delivery is important in order to establish the call. In NTN, due to limited link margin and sometimes poor link conditions due to clutter like NLOS blockage page channel can not be reached.
This creates delays and even difficulty in connecting UE to the network.
Therefore, it is important to ensure synchronization of the UE with the network under low SNR or NLOS conditions.
This can be achieved using a dedicated notification/alert message to make cooperative and link the paging delivery with this notification channel.
Objectives for the study are:
  Design a notification channel for indication of paging for the UE considering,
    Identify the notification message requirement - size and content [RAN1/2]
    Identify and specify possible solutions for the support of a robust notification/alert message and its delivery (including paging procedure impact) over a dedicated downlink-only physical channel(s), and specify if needed [RAN1, RAN2, RAN3]
2) Robust Notification/Alert

## Slide 8
Rel-17/18 NR-NTN assumes 100% GNSS service availability. But this is not practical.
There is a need to increase the robustness of uplink time and frequency synchronization in NTN-based access against GNSS temporarily degraded performance.
This feature is needed to increase the service availability of the user equipment in all 3GPP-based satellite networks whatever bands, orbits, or terminal types are planned to be deployed in the next 5 years.
Objectives are:
  Connected mode: Study potential enhancements (e.g. enhanced close loop) for the UE pre-compensation for UL time and frequency synchronization during long connection times in case GNSS availability and accuracy are reduced and specify if needed.
  Initial access: Study potential enhancements for the UE pre-compensation for UL time and frequency synchronization during initial access in case GNSS availability and/or accuracy is reduced and specify if needed.
3) Enhanced GNSS Operation

## Slide 9
In the last plenary multiple options are discussed including Full gNB, DU only, and gNB + part of core.
With discussion it is evident that the Full gNB-only option can be an easy enabler for Rel 19 to go with. Therefore, this release can focus only Full gNB onboard.
Objectives include
  Specify the support of gNB on board in TS 38.300 and define, if needed, any necessary enhancements related to NG protocol to address the feeder link switchover issue.
  Evaluate and specify, if needed, any necessary enhancements related to the intra and inter-gNB mobility, especially for inter-gNB Xn interface over feeder link and with/without ISL.
4) Regenerative Payload

## Slide 10: IoT-NTN Enhancement
Detailed Objectives

## Slide 11
Load balancing between NB-IoT anchor carriers mapped to the same or different satellite beams is necessary for the operators for various reasons.
In addition, since NB-IoT NTN is expected to be used for more use cases than just pure IoT and messaging, there are use cases in which some basic level of mobility between beams might need to be supported.
NB-IoT currently does not support CONNECTED_MODE mobility or any kind of Network-controlled mobility or load-balancing, the NTN operator is severely limited in the ability to manage such scenarios.
Objectives include
  Specify NB-IoT enhancements to support Network-controlled anchor to anchor carrier switching for UE
  Study and define if needed, NB-IoT enhancements (e.g. SIB signaling) to support Network assisted carrier switching for UE.
1) Mobility enhancements

## Slide 12
S&F operation allows for delay-tolerant, non-real-time IoT NTN services to be offered in areas visited by the satellites with no NTN gateway infrastructure immediately available.
This facilitates cost-effective deployment of IoT NTN services and enables an immediate operational service.
Objectives include
  Define the necessary enhancements into RAN to support store and forward (S&F) operation for delay-tolerant services considering:
    Network and UE Capabilities on S&F
    Signalling procedures for S&F operation
    Data transmission under S&F operation (e.g. enforcement of specific S&F QoS requirements such as maximum message size and acknowledgement policy)
  Enhance S1 protocol to address the feeder link switch over
2) Support of S&F Satellite operation

## Slide 13: References
RP-232610 - Moderator's summary for REL-19 RAN2 topic NTN for NR (RAN Vice-Chair, Deutsche Telekom)
RP-232621 - Moderator's summary for REL-19 RAN2 topic NTN for IoT (RAN Vice-Chair, Deutsche Telekom)
RP - 230915 - Draft_MeetingReport_RAN_101_230915_eom
RP- 232725 - Summary for RAN Rel-19 Package: RAN1/2/3-led
RP- 232860 - Candidate topics for a Rel-19 NR-NTN-evolution Work Item
RP- 232861- Candidate topics for a Rel-19 IoT-NTN-evolution WI

## Slide 14: THANK YOU